## Slide 1: KeyStone ARM Cortex A-15 CorePac Overview
KeyStone Training
Multicore Applications
Literature Number: SPRP804

## Slide 2: Agenda
ARM CorePac in KeyStone II
ARM Cortex A-15 Features
Interface to the SOC and Coherency Issues
Benchmarks
Interrupt Controller
Power Management
Debug and Trace

## Slide 3: ARM CorePac in KeyStone II
ARM Cortex A-15 CorePac Overview

## Slide 4: KeyStone II and ARM CorePac (1/2)
Single, Dual, or Quad-ARM Cortex A15 CorePac operating at up to 1.4 GHz.
L1 Memory: 32KB L1 Data cache 32KB L1 Program Cache
Up to 128-bit access
64-byte L1 D cache line (up to 6 outstanding requests)
  L2 Memory: 4 MB L2 Cache is shared between the 1 to 4 ARM A-15 core(s)
    4 tag banks
    4 data banks
64-byte cache line
Notes: 4
Contains an ARM cluster with one, two or 4 ARMs in it.
Running at 1.4GHz.
Two levels of memory just like DSP.
But L2 is shared for cache coherency.
Connected to the MSMC through ACE also provided cache coherency with other peripheral masters.
Power management.(Wait for Interrupt/ Wait for Event).
BootROM.

## Slide 5: KeyStone II and ARM CorePac (2/2)
AMBA 4.0 AXI Coherency Extension (ACE) master port
Module interrupt controller
Cluster-level and core-level power management and low-power standby modes
Configured 64/128-bit AMBA interface and 64/128-bit Accelerator Coherency Support (ACP)
Advance debug features
Notes: 5
Contains an ARM cluster with one, two or 4 ARMs in it.
Running at 1.4GHz.
Two levels of memory just like DSP.
But L2 is shared for cache coherency.
Connected to the MSMC through ACE also provided cache coherency with other peripheral masters.
Power management.(Wait for Interrupt/ Wait for Event).
BootROM.

## Slide 6
ARM CorePac Functional Block Diagram
Notes: CTM – Cross Trigger matrix
STM – System Trace Microcell
ACP – Accelerated coherency port
Next – Asynchronous interface to MSMC
AXI – is really via the MSMC
This is a functional diagram. Physically, all ports go through the MSMC port (except the interrupt?)

## Slide 7: ARM Cortex A-15 Features: ARM Core
ARM Cortex A-15 CorePac Overview

## Slide 8: Cortex A-15 Features: ARM Core (1/2)
Superscalar architecture:
  2 ALU, 2 shifts, branch unit, multiply and divide, load store
  3 concurrent decoded, up to 8 concurrent issues
Full implementation of ARMv7-A architecture instruction set:
  More MAC instructions (normalization and rounding)
  Integer divide
  Automatic thumb mode (16-bit instructions)
Pipeline optimization:
  Deeper pipeline, 13 stages to issue (2 integer, 4 multiply and load, more for NEON and FPU(2-10))
  Out-of-order pipeline (3-12 stages) execution
Notes: 8 issues:
2 for Neon- VFP
2 for load and store
4 for the other (ALU, Shift, multiply)

## Slide 9: Cortex A-15 Features: ARM Core (2/2)
Dynamic branch prediction – Loop prediction and indirect branch predictor
  Branch Target Buffer (BTB)
  Global History Buffer (GHB) has three arrays:
    Taken array
    Not taken array
    Selector array
  Sophisticated hardware algorithm makes the prediction

## Slide 10: Cortex A-15 Features: Fetch & Memory
Increase fetch from 64 to 128 bits
Full support for unaligned fetch address
L1D and L1P:
  32KB size
  Configured as cache
L2 is unified memory that serves ALL cores in the cluster:
  4MB size
  Configured as cache

## Slide 11: ARM Cortex A-15 Features: NEON
ARM Cortex A-15 CorePac Overview

## Slide 12: SIMD Engine NEON
64/128-bit data instructions
Fully integrated into the main pipeline
32x 64-bit registers that can be arranged as 128-bit registers
Data can be interpreted as follows:
  Byte
  Half-word (16-bit)
  Word
  Long

## Slide 13: NEON Registers
NEON registers load and store data into 64-bit registers from memory with on-the-fly interleave, as shown in this diagram.
Source: ARM Compiler Toolchain Assembler Reference; DUI0489C

## Slide 14: ARM Cortex A-15 Features: Vector Floating Point (VFP)
ARM Cortex A-15 CorePac Overview

## Slide 15: Vector Floating Point (VFP)
Fully integrated into the main pipeline
32 DP registers for FP operations
Native (hardware) support for all IEEE-defined floating-point operations and rounding modes; Single- and double-precision
Supports fused MAC operation (e.g., rounding after the addition or after the multiplication)
Supports half-precision (IEEE754-2008); 1-bit sign, 5-bit exponent, 10-bit mantissa

## Slide 16: ARM Cortex A-15 Features: Memory Management Unit (MMU)
ARM Cortex A-15 CorePac Overview

## Slide 17: Memory Management Unit (MMU)
Logical-to-physical memory translation:
  User protected
  Hardware manages the actual memory
Large physical addressing; 40-bit (1TB)
Three-level data structure for virtual 4kB page:
  Two levels for virtual 2MB pages (Linux huge pages)
  Translation Lookaside Buffers (TLB) cache one page of address translations per entry to speed up the translation process:
    L1 instruction access
    L1 data access
    L2 TLB
Notes: The translation between virtual address to physical address is done via two or three steps
32 L1 Instructions
2 by 32 data L1
4 ways 512-entry L2 TLB (for each processor)

## Slide 18: MMU, TLB, and Page
CorePac
MMU
TLB
Memory
…
Page 1
Page 2
Page 3
Page 4
Page 5
Logical
Address
Physical
Address

## Slide 19: Memory Management Unit (MMU)
To support multiple operating systems (adding a Guest operating system):
Three privilege layers:
  User Mode is for “Guest” (application)
  Supervisor controls multiple guests
  Hypervisor controls the complete system
Two-stage translation:
  From logical to intermediate physical address for supervisor for each operating system
  From intermediate to real address for hypervisor for the complete system

## Slide 20: Two-Stage MMU: Guest to Supervisor

## Slide 21: Two-Stage MMU: Stage One
Source: Virtualization is Coming to a Platform Near You

## Slide 22: Two-Stage MMU: Stage Two
Source: Virtualization is Coming to a Platform Near You

## Slide 23: Interface to the SOC and Coherency Issues
ARM Cortex A-15 CorePac Overview

## Slide 24: ARM Cluster Buses AMBA – Advance Microcontroller Bus Architecture
AXI (AMBA Advanced eXtensible Interface) connects the ARM cluster with MSMC module using the AXI-VBUS master.
APB (AMBA Advanced Peripheral Bus) provides access to peripherals and internal memories.
ATB (AMBA Trace Bus) supports the trace features for the ARM cluster.

## Slide 25: ARM AXI-VBUSM Interfaces to the MSMC

## Slide 26: ARM AXI-VBUSM Interfaces to the MSMC
40-bit address access to external memory (8G DDRA, 2G DDRB)
Snooping mechanism maintains coherency between L2 cache and DDRA and MSM memory
Access to all SOC internal memory via TeraNet
ARM cluster PrivID for the TeraNet is 8

## Slide 27: Keystone ll: ARM - IO Coherency External Write to Shared Memory (MSM/DDR)
1
EDMA issues write to shared SRAM.

## Slide 28: Keystone ll: ARM - IO Coherency External Write to Shared Memory (MSM/DDR)
1
2
EDMA issues write to shared SRAM.
Coherence Controller issues WBInv snoops to ARM.

## Slide 29: Keystone ll: ARM - IO Coherency External Write to Shared Memory (MSM/DDR)
1
2
3
ARM evicts the line.
Coherence Controller issues WBInv snoops to ARM.
EDMA issues write to shared SRAM.

## Slide 30: Keystone ll: ARM - IO Coherency External Write to Shared Memory (MSM/DDR)
1
2
3
ARM evicts the line.
Coherence Controller issues WBInv snoops to ARM.
EDMA issues write to shared SRAM.
Coherence controller merges EDMA write with victim & writes to SRAM.
4

## Slide 31: Keystone ll: ARM - IO Coherency External Read to Shared Memory (MSM/DDR)

## Slide 32: Keystone ll: ARM - IO Coherency External Read to Shared Memory (MSM/DDR)
1
EDMA issues read to shared SRAM.

## Slide 33: Keystone ll: ARM - IO Coherency External Read to Shared Memory (MSM/DDR)
1
EDMA issues read to shared SRAM.
Coherence Controller issues read snoops to ARM.
2

## Slide 34: Keystone ll: ARM - IO Coherency External Read to Shared Memory (MSM/DDR)
1
EDMA issues read to shared SRAM.
Coherence Controller issues read snoops to ARM.
2
3
ARM evicts updated data.

## Slide 35: Keystone ll: ARM - IO Coherency External Read to Shared Memory (MSM/DDR)
1
EDMA issues read to shared SRAM.
Coherence Controller issues read snoops to ARM.
2
3
ARM evicts updated data.
4
Coherence controller returns read data to EDMA.

## Slide 36: KeyStone II: IO Cache Coherency
IO coherency for the ARM, SMP for the quad cluster:
  DDR3A from 0x08_0000_0000 to 0x09_FFFF_FFFF (8 G)
  MSMC SRAM
Coherency for ease of use and performance
TeraNet
Write-invalidate
Read-snoop for
DDR3A
Write-invalidate
Read-snoop for MSMC SRAM
ARM
A15
Notes: One still needs to do ensure consistency, with load and store exclusive instructions and data barriers (DMB); SIMPLIFY?
I think that the reason why there are two snoops is because there are two ways to get into the MSMC and from the MSMC to the memories, but the DSP to MSMC -

## Slide 37: ARM CorePac: Cache and Coherency
L1 to L2 cache coherency based on SCU (Snoop Control Unit) algorithm.
Unified L2 Cache coherency for external (to the CorePac) memory and IO; Based on snooping cache coherency protocol.
  Between ARM cache and DDR3A
  Between ARM cache and MSMC SRAM (on-chip scratch memory)
  No IO or DDRB coherency supported by the hardware.
Notes: Include memory portion of KII diagram

## Slide 38: Error Correction and Latency
32KB L1 cache program, 32KB L1 cache data
Large L2 cache (4MB, 16-way set associative)
  1MB, 16-way set associative in some variants
Internal and external memory Error Correction Code (ECC)
  1 bit error correct
  2 bits error detect
L1 hit: 4 cycles latency (4 stage load pipeline, can be hidden)
L1 miss, L2 hit: 20 cycles (4MB) or less (16 cycles 1MB)
L2 miss MSMC SRAM ~50 cycles
L2 miss DDRA memory ~100ns (~140 cycles) if DDR page is open

## Slide 39: Reliability
The KeyStone II ARM A15 CorePac is designed for high-reliability embedded applications; 100k power-on hours at 105C.

## Slide 40: Benchmarks
ARM Cortex A-15 CorePac Overview

## Slide 41: Benchmarks Overview
Dhrystone, DMIPS/MHz, CPU core and L1 only:
  3.5 DMIPS/MHz (highly dependant on compiler)
  19600 DMIPS with KeyStone II Quad-ARM CorePac at 1.4GHz
Floating point:
  Quad single-precision IEEE-754 FMAC per cycle
Notes: Dhrystone score of 3.5DMIPS/MHz requires right version of compiler (ARM RVCT or GCC 4.8.0) that uses NEON SIMD instructions for loads and stores, measures core and L1D only. Benchmark confirms the 3-issue performance.
Floating point is 4 operations per cycle. An operation is add, multiply, multiply and accumulate, etc. In a typical application loads and stores will reduce the sustained operations to 50% or less.
19600 = 1.4 * 3.5 * 4 (cores)

## Slide 42: Memory Bandwidth Benchmarks
Memory bandwidth, external memory only:
  Stream Copy a(i) = b(i), where a and a b are arrays.
  Stream Scale a(i) = q * b(i), where a and b are arrays, and q is a constant.
  Stream Add computes a(i) = b(i) + c(i), where a, b, and c are arrays.
  Stream Triad computes a(i) = b(i) + q * c(i), where a, b, and c are arrays, and q is a constant.
  Array sizes are defined to force missing on cache regardless of size
The STREAM benchmark is the de facto industry standard benchmark for measurements of computer memory bandwidth.
DDR3-1600 theoretical throughput is 12.8 GB/s
~30% to ~50% achieved
Physical placement of arrays is critical; Linux virtual memory with 4kB pages is good.

## Slide 43: Interrupt Controller
ARM Cortex A-15 CorePac Overview

## Slide 44: Purpose of Interrupt Controller
Masking and unmasking of interrupts and events
Prioritize interrupt
Distribution of interrupts to the appropriate processor
Software generation of interrupts
Tracking the status of interrupt
Notes: Wh

## Slide 45: GIC-400 (ARM Generic Interrupt Controller)
Event sources:
  Various IP and peripherals
  Software generated (SGI) by ARM core
  Signal over the AXI interface
Virtual and physical interrupts
Distribution and CPU interfaces
Notes: Distribution and CPU interface

## Slide 46: GIC-400 Interrupt Controller Distributor Side
The ARM Generic Interrupt Controller, the GIC-400, is a high-performance, area-optimized interrupt controller with an Advanced Microcontroller Bus Architecture (AMBA) Advanced eXtensible Interface (AXI) interface.
Interrupt’s sources
  Up to 1020 interrupts
  4 special purpose interrupts
  Each interrupt has a unique ID
  Private and shared interrupts
  32 ID for private interrupts, 16 for PPI and 16 for software generated interrupts
    Note – These are banked ID, meaning, same ID for different interrupts (for different CPU)

## Slide 47: GIC-400 Interrupt Controller CPU Interface
Signal to the CPU is FIQ or IRQ
Grouping
  Group 0 interrupts can be sent to processors using IRQ or FIQ
  Group 1 interrupts can be sent only via IRQ
Interrupt state – pending, active, active pending
CPU acknowledge the interrupt
  Status of interrupt is changing from pending to active or active pending, enable other interrupts

## Slide 48: GIC400 in KeyStone II
The following figure gives an overview of the GIC-400 in KeyStone II devices. It shows the interrupts that are sent to the GIC-400 from various sources and the key phases of interrupt-related signaling in the SoC.

## Slide 49: Power Management
ARM Cortex A-15 CorePac Overview

## Slide 50: Advanced Power Management
Multiple power domains inside the ARM CorePac
Extremely fast state save and restore speeds up hibernation
Fine-grain pipeline shutdown using 32-entry loop buffer disables fetch and some decode pipeline stages.

## Slide 51: Energy Efficiency
Clock gating inside the ARM CorePac:
  Total dynamic power consumption for a fully-loaded 1.4GHz core will range from 1.2W to 0.35W depending on the type of instructions it runs.
  Wait for interrupt and event (WFI, WFE) instructions bring the dynamic power down to <0.1W per core.
Power switches per core and per CorePac including L2:
  Each ARM A15 core can be shut down independently.
  The entire ARM A15 CorePac, including the 4MB/1MB L2 cache, can also be shut down.
  Reduces static power to <5%
Notes: Depending on the transistor temperature, static power (leakage) is ½ to 2/3 of total power. Dynamic power scales with clock speed, static does not.

## Slide 52: Debug and Trace
ARM Cortex A-15 CorePac Overview

## Slide 53: Debug and Trace Options
Lab-based debug; CCSv5 gives full support
  Run-Time debug module
PMU (Performance Monitoring Unit) is a set of counters that can gathers statistics various processor and memory events.
System Trace Macrocell (STM) provides:
  Logic to control the trace
  Path to move the trace data outside
Embedded Cross Trigger (ECT) unit enables an event from one CorePac to trigger a trace at another CorePac

## Slide 54: Lab-Based Debug
CCSv5 works with the ARM cores.
The ARM integrated development environment, RealView Development Suite (RDS), provides lab-based debug facilities (breakpoint, memory view, etc.).
GNU Debugger (GDB)
ARM hardware debug registers facilitate debugging.

## Slide 55: PMU Block Diagram

## Slide 56: System Trace Macrocell (STM)
System Trace Macrocell (STM) enables tracing of system activities from multiple sources; either hardware events or software instrumentation.
Coresight is a set of hardware and software architecture specification documents that enable easy development of on-chip trace and debug.

## Slide 57: STM Challenges
Facilities for collecting trace data:
  Triggering
  Filtering
Options for storing and delivering trace data to host:
  Export using trace port and trace port analyzer (TPA) to capture the trace information
  Write the trace to the Embedded Trace Buffer (ETB) and read it using JTAG or post-mortem memory read

## Slide 58: STM as Part of the SoC

## Slide 59: Tracing Features
Packetized trace, real-time asynchronous trace export
Multicore trace using single capture unit
CoreSight components include:
  PFT (Program Flow Trace)
  ADI (Arm Debug Interface)
  HTM (AHB Trace Macrocell) bus trace
  ITM (Instrumentation Trace Macrocell) (printf)
  DWT (Data Watch Trace)
  CoreSight Trace Funnel (CTF) combines multiple trace streams

## Slide 60: Embedded Cross Trigger (ECT) Module
Cross Trigger Interface (CTI) controls the trigger interface for each CorePac.
  Combines and maps triggering requests
  Enables the debug logic, PTM (Program Trace Macrocell), and PMU (Performance Monitoring Unit) to interact with each other and with other CoreSight components
Cross Trigger Matrix (CTM) controls the distribution of events across CorePacs and from external modules.
  Matrix connections refers to the number of trigger inputs and trigger outputs that are connected between debug components in the MPCore and CTIs.
Notes: ECT - Embedded Cross Triggering

## Slide 61: Cross Triggering: Two CTIs & the CTM

## Slide 62: For More Information
ARM Reference Manuals http://infocenter.arm.com/help/index.jsp
  A15 Technical Reference Manual (TRM) r2p2
  GIC-400 r0p0rel1
STREAM Benchmark http://www.cs.virginia.edu/stream/
For questions regarding topics covered in this training, visit the support forums at the TI E2E Community website.