## Slide 1: PRU Overview
Embedded Processors Training
Multicore Applications
Literature Number: SPRPXXX

## Slide 2: Agenda
PRU architecture Overview
Code Development
Communicating with LINUX (ARM)

## Slide 3: ARM SoC Architecture
L1D, L1P caches (32KB):
  Single cycle access
L2 cache (256KB)
  Min latency of 8 cycles
Access to on-chip SRAM:
  20 cycles
Access to L3 RAM over L3 Interconnect:
  40 cycles
Shared
Memory
Peripherals
Peripherals
GP I/O
L4 Interconnect
ARM Subsystem
Cortex-A8
L1 Instruction Cache
L1 Data Cache
L2 Data Cache
L3 Interconnect
Notes: - ARM Cortex-A8 designed for performance
- High Performance != Real Time

## Slide 4: PRU in Sitara Device
Programmable Real-Time Unit (PRU) Subsystem
Interconnect
INTC
Peripherals
PRU0 I/O
Inst. RAM
Shared RAM
DataRAM
Inst. RAM
DataRAM
PRU1 I/O
Shared
Memory
Peripherals
Peripherals
GP I/O
L4 Interconnect
ARM Subsystem
Cortex-A8
L1 Instruction Cache
L1 Data Cache
L2 Data Cache
PRU0 (200MHz)
PRU1 (200MHz)
L3 Interconnect
L3 Interconnect
Notes: ARM + PRU + memories + peripherals = SoC
PRU works as a co-processor in system-level implementation, or
- PRU works independently

## Slide 6: Programmable Real-Time Unit (PRU) Subsystem
User Guide
http://processors.wiki.ti.com/index.php/PRU-ICSS
Notes: Notes:
  AM335x:
  - 8K Byte instruction RAM (2K instructions) per core
  - 8K Bytes data RAM per core
  - 12K Bytes shared RAM
Although PRU can only run from IRAM, it can be reset and new code can be loaded. This allows you to use the PRU for multiple functions.
Each PRU has a total of 32 output pins and 30 input pins. Pins are multiplexed with other peripherals at the system level so there are pin muxing considerations to be kept in mind.
Main point:
The PRU subsystem has key features and dedicated resources that help solve real-time problems.
Key features:
2 PRU cores – each with dedicated instruction RAM
- RISC processors
IEP (timer) –
eCap
instruction fetch: grab the instruction located at address pc instruction
decode: parse the instruction. what is the opcode, what registers do we need, what is value of the immediate, etc read registers:
grab whatever register values we need from the register file execute: we now have all the data we need to execute the instruction,
so execute the instruction. if it's an add instruction, add the register values, etc.
write register: write a new register value into the register file, if necessary [not necessary for stores]

## Slide 7: Programmable Real-Time Unit (PRU) Subsystem
Programmable Real-Time Unit (PRU) is a low-latency microcontroller subsystem
Two independent PRU execution units
  32-Bit RISC architecture
  200MHz – 5ns per instruction
  Single cycle execution - No pipeline
  Dedicated instruction and data RAM per core
  Shared RAM
Interrupt Controller for system event handling
Fast I/O interface
  Up to 30 inputs and 32 outputs on external pins per PRU unit
32 GPO
30 GPI
32 GPO
30 GPI
Master I/F (to SoC interconnect)
Slave I/F (from SoC interconnect)
AM335x PRU Subsystem Block Diagram
Events to ARM INTC
Events from Peripherals + PRUs
Scratchpad
Interrupt Controller (INTC)
PRU1 Core
(8KB IRAM)
PRU0 Core
(8KB IRAM)
DRAM0
(8K Bytes)
DRAM1
(8K Bytes)
shared
(12K Bytes)
MII1 RX/TX
MII0 RX/TX
32-bit Interconnect bus
IEP (Timer)
eCAP
MPY/MAC
UART
Industrial Ethernet
Industrial Ethernet
MDIO
Notes: Notes:
  AM335x:
  - 8K Byte instruction RAM (2K instructions) per core
  - 8K Bytes data RAM per core
  - 12K Bytes shared RAM
Although PRU can only run from IRAM, it can be reset and new code can be loaded. This allows you to use the PRU for multiple functions.
Each PRU has a total of 32 output pins and 30 input pins. Pins are multiplexed with other peripherals at the system level so there are pin muxing considerations to be kept in mind.
Main point:
The PRU subsystem has key features and dedicated resources that help solve real-time problems.
Key features:
2 PRU cores – each with dedicated instruction RAM
- RISC processors
IEP (timer) –
eCap – PWM (Pulse width Modulation) Enhanced Capture Module – input or output
instruction fetch: grab the instruction located at address pc instruction
decode: parse the instruction. what is the opcode, what registers do we need, what is value of the immediate, etc read registers:
grab whatever register values we need from the register file execute: we now have all the data we need to execute the instruction,
so execute the instruction. if it's an add instruction, add the register values, etc.
write register: write a new register value into the register file, if necessary [not necessary for stores]

## Slide 8: PRU features
2 PRUs, each had private memory
  8K data
  8K program
In between there Is scratch pad memory (3 banks, 30 32-bit registers)
Shared memory:
  Shared ram 12k
Master I/F (to SoC interconnect)
Slave I/F (from SoC interconnect)
AM335x PRU Subsystem Block Diagram
Events to ARM INTC
Events from Peripherals + PRUs
Scratchpad
Interrupt Controller (INTC)
PRU1 Core
(8KB IRAM)
PRU0 Core
(8KB IRAM)
DRAM0
(8K Bytes)
DRAM1
(8K Bytes)
shared
(12K Bytes)
MII1 RX/TX
MII0 RX/TX
32-bit Interconnect bus
IEP (Timer)
eCAP
MPY/MAC
UART
Industrial Ethernet
Industrial Ethernet
MDIO

## Slide 9: Scratch Pad

## Slide 11: Constant Table

## Slide 12: Constant Table

## Slide 13: PRU features
Interrupt Controller
  64 input events
  10 interrupt channels – hardware priorities
  16 software events can be generated by 2 PRU
Two MII ports
One MDIO port
IEP (Industrial Ethernet peripheral)
Enhanced Capture Module (ECAP)
Notes: IEP – Industrial Ethernet Peripheral - refers to the use of standard Ethernet protocols with rugged connectors and extended temperature switches in an industrial environment
The industrial ethernet peripheral (IEP) is intended to do the hardware work required for industrial ethernet
functions. The IEP module features an industrial ethernet timer with eight compare events

## Slide 14: MAC/MPY integration

## Slide 15: Features & Benefits
Feature | Benefit
Each PRU has dedicated instruction and data memory and can operate independently or in coordination with the ARM or the other PRU core | Use each PRU for a different task; use PRUs in tandem for more advanced tasks
Access all SoC resources (peripherals, memory, etc.) | Direct access to buffer data; leverage system peripherals for various implementations
Interrupt controller for monitoring and generating system events | Communication with higher level software running on ARM; detection of peripheral events
Dedicated, fast input and output pins | Input/output interface implementation; detect and react to I/O event within two PRU cycles
Small, deterministic instruction set with multiple bit-manipulation instructions | Easy to use; fast learning curve

## Slide 16: PRU Functional Block Diagram
R0
R29
R30
R1
CONST TABLE
Instruction RAM
32 GPO
30 GPI
…
PRU Execution unit
General Purpose Registers
All instructions are performed on registers and complete in a single cycle
Register file appears as linear block for all register to memory operations
Special Registers (R30 and R31)
R30
  Write: 32 GPO
R31
  Read: 30 GPI + 2 Host Int status
  Write: Generate INTC Event
Instruction RAM
8KB in size; 2K Instructions
Can be updated with PRU reset
Constant Table
Ease SW development by providing freq used constants
Peripheral base addresses
Few entries programmable
Execution Unit
Logical, arithmetic, and flow control instructions
Scalar, no Pipeline, Little Endian
Register-to-register data flow
Addressing modes: Ld Immediate & Ld/St to Mem
INTC
EXECUTION UNIT
R2
R31
Notes: 16
16
This slide gives a functional block diagram of the PRU core. The two PRU cores in the PRU SS each possess these features.
Execution Unit
The PRU core supports logic, arithmetic, and flow control instructions. About 40 instructions in total.
The PRU core does not use a pipeline and only one data item can be processed at a time (scalar), this makes the PRU simple to program. The PRU is a little endian processor.
Each PRU has a register-to-register data flow architecture, meaning all operations (except load immediate) accept only registers as operands. For example, to add a constant to a register, you must first load the constant into a register and add the two registers.
There are two ways to move data around:
    First, you can load a 16-bit immediate into a register. Therefore, to init a 32-bit register, you need to do two 16-bit loads.
    Second, to load or store data from memory, you need to load the address to a register and use a load burst or store burst instruction to move data between registers and memory. Notice data is moved between memory and registers.
Instruction RAM
The PRU core includes a 4KByte instruction RAM allowing for up to 1K instructions.
The instruction RAM is fully accessible by the ARM or the DSP when the PRU is in reset.
General Purpose Registers
All PRU instructions are performed on the 32 general purpose registers of each PRU core.
These registers behave as a linear block when used with memory load/store instructions. This allows you to burst multiple data bytes directly to (or from) memory to multiple registers. For example, you can burst 8 bytes of data from memory to the register set starting at R0. This would load 4 bytes into R0 and 4 bytes into R1. Also, you don’t have to align data on a register boundary, you can specify the data copy start at word 1 of R0 or byte 3 of R2.
One useful feature of the PRU is that it is easy to select bits, bytes, and words within a register through a “dot” operator. This allows for easy manipulation of data. The “dot” operator will be discussed later.
Special Registers (R30 and R31)
  Each PRU core has 30 GPIs and 32 GPOs. Additionally, each PRU can generate up to 32 events to the INTC and it can read the status of two host interrupts from the INTC. As we’ll see later, the host interrupts are the combined outputs of INTC.
  Writing to R30 toggles the GPOs of the PRU.
  Writing to R31 generate events to the interrupt controller.
  Reading from R31 returns the status of the GPIs and the two host interrupts generated by the INTC.
Constants Table
  The PRU will often have to access system resources like memory mapped registers or DSP L2 memory. The constants table contains some of the most commonly-used addresses. The constants table can be used to save instructions and cycles. Some of the entries in the constants table are programmable.
Notes:
Execution Unit Highlights
  Supports logical, arithmetic, and flow control instructions
  Scalar: One data item at a time processing
  No pipelining
  Little endian, just like the ARM and DSP.
  It has a register-to-register data flow architecture, meaning all operations (except load immediate) accept only registers as operands. For example, to add a constant to a register, you must first load the constant into a register and add the two registers.
  Two ways to move data around:
    First, you can load a 16-bit immediate into a register. Therefore, to init a 32-bit register, you need to do two 16-bit loads.
    Second, to load or store data from memory, you need to load the address to a register and use a load burst or store burst instruction to move data between registers and memory. Notice data is moved between memory and registers, this brings us to the register set…
Register Set
  30 32-bit general purpose registers and two special purpose registers, which will be discussed next.
  Registers behave as a linear block for all memory operations. This allows you to burst multiple data bytes directly to (or from) memory to multiple registers. For example, you can burst 8 bytes of data from memory to the register set starting at R0. This would load 4 bytes into R0 and 4 bytes into R1. Also, you don’t have to align data on a register boundary, you can specify the data copy start at word 1 of R0 or byte 3 of R2.
  One useful feature of the PRU is that it is easy to select bits, bytes, and words within a register through a “dot” operator. This allows for easy manipulation of data. The “dot” operator will be discussed later.
Special Regs 30 and 31
  Each PRU core has 30 GPIs and 32 GPOs. Additionally, each PRU can generate up to 32 events to the INTC and it can read the status of two host interrupts from the INTC. As we’ll see later, the host interrupts are the combined outputs of INTC.
  Writing to R30 toggles the GPOs of the PRU.
  Writing to R31 generate events to the interrupt controller.
  Reading from R31 returns the status of the GPIs and the two host interrupts generated by the INTC.
Constants Table
  The PRU will often have to access system resources like memory mapped registers or DSP L2 memory. The constants table contains some of the most commonly-used addresses. As we’ll see next, the constants table can be used to save instructions and cycles. Some of the entries in the constants table are programmable.

## Slide 17: Fast I/O Interface
Reduced latency through direct access to pins
  Read or toggle I/O within a single PRU cycle
  Detect and react to I/O event within two PRU cycles
Independent general purpose inputs (GPIs) and general purpose outputs (GPOs)
  PRU R31 directly reads from up to 30 GPI pins
  PRU R30 directly writes up to 32 PRU GPOs
Configurable I/O modes per PRU core
  GP input modes
    Direct connect
    16-bit parallel capture
    28-bit shift
  GP output modes
    Direct connect
    Shift out
Peripherals
GPIO1
GPIO2
GPIO3
....
PRU Subsystem
Cortex A8
L3F L3S
GPIO 3.19
PRU output 5
L4 PER
Pinmux
Device pin
Notes: GPIOs:
Direct access
Low latency
Measure latency difference – may want to compare against the ARM accessing a GPIO…
The PRU enhanced GPIO are much faster as the PRU does access the pin directly. We physically use the same physical pins but used a different pinmux option. The below picture show the differences between the two setup:
While generic general-purpose input/output (GPIO) pins can be used to implement some functions, GPIO supported by the SoC can be inadequate when a fast response time is required since often these pins cannot be toggled or sampled at a very fast rate. The PRU includes dedicated, fast input/output pins which can be read or toggled within a single cycle.

## Slide 18: GPIO Toggle: Bench measurements
PRU IO Toggle:
ARM GPIO Toggle
~200ns
~5ns = ~40x Faster

## Slide 19: Integrated Peripherals
Provide reduced PRU read/write access latency compared to external peripherals
Local peripherals don’t need to go through external L3 or L4 interconnects
Can be used by PRU or by the ARM as additional hardware peripherals on the device
Integrated peripherals:
  PRU UART
  PRU eCAP
  PRU MDIO
  PRU MII_RT
  PRU IEP
    Real-time Ethernet specific modules
Programmable Real-Time Unit (PRU) Subsystem
Interconnect
INTC
UART
Inst. RAM
Shared RAM
DataRAM
Inst. RAM
DataRAM
PRU0 (200MHz)
PRU1 (200MHz)
eCAP
MII x2
MDIO
IEP (Timer)

## Slide 20: PRU “Interrupts”
The PRU does not support asynchronous interrupts.
  However, specialized h/w and instructions facilitate efficient polling of system events.
  The PRU-ICSS can also generate interrupts for the ARM, other PRU-ICSS, and sync events for EDMA.
From UofT CSC469 lecture notes, “Polling is like picking up your phone every few seconds to see if you have a call. Interrupts are like waiting for the phone to ring.
  Interrupts win if processor has other work to do and event response time is not critical
  Polling can be better if processor has to respond to an event ASAP”
Asynchronous interrupts can introduce jitter in execution time and generally reduce determinism. The PRU is optimized for highly deterministic operation.

## Slide 22: PRU Memory Map (local)
Each PRU sees his RAM at 0x000 0000 and the other one at 0x0000 2000
Local memory – allow fast access to RAM and subsystem resources
(DRAM, INTC, MII, UART). Different for PRU0 and PRU1
Global memory – allow external masters to access memory
(PRU can use global memory but high latency)

## Slide 23: PRU Memory Map (Global)
This is the host view of the PRU memories

## Slide 24: PRU Read Latencies: Local vs Global Memory Map
 | Local MMR Access ( PRU cycles @ 200MHz ) | Global MMR Access ( PRU cycles @ 200MHz )
PRU R31 (GPI) | 1 | N/A
PRU CTRL | 4 | 36
PRU CFG | 3 | 35
PRU INTC | 3 | 35
PRU DRAM | 3 | 35
PRU Shared DRAM | 3 | 35
PRU ECAP | 4 | 36
PRU UART | 14 | 46
PRU IEP | 12 | 44
Note: Latency values listed are “best-case” values.

## Slide 25: PRU Memory Access FAQ
Q: Why does my PRU firmware hang when reading or writing to an address external to the PRU Subsystem?
A: The OCP master port is in standby and needs to be enabled in the PRU-ICSS CFG register space, SYSCFG[STANDBY_INIT].
Notes: /* Clear SYSCFG[STANDBY_INIT] to enable OCP master port */
CT_CFG.SYSCFG_bit.STANDBY_INIT = 0;

## Slide 26: AM335x PRU-ICSS Power
PRU Test Case: Addition and Subtraction loop
Baseline: PRU released from reset and PRU clock is enabled
Test Case | OPP100 (mW) PRU 200MHz@1.1V
Baseline | 13.1
PRU test on PRU0 | 17.3
PRU test on PRU1 | 16.8
PRU test on PRU0 and PRU1 | 20.4

## Slide 27: AM437x PRU-ICSS Power
PRU Test Case: Addition and Subtraction loop
Baseline: PRU released from reset and PRU clock is enabled
Test Case | OPP100 (mW) PRU 200MHz@1.1V | OPP50 (mW) PRU 100MHz@0.95V
Baseline | 28.4 | 12.6
PRU test on ICSS0_PRU0 | 37.3 | 15.8
PRU test on ICSS0_PRU1 | 36.1 | 15.3
PRU test on ICSS1_PRU0 | 40.0 | 16.5
PRU test on ICSS1_PRU1 | 36.6 | 15.0
PRU test on all 4 PRUs | 55.2 | 21.4

## Slide 28: Use Cases Examples
Development Complexity
Not all use cases are feasible on PRU
Development complexity
Technical constraints (i.e. running Linux on PRU)
                Industrial Protocols
                ASRC
            10/100 Switch
                Smart Card
                DSP-like functions
                Filtering
              FSK Modulation
                LCD I/F
                Camera I/F
            RS-485
          UART
          SPI
        Monitor Sensors
      I2C
    Bit banging
  Custom/Complex PWM
Stepper motor control

## Slide 29: Replicape 3D Printer
Replicate 3D Printer uses AM335x on BeagleBone
  Cortex-A8 runs Linux, networking, HMI, model processing
    Host apps written in Python
  PRU controls step and direction of 5 stepper motors
    App written in PRU assembly
A8 calculates data, PRU communicates with motors
  Shared region of DDR reserved for A8/PRU communication
  Data consist of pin/delay timing tuples (8 bytes each)
Sequence:
  GPIO pins are set – one or more of the 32-bit GPIO banks set with a predefined mask
  Delay is applied (# of 200MHz instructions)
  After sequence completes, PRU sends a signal to the host indicating that the segment is finished
  Host updates its memory usage for the PRU
More info @ hipstercircuits.com
Notes: On Replicape one PRU is used for controlling the step and direction pins for all the five stepper motor controllers on the board. The way it has been done is by having a region is set aside in the DDR memory that is shared between the host CPU and the PRU for feeding the stepper timing data. The timing data consist of (pin, delay) tuples, each 8 bytes long, so first the pins are set, and this is really just an update of one or more of the 32bit GPIO banks with a predefined mask, then the delay is applied in number of 200 MHz instructions to wait. Each sequence of several pin, delay tuple is terminated by a zero to indicate end of sequence. This puts a limit on the pin configurations, so there is no overlap between the banks and never pins=0 at the start.
Once the sequence is completed, the PRU sends a signal to the host indicating that the segment is finished and the host must then update its memory usage for the PRU so it never overwrites the beginning of the circular buffer. Once the end of the buffer is reached, a magic number is used to indicate a jump back to the beginning of the buffer. The host software is written in Python and the PRU code is assembly.

## Slide 30: TI solves the complex communications problem by integrating multi-protocol support in the ARM SoCs
Host Interface
MCU or MPU
(Protocol Stack)
Ind Comm
ASIC/FPGA
(MAC layer)
AM1810 (Profibus)
AM335x (Multi-protocols)
AM435x (Multi-protocols)
AM57xx (Roadmap for Multi-protocol, host/slave)
ARM
CPU
(Stack and application)
Shared Memory
PRU-ICSS
PRU0/1
UART/MII
Timer
Typical Solution – Today
MCU/MPU for application
External ASIC/FPGA for communications (especially for slave)
TI’s ARM + PRU solution = 4 benefits
  System BOM savings (>40%) by eliminating the external ASIC
  Supports multiple protocols using the same hardware (PRU is completely programmable)
  Easily adapt to changing standards or create
  Scalable solution for Human Machine Interface, Programmable Logic Control and I/O devices
PRU-ICSS (PRU based Industrial Communications Subsystem)

## Slide 31: Code development C and Assembly

## Slide 32
PRU Instruction Set
Screen shot of
http://processors.wiki.ti.com/index.php/PRU_Assembly_Instructions

## Slide 33
PRU Instruction Set
Screen shot of
http://processors.wiki.ti.com/index.php/PRU_Assembly_Instructions

## Slide 34
PRU Instruction Set
Screen shot of
http://processors.wiki.ti.com/index.php/PRU_Assembly_Instructions

## Slide 36
PRU Instruction Set
Add Example

## Slide 37
PRU Instruction Set
Bit-Byte Support
The PRU support native bit and byte arithmetic make it very suitable for MAC layer processing

## Slide 38: Building PRU executables
PSAM
Code generation Tools
  Assembler
  C compiler

## Slide 39: What is PASM
PASM is a command line driven assembler
It is designed to build single executable images using a flexible source code syntax and a variety of output options.
PASM is available for Windows and Linux
PASM User Guide and Information
http://processors.wiki.ti.com/index.php/PASM_Tool

## Slide 40: TI Code Generation Tools (CGT)
Standard tools for many TI’s processors
Can be used from CCS or command line
C compiler, assembler, linker
All development can be done from IDE (CCS)

## Slide 41: TI Code Generation Tools (CGT)

## Slide 42: TI Code Generation Tools (CGT)

## Slide 43: C Compiler
Developed and maintained by TI CGT team
  Remains very similar to other TI compilers
Full support of C/C++
  Adds PRU-specific functionality
  Can take advantage of PRU architectural features automatically
  Contains several intrinsic
    List can be found in Compiler documentation
Full instruction-set Assembler for hand-tuned routines

## Slide 44: Coding Considerations
There are some “tricks” we have to use to get the compiler to perform some operations
  Variables have to be “mapped” to Constant Table entries
  The compiler will automatically use the MAC unit if the --hardware_mac switch is passed to it
  Optimization can be tricky; be sure to mark variables that can change via outside forces (e.g., host, other PRU core) as volatile

## Slide 45: Coding Considerations
There are also some limitations
  The C environment does not know that the final eight CT registers have a variable offset, and thus that feature cannot be easily utilized
  The compiler does not currently use the scratchpad for register state saving
    This support is tentatively planned for a future CGT release

## Slide 46: CGT C programming and CGT Assembly
Advantages of coding in Assembly over C
  Code can be tweaked to save every last cycle and byte of RAM
  No need to rely on the compiler to make code efficient
  Easily make use of scratchpad
Advantages of coding in C over Assembly
  More code reusability
  Can directly leverage kernel headers for interaction with kernel drivers
  Optimizer is extremely intelligent at optimizing routines
    “Accelerating” math via MAC unit, implementing LOOP instruction, etc.
  Not mutually exclusive - inline Assembly can be easily added to a C project

## Slide 47: TI PRU CGT Assembler vs PASM
Advantages of using TI PRU CGT Assembler over PASM
  The biggest advantage is that the TI PRU linker produces ELF files that enable source-level debugging within CCS. No more debugging in disassembly window!!
  The TI PRU assembler uses the same shell as other TI compilers. Customers only need to learn one set of conventions, directives, etc.
  TI PRU assembler will be maintained in the future, while PASM will not be updated anymore.
  The TI PRU assembler uses the powerful TI linker which allows more flexibility then PASM and facilitates linking PRU programs with host CPU image for runtime loading and symbol sharing.
Disadvantages of using TI PRU Assembler over PASM
  Have to learn new directives if already used to PASM
  TI PRU assembler requires more command line options and a linker command file.
  Some porting effort required for reusing legacy PASM projects.
  There are some differences in the instructions and directives supported TI PRU Assembler versus PASM. Theses are listed in the TI PRU Compiler package release notes which is located at the root of the install folder.

## Slide 48: PRU Register Headers
Created to make accessing a register easier
  Register names match those in documentation
Code Completion feature in CCS automatically lists all members
Allow user to program at the register-level or at a bit-field level
  Note that bit-field accesses could potentially cause some issues with other C compilers (e.g., gcc), but register-level shouldn’t
  PRU cregister mechanism used to leverage constants table when possible.
Currently provides definition for the following:
PRU INTC
PRU Config
PRU IEP
PRU Control
PRU ECAP
PRU UART

## Slide 49: PRU Register Headers Layout
Excerpt from config.h
  Access register directly pruCfg.SYSCFG
  Or access specific bitfields CT_CFG.SYSCFG_bit.STANDBY_INIT
Example of how to use in C file
  #include the specific header
  Map the constant table entry to register structures
  Access registers or fields

## Slide 50: Communication with the Host

## Slide 52: PRU SW Stack
RemoteProc-PRU
RemoteProc
rpmsg-PRU
rpmsg
virtio
PRU Data Memory
vring
Application
PRU FW
PRU rpmsg lib
DTB File passed from U-Boot
User Space
Kernel
PRU
Application uses /dev/rpmsg-pru interface to send messages
Client drivers specifically for PRU core
Core Linux drivers

## Slide 53: Remoteproc
The remoteproc framework allows different platforms/architectures to control (power on, load firmware, power off) remote processors while abstracting any hardware differences
Documentation in the SDK release
/board-support/linux-3.12.10-ti2013.12.01/Documentation/remoteproc.txt
Remoteproc APIs
int rproc_boot(struct rproc *rproc)
void rproc_shutdown(struct rproc *rproc)
struct rproc *rproc_alloc()

## Slide 54: rpmsg
rpmsg is a Linux framework designed to allow for message passing between the kernel and a remote processor
Documentation in the SDK release
/board-support/linux-3.12.10-ti2013.12.01/Documentation/rpmsg.txt
rpmsg APIs
int rpmsg_send(struct rpmsg_channel *rpdev, void *data, int len);
int register_rpmsg_driver(struct rpmsg_driver *rpdrv);

## Slide 55: Virtio & Vring
Virtio is a virtualized I/O framework
  We will use it to communicate with virtio device (vdev)
    There are several ‘standard’ vdevs, but only virtio_ring is used by TI software
  The host and PRU will communicate with one another via the virtio_rings (vrings)
Virtual device definition example in the SDK release
/board-support/linux-3.12.10-ti2013.12.01/Documentation/devicetree/bindings/virtio/mmio.txt

## Slide 56: Virtio & Vring
Virtio_ring (vring) is the transport implementation for virtio
A vring consists of three primary parts:
  A descriptor array
  The available ring
  The used ring
  In our case the vring contains our list of buffers used to pass data between the host and PRU cores via rpmsg

## Slide 57: Understanding the Resource Table
What is a Resource Table?
  A Linux construct used to inform the remoteproc driver about the remote processor’s available resources
  Typically refers to memory, local peripheral registers, etc.
  Firmware-dependent
Documentation in the SDK release
/board-support/linux-3.12.10-ti2013.12.01/Documentation/remoteproc.txt
/**
struct resource_table - firmware resource table header
@ver: version number
@num: number of resource entries
@reserved: reserved (must be zero)
@offset: array of offsets pointing at the various resource entries
The header of the resource table, as expressed by this structure,
contains a version number (should we need to change this format in the * future), the number of available resource entries, and their offsets * in the table.
*/

## Slide 58: Thank you!
For more information about the PRU, visit:
Complete on-line training (boot Camp) –
www.ti.com/sitarabootcamp
PRU-ICSS Wiki – http://processors.wiki.ti.com/index.php/PRU-ICSS
PRU Evaluation Hardware – http://www.ti.com/tool/PRUCAPE
Support –
http://e2e.ti.com