## Slide 1: KeyStone Peripherals Usage DSP View
KeyStone Training
Multicore Applications
Literature Number: SPRPXXX

## Slide 2: Agenda
KeyStone II Peripherals and Coprocessors
Resource Management
DSP CorePac CSL Layer
DSP CorePac LLD Layer
  LLD Functions
  LLD Support in MCSDK 3.x
  LLD Usage
  NWAL2

## Slide 3: KeyStone II Peripherals and Coprocessors
KeyStone Peripherals Usage

## Slide 4: KeyStone I Device Architecture
Application-Specific
Coprocessors
Memory Subsystem
Multicore Navigator
Network Coprocessor
C66x™
CorePac
HyperLink
TeraNet
External Interfaces
Miscellaneous
Notes: 4
NEW

## Slide 5: Peripherals and Coprocessors (1/3)
High Bit Rate Interfaces
  HyperLink
  SRIO
  PCIe
  10/100/1G SGMII
  10G SGMII
  USB3
  AIF2
  TSIP

## Slide 6: Peripherals and Coprocessors (2/3)
Low Bit-Rate Interfaces
  UART
  I2C
  SPI
  GPIO
IP that support multicore co-operation
  Multicore Navigator
  EDMA
  Semaphore
  Timers

## Slide 7: Peripherals and Coprocessors (3/3)
Coprocessors
  VCP
  TCPE
  TCPD
  FFTC
  BCP

## Slide 8: Challenges
How to share resources between different cores?
  Protect resources from conflict usage
  ARM runs Linux, C66x runs BIOS
  Solution: Resource Management
How to use these peripherals and IP?
  Configuration
  Run-time usage
  Solution: Chip Support Library (CSL) and Low Level Drivers (LLD) on DSP, LINUX drivers on the ARM

## Slide 9: Resource Management
KeyStone Peripherals Usage

## Slide 10: Resource Management: Background
Initial KeyStone I devices had only DSP cores. The system architect was responsible for resource allocation.
  Issues with pre-build libraries and plug-in RTSC modules
  Special KeyStone I device that includes an ARM core in addition to DSP
KeyStone I solution – hybrid solution – share resources between DSP and ARM.
  ARM resources are defined in the device tree structure
  DSP resources manage by the RM LLD
Compatibility with pre-RM code

## Slide 11: Keystone I Resource Manager (RM) LLD (1/2)
Prevents DSP applications from stepping on resources taken by ARM Linux
Initialization and usage permissions for select LLD resources defined in user-defined resource table
  QMSS, CPPI, and PA LLDs
Operates under the hood of LLDs
  Resource init and usage requests made between LLDs and RM directly:
    LLD operates normally if resource request is “allowed”
    LLD returns error if resource request is “denied”
      Application must take steps to handle
Permission tables located in shared memory
  Restricts RM to DSP cores only
LLD resource storage still in hands of LLD
  Full backwards compatibility with applications not utilizing RM

## Slide 12: Keystone I Resource Manager (RM) LLD (2/2)
Core 0
App
QMSS LLD
App
CPPI LLD
PA LLD
QMSS LLD
CPPI LLD
PA LLD
RM
RM
rmResourceTable{
{RES_ID, START, END},
{ …, …, … },
…
}
Shared Permissions
Core 1
…
resource_table.h
Permission validation
Permission validation
Rm_init maps rmResourceTable to internal Permission Tables
Queue/cppiChOpen/ …
Queue/cppiChOpen/ …
Init/usePermissionCheck
Init/usePermissionCheck
Rm_init
Rm_start

## Slide 13: Keystone I RM: Lessons Learned
Very tedious to add new resources since RM has static definitions in both code and data of resources it manages.
Resource table with privileges defined at compile time.
  Privileges cannot be manipulated at runtime
System integrator must align Linux DTB resources with DSP RM resource table.
  Tedious and error-prone
Shared memory architecture provides no communication path to ARM.
  Not easily portable to new devices

## Slide 14: Keystone II RM: Major Requirements
Remove static definitions of managed resources from RM.
  Easy addition of new resources
Enable management of resources at all levels within system software architecture.
  Core, task, application component (LLD)
  Pre/post-main execution
Runtime modification of resource permissions.
Automate reservation of resources taken by Linux kernel.
Generic, processor-independent transport interface that allows RM instances to communicate regardless of device hardware architecture.
  Transport glue logic provided by application
  Easy to port RM to new devices

## Slide 15: Keystone II RM – Overview (1/2)
Instance-based Client/Server Architecture:
  Three instance hierarchy:
    RM Server – Global management of resources and permission policies
    RM Client – Provide resource services to system software elements
    RM Client Delegate (CD)
      Offloads management of resource subsets from Server.
      Provides singular data path to Server
  Resource services provided via instance service API
RM Instances Communication Over Generic Transport Interface
  Application must setup data paths between RM instances
  Allows RM to run on any device architecture without modification to RM source

## Slide 16: Keystone II RM – Overview (2/2)
Resources Tracked by RM Defined in Global Resource List (GRL)
  GRL captures all resources that will be tracked for a given device
  Facilitates automatic extraction of resources used by ARM Linux from Linux DTB
Policies Specify RM Instance Resource Privileges
  Resource initialization, usage, and exclusive right privileges assigned to RM instances
    Resource assignment to RM instances allows resource management at all software system levels.
  Runtime modification of policy privileges
    APIs and Linux CLI (Planned)
Resources Stored within Balanced Search Tree Allocators
  Reduce memory usage and resource lookup times
  Allocators facilitated by NameServer

## Slide 17: Keystone II RM: Overview
ARM/DSP n+2
RM Client Instance
ARM/DSP n
Transport-Specific Data Path
ARM/DSP n+1
ARM  DSP Transport
Transport API
RM CD Instance
Resources Allocated from Server
CD Service Transaction Handler
Client Service Transaction Handler
RM Server Instance
Resource Allocators
PA
QMSS
Allocation policies
CPPI
QMSS
Etc
User Mode (ARM)
Available resources are inverse of Linux DTB
Resource Policies
Transport API
PA
CPPI
QMSS
Etc
Memory Allocator
CPPI
PA
Mem Alloc
Etc
ARM/DSP n+3
RM Client Instance
QMSS
CPPI
PA
Mem Alloc
Etc
Service
Port
Service
Port
Transport API
Client Service Transaction Handler
DSP  DSP Transport
DSP  DSP Transport
Service
Port
ARM  DSP Transport
Transport API
CD Service Transaction Handler
Service
Port
Global Resource List (GRL)
Linux DTB
DSP  DSP Transport

## Slide 18: Keystone II RM: Instance Topology Example
Linux User-Space
RM Server
RM Client Delegate
RM Client
BIOS
IPC
LLD
DSP Multicore Application
Etc
ARM
DSP 1
DSP 2
LLD
Etc
LLD
Etc

## Slide 19: Keystone II RM - Services
RM Services:
  Allocate (initialization, usage)
  Free
  Map resource(s) to NameServer name
  Get resource(s) tied to existing NameServer name
  Unmap resource(s) from existing NameServer name
Non-blocking service requests directly return result
Blocking service requests return ID to system

## Slide 20: Keystone II RM: Global Resource List (GRL)
Specified in Device Tree Source (DTS) format
  Open source, dual GPL/BSD-licensed LIBFDT used for parsing GRL
Input to Server on initialization
Server instantiates allocator for each resource specified in GRL
A GRL specification for a resource includes:
  Resource name
  Resource range (base + length)
  Linux DTB alias path (if applicable)
  Resource NameServer assignments (if applicable)
Permissions not specified in GRL - In the polices

## Slide 21: Keystone II RM: Policy Example
/* RM Server global policy */
/ {
/* All RM instances expected to be resource assignees within the policy.
/* RM will fail at init if
* it finds a resource assignee that is not in the user-instances list */
valid-instances = "RM_Server",
"RM_Client_Delegate",
"RM_Client";
/* RM will deny any resource requests for resources not defined in the policy. */
/* Format for assigning resources to specific RM instances */
qmss {
gp-queue {
assignments = <2000 1000>, "iu=(RM_Server RM_Client_Delegate RM_Client)",
<3000 1>, "iux=(RM_Server) & iu=(RM_Client_Delegate RM_Client)";
<4000 1>, “s=(RM_Client_Delegate RM_Client)”;
};
};
cppi {
pass-rx-flow-id {
assignments = <0 20>, "iux=(*)";
};
};

## Slide 22: DSP CorePac CSL Layer
KeyStone Peripherals Usage

## Slide 23: CSL Overview
(Almost) All peripherals are controlled by Memory Mapped Registers (MMR).
MMR may have different address in different (future) devices.
CSL has two layers:
  The first layer assigns a standard name to MMR.
  The second layer is a set of functions to manipulate these registers.
Application needs only to know the API of the CSL functions.

## Slide 24: CSL Registers #define
MMR address depends on the device family. Currently there are two families.
The include file and device-specific CSL files are located here:
  pdk_keystone2_X_XX_XX_XX\packages\ti\csl\device\k2H
  pdk_keystone2_X_XX_XX_XX\packages\ti\csl\device\k2E
The include file cslr_device.h contains the address definitions of the MMR**
** In KeyStone 1 releases, the file cslr_device.h is here: pdk_c6678_X_XX_XX_XX\packages\ti\csl

## Slide 25: cslr_device.h
#define CSL_TAC_BEI_CFG_REGS (0x02580000 + 0x8000)
#define CSL_TAC_SGCCP_0_CFG_REGS (0x02580000 + 0x10000)
#define CSL_TAC_SGCCP_1_CFG_REGS (0x02580000 + 0x20000)
#define CSL_TAC_SGCCP_2_CFG_REGS (0x02580000 + 0x30000)
#define CSL_TAC_SGCCP_3_CFG_REGS (0x02580000 + 0x40000)
#define CSL_CIC_0_REGS (0x02600000)
#define CSL_CIC_1_REGS (0x02604000)
#define CSL_CIC_2_REGS (0x02608000)
#define CSL_GPIO_CFG_REGS (0x0260BF00)
#define CSL_BOOT_CFG_REGS (0x02620000)
#define CSL_USB_SERDES_CFG_REGS (0x02630000)
#define CSL_SEMAPHORE_REGS (0x02640000)
#define CSL_USB_CFG_REGS (0x02680000)
#define CSL_EDMACC_0_REGS (0x02700000)
#define CSL_EDMACC_4_REGS (0x02708000)
#define CSL_EDMACC_1_REGS (0x02720000)

## Slide 26: Registers Definition: cslr_XXX.h
Use the semaphore as an example
As we saw, the base address of the semaphore registers is defined at cslr_device.h
The include file cslr_sem.h is here: pdk_keystone2_X_XX_XX_XX\packages\ti\csl directory
This include file defines all the semaphore register values and structures. The following slide shows part of the cslr_sem.h file

## Slide 27
typedef struct {
volatile Uint32 SEM_PID;
volatile Uint32 SEM_SCRATCH;
volatile Uint32 SEM_RST_RUN;
volatile Uint32 SEM_EOI;
volatile Uint8 RSVD0[240];
volatile Uint32 SEM[64];
volatile Uint32 ISEM[64];
volatile Uint32 QSEM[64];
volatile Uint32 SEMFLAGL_CLEAR[16];
volatile Uint32 SEMFLAGH_CLEAR[16];
volatile Uint32 SEMFLAGL_SET[16];
volatile Uint32 SEMFLAGH_SET[16];
volatile Uint32 SEMERR;
volatile Uint32 SEMERR_CLEAR;
volatile Uint32 SEMERR_SET;
} CSL_SemRegs;
//* SEM_PID */
#define CSL_SEM_SEM_PID_SCHEME_MASK (0xC0000000u)
cslr_sem.h

## Slide 28: CSL Function Layer: csl_XXX.h and CSL_XXXAux.h
Each IP has at least two csl include file for interfacing with higher layer:
csl_XXX.h defines the objects that are used in the APIs
CSL_XXXAux.h defines the inline functions to manipulate and configure the IP. Functions that are not inline are defined in source files.
The next two slides show part of csl_sem.h and csl_semAux.h

## Slide 29
/**@defgroup CSL_SEM_FUNCTION SEM Functions@ingroup CSL_SEM_API*/
/**@addtogroup CSL_SEM_SYMBOL@{*/
/** * Handle to access SEM registers. */
#define hSEM ((CSL_SemRegs*)CSL_SEMAPHORE_REGS)
/**@}*/
csl_sem.h

## Slide 30
CSL_IDEF_INLINE Uint8 CSL_semAcquireDirect (Uint8 semNum)
{
/* Direct Access Request: Read from the SEMn register */
return CSL_FEXT (hSEM->SEM[semNum], SEM_SEM_FREE0);
}
csl_semAux.h
CSL_IDEF_INLINE void CSL_semReleaseSemaphore (Uint8 semNum)
{
/* Semaphore is released up by writing a 1 to the SEMn register */
hSEM->SEM[semNum] = CSL_FMK (SEM_SEM_FREE0, 1);
}

## Slide 31: CSL Layer Summary
Defines MMR and API to manipulate IP
Keeps application compatible with new devices
Each IP has at least one cslr file and two csl files
A partial list of CSL include files are shown on the next slide
Most of the IP have higher layer LLDs based on the CSL. So the CSL layer is transparent to the application.

## Slide 32
Partial List of CSL Include Files

## Slide 33: DSP CorePac LLD Layer: Functions
KeyStone Peripherals Usage

## Slide 34: LLD Overview
Low Level Drivers (LLD) hide the details of CSL from the application.
Simple IP and peripherals do not have LLD. The application uses CSL directly.
Most of the IPs use LLD.
Drivers for Linux system will be discussed later.

## Slide 35: KeyStone I: Interface via LLD and CSL Layers

## Slide 36: Understanding the LLD
Almost all LLDs are part of the Platform Development Kit (PDK), which is part of MCSDK.
  EDMA LLD is not part of PDK
The Real Time Software Component (RTSC) system enforces a fix structure to all the LLD modules.
The lowest level of PDK functionality is CSL.
LLD drivers are the next layer above.
The next section addresses the LLDs that are part of the PDK for MCSDK release 3.x
Almost all LLD drivers are used the same way.

## Slide 37: DSP CorePac LLD Layer: MCSDK 3.x Support
KeyStone Peripherals Usage

## Slide 38
Supported LLD Drivers: MCSDK 3.0

## Slide 39
Directory
Structure of
LLD Drivers
(1/3)

## Slide 40: Directory Structure of LLD Drivers (2/3)
Top directory
  Include files that are visible to the application
  XDC files that help with building projects
Subdirectories:
  Build: Make files to build the generic libraries
  Device: Device specific source code, usually definition and device specific functions
  Docs: The most important subdirectory, will be discussed later.
  Example: Code to support the example project
  Include: Include files that are needed for internal module build

## Slide 41: Directory Structure of LLD Drivers (3/3)
Additional Subdirectories:
  Lib: Contains two generic libraries; little endian or big endian version (the additional e means big endian)
  Package: Files that are used during the automatic building of the module
  SRC: Contains the source files that are not device dependent
  Test: Contains files that are part of the example test

## Slide 42: Docs Directory
In the top directory
  Software manifest (licensing, export control, etc.)
  Release notes
  User Guide*
  Other module-specific documents
Doxygen Subdirectory
  Collection of linked HTML files generated from the source code that describe the module objects and functions
  Easy navigation between different types of information
  The main tool to understand how to use the module
  * not all modules have a user guide

## Slide 43: HTML Documents: Main Page

## Slide 44: HTML Documents: Modules

## Slide 45: HTML Documents: Data Structures

## Slide 46: HTML Documents: Files

## Slide 47: DSP CorePac LLD Layer: LLD Usage
KeyStone Peripherals Usage

## Slide 48: Developing LLD Code
Get a resource (open, create).
  Resource management
Configure the resource (one core, each core).
  Understand the structure of the parameters of the configuration function (example to follow)
Configure dependencies (Multicore Navigator).
Use in run time.
Follow the MCSDK example to understand what needs to be done (reverse engineer the C code).

## Slide 49: PDK Example: Using SRIO Direct IO
if (coreNum == CORE_SYS_INIT)
{
System_printf ("Debug(Core %d): System Initialization for CPPI & QMSS\n", coreNum);
/* System Initialization */
if (system_init() < 0)
return;
/* Power on SRIO peripheral before using it */
if (enable_srio () < 0)
{
System_printf ("Error: SRIO PSC Initialization Failed\n");
return;
}
/* Device Specific SRIO Initializations: This should always be called before
* initializing the SRIO Driver. */
if (SrioDevice_init() < 0)
return;
/* Initialize the SRIO Driver */
if (Srio_init () < 0)
{
System_printf ("Error: SRIO Driver Initialization Failed\n");
return;
}

## Slide 50: QMSS Example: Inside qmss_init
/* Initialize Queue Manager Sub System */
result = Qmss_init (&qmssInitConfig, &qmssGblCfgParams);
if (result != QMSS_SOK)
{
System_printf ("Error initializing Queue Manager SubSystem error code : %d\n", result);
return -1;
}
/* Start the QMSS. */
if (Qmss_start() != QMSS_SOK)
{
System_printf ("Error: Unable to start the QMSS\n");
return -1;
}
/* Memory Region 0 Configuration */
memRegInfo.descBase = (UInt32 *)l2_global_address((UInt32)host_region);
memRegInfo.descSize = SIZE_HOST_DESC;
memRegInfo.descNum = NUM_HOST_DESC;
memRegInfo.manageDescFlag = Qmss_ManageDesc_MANAGE_DESCRIPTOR;
memRegInfo.memRegion = Qmss_MemRegion_MEMORY_REGION_NOT_SPECIFIED;
/* Initialize and inset the memory region. */
result = Qmss_insertMemoryRegion (&memRegInfo);

## Slide 51: Locate qmss_init in Doc Directory (QMSS)

## Slide 52
Qmss_InitCfg Struc Reference

## Slide 53: Enable SRIO
static Int32 enable_srio (void)
{
/* SRIO power domain is turned OFF by default. It needs to be turned on before doing any
* SRIO device register access. This not required for the simulator. */
/* Set SRIO Power domain to ON */
CSL_PSC_enablePowerDomain (CSL_PSC_PD_SRIO);
/* Enable the clocks too for SRIO */
CSL_PSC_setModuleNextState (CSL_PSC_LPSC_SRIO, PSC_MODSTATE_ENABLE);
/* Start the state transition */
CSL_PSC_startStateTransition (CSL_PSC_PD_SRIO);
/* Wait until the state transition process is completed. */

## Slide 54: SRIO Handle to the Instance
hDrvManagedSrioDrv = Srio_start(&drvCfg);

## Slide 55: DSP CorePac LLD Layer: NWAL (Network Adaptation Layer)
KeyStone Peripherals Usage

## Slide 56: NETCP Configuration
NETCP is very sophisticated device that can offload all networking processing from CPU, but requires (of course) configuration.
The DSP LLD does not hide all implementation details from the application; They require multiple LLD calls and explicit usage of Multicore Navigator to configure the NETCP.
NWAL (Network Adaptation Layer) is higher layer driver library for easy configuration of the NETCP device.
NETAPI is a user’s space library that supports networking.

## Slide 57: NWAL
The Network Adaptation Layer (NWAL) provides high-level driver functionality abstracting NETCP LLD for PA and SA.
NWAL supports NETCP functionality:
  Classification and routing of ingress packages based on L2 (MAC), L3 (IP) and L4 (UDP - port) or L5 (GTPU ID)
  MAC/IPSec/IP/UDP header generation for outgoing packets
NWAL APIs provide both blocking/synchronous and non-blocking/asynchronous support for the NETCP configuration.
NWAL is part of PDK release.

## Slide 58: NWAL: NETCP Security Accelerator (SA) Configuration
Unidirectional IPSec SA creation and deletion
Unidirectional IPSec Security Policy creation and deletion

## Slide 59: NWAL Dependencies
Initialization of Queue Manager Subsystem (QMSS)
Initialization of memory buffer pool with packet DMA resources including descriptors

## Slide 60: NWAL Documentation T:\pdk_keystone2_1_00_00_09\packages\ti\drv\nwal\docs\doxygen\html

## Slide 61: NWAL Functions (Partial List)

## Slide 62: For More Information
Software downloads and device-specific Data Manuals for the KeyStone SoCs can be found at TI.com/multicore.
For articles related to multicore software and tools, refer to the Embedded Processors Wiki for the KeyStone Device Architecture.
For questions regarding topics covered in this training, visit the support forums at the TI E2E Community website.