## Slide 1: KeyStone SoC Architecture Overview
KeyStone Training
Multicore Applications
Literature Number: SPRP816

## Slide 2: Agenda
KeyStone I Architecture
  CorePac & Memory Subsystem
  Internal Communications and Transport
  External Interfaces
  Coprocessors and Accelerators
  Miscellaneous
KeyStone II Architecture
  ARM Cortex-A15 CorePac
  Performance/Throughput Improvements
KeyStone Platform
  Debug
  Device-Specific Offerings
Notes: NEW

## Slide 3: KeyStone I Architecture
CorePac & Memory Subsystem
Internal Communications and Transport
External Interfaces
Coprocessors and Accelerators
Miscellaneous

## Slide 4: KeyStone I Device Architecture
Application-Specific
Coprocessors
Memory Subsystem
Multicore Navigator
Network Coprocessor
C66x™
CorePac
HyperLink
TeraNet
External Interfaces
Miscellaneous
Notes: 4
NEW

## Slide 5: KeyStone I CorePac
1 to 8 C66x CorePac DSP Cores operating at up to 1.25 GHz
  Fixed- and floating-point operations
  Code compatible with other C64x+ and C67x+ devices
L1 Memory
  Can be partitioned as cache and/or RAM
  32KB L1P per core
  32KB L1D per core
  Error detection for L1P
  Memory protection
Dedicated L2 Memory
  Can be partitioned as cache and/or RAM
  512 KB to 1 MB Local L2 per core
  Error detection and correction for all L2 memory
Direct connection to memory subsystem
C66x™
CorePac
L1P
Cache/RAM
L1D
Cache/RAM
L2 Memory Cache/RAM
Application-Specific
Coprocessors
Multicore Navigator
Network Coprocessor
HyperLink
Memory Subsystem
TeraNet
External Interfaces
Miscellaneous
1 to 8 Cores @ up to 1.25 GHz
Notes: 5
NEW

## Slide 6: KeyStone I Memory Subsystem
  Multicore Shared Memory (MSM SRAM)
  1 to 4 MB
  Available to all cores
  Can contain program and data
  All devices except C6654
Multicore Shared Memory Controller (MSMC)
  Arbitrates access of CorePac and SoC masters to shared memory
  Provides a connection to the DDR3 EMIF
  Provides CorePac access to coprocessors and IO peripherals
  Provides error detection and correction for all shared memory
  Memory protection and address extension to 64 GB (36 bits)
  Provides multi-stream pre-fetching capability
DDR3 External Memory Interface (EMIF)
  Support for 16-bit, 32-bit, and (for C667x devices) 64-bit modes
  Specified at up to 1600 MT/s
  Supports power down of unused pins when using 16-bit or 32-bit width
  Support for 8 GB memory address
  Error detection and correction
MSMC
MSM
SRAM
DDR3 EMIF
Memory Subsystem
C66x™
CorePac
L1P
Cache/RAM
L1D
Cache/RAM
Application-Specific
Coprocessors
Multicore Navigator
Network Coprocessor
HyperLink
TeraNet
External Interfaces
Miscellaneous
L2 Memory Cache/RAM
1 to 8 Cores @ up to 1.25 GHz
Notes: 6
NEW

## Slide 7
Enhanced DMA: EDMA3 1D Transfer
1D transfer is used to move a vector.

## Slide 8
EDMA3: 2D Transfer
2D transfer is used to move a matrix; That is, to share a frame between multiple cores.

## Slide 9
EDMA3: 3D Transfer
3D transfer is used to move multiple matrices. That is, to share frames between multiple cores.

## Slide 10
EDMA3: Transfer 2D Destination
It is faster to have strides in SRAM (like L2) than in DDR, so that it reads a complete line and distributes between L2 memories.

## Slide 11
EDMA3: Source and Destination
Matrix transport is used to turn rows into columns.
Based on the direction, use 2D in the source (Shared L2 to DDR) or the destination (DDR to Shared L2).

## Slide 12: KeyStone I Multicore Navigator
Provides seamless inter-core communications (messages and data exchanges) between cores, IP, and peripherals. “Fire and forget”
Low-overhead processing and routing of packet traffic to and from peripherals and cores
Supports dynamic load optimization
Data transfer architecture designed to minimize host interaction while maximizing memory and bus efficiency
Consists of a Queue Manager Subsystem (QMSS) and multiple, dedicated Packet DMA (PKTDMA) engines
Packet
DMA
Multicore Navigator
Queue
Manager
MSMC
MSM
SRAM
Memory Subsystem
C66x™
CorePac
L1P
Cache/RAM
L1D
Cache/RAM
Application-Specific
Coprocessors
Network Coprocessor
HyperLink
TeraNet
External Interfaces
Miscellaneous
L2 Memory Cache/RAM
1 to 8 Cores @ up to 1.25 GHz
DDR3 EMIF
Notes: 12
NEW

## Slide 13: KeyStone I Network Coprocessor
Provides hardware accelerators to perform L2, L3, and L4 processing and encryption that was previously done in software
Packet Accelerator (PA)
  Single or multiple IP address option
  UDP (and TCP) checksum and selected CRCs
  L2/L3/L4 support
  Quality of Service (QoS)
  Multicast to multiple destinations inside the device
  Timestamps
Security Accelerator (SA)
  Hardware encryption, decryption, and authentication
  Supports IPsec ESP, IPsec AH, SRTP, and 3GPP protocols
Network Coprocessor
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Packet
Accelerator
Security
Accelerator
Packet
DMA
Multicore Navigator
Queue
Manager
MSMC
MSM
SRAM
Memory Subsystem
C66x™
CorePac
L1P
Cache/RAM
L1D
Cache/RAM
Application-Specific
Coprocessors
HyperLink
TeraNet
External Interfaces
Miscellaneous
1 to 8 Cores @ up to 1.25 GHz
L2 Memory Cache/RAM
DDR3 EMIF
Notes: 13
NEW

## Slide 14: KeyStone I External Interfaces
2x SGMII ports support 10/100/1000 Ethernet
4x high-bandwidth Serial RapidIO (SRIO) lanes
2x PCIe at 5 Gbps
SPI for boot operations
UART for development/testing
I2C for EPROM at 400 Kbps
GPIO
Device-specific Interfaces
  Wireless Applications
  General Purpose Applications
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
S
P
I
I
C
2
GPIO
Device Specific I/O
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Packet
DMA
Multicore Navigator
Queue
Manager
MSMC
MSM
SRAM
Memory Subsystem
C66x™
CorePac
L1P
Cache/RAM
L1D
Cache/RAM
Application-Specific
Coprocessors
HyperLink
TeraNet
Miscellaneous
Network Coprocessor
1 to 8 Cores @ up to 1.25 GHz
L2 Memory Cache/RAM
DDR3 EMIF
Packet
Accelerator
Security
Accelerator
Device Specific I/O
Notes: 14
NEW

## Slide 15: TeraNet Switch Fabric
A non-blocking switch fabric that enables fast and contention-free internal data movement
Provides a configured way – within hardware – to manage traffic queues and ensure priority jobs are getting accomplished while minimizing the involvement of the CorePac cores
Facilitates high-bandwidth communications between CorePac cores, subsystems, peripherals, and memory
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
S
P
I
I
C
2
GPIO
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Packet
DMA
Multicore Navigator
Queue
Manager
MSMC
MSM
SRAM
Memory Subsystem
C66x™
CorePac
L1P
Cache/RAM
L1D
Cache/RAM
Application-Specific
Coprocessors
HyperLink
TeraNet
Miscellaneous
Network Coprocessor
1 to 8 Cores @ up to 1.25 GHz
L2 Memory Cache/RAM
DDR3 EMIF
Packet
Accelerator
Security
Accelerator
Device Specific I/O
Device Specific I/O
Notes: 15
NEW

## Slide 16: KeyStone I TeraNet Data Connections
QMSS
MSMC
DDR3
Shared L2
S
S
Core
S
PCIe
S
TAC_BE
S
SRIO
PCIe
QMSS
M
M
M
TPCC
16ch QDMA
M
TC0
M
TC1
M
M
DDR3
XMC
M
DebugSS
M
TPCC
64ch
QDMA
M
TC2
M
TC3
M
TC4
M
TC5
TPCC
64ch
QDMA
M
TC6
M
TC7
M
TC8
M
TC9
Network
Coprocessor
M
HyperLink
M
HyperLink
S
AIF / PktDMA
M
FFTC / PktDMA
M
RAC_BE0,1
M
TAC_FE
M
SRIO
S
S
RAC_FE
S
TCP3d
S
TCP3e_W/R
S
VCP2 (x4)
S
M
EDMA_0
EDMA_1,2
Core
S
M
Core
S
M
L2 0-3
S
M
Facilitates high-bandwidth communication links between DSP cores, subsystems, peripherals, and memories.
Supports parallel orthogonal communication links
CPUCLK/2
256bit TeraNet
FFTC / PktDMA
M
TCP3d
S
RAC_FE
S
VCP2 (x4)
S
VCP2 (x4)
S
VCP2 (x4)
S
RAC_BE0,1
M
CPUCLK/3
128bit TeraNet
S
S
S
S
Notes: CPT see physical addresses. In MSMC, one CPT per bank.

## Slide 17: KeyStone I HyperLink Bus
Provides the capability to expand the device to include hardware acceleration or other auxiliary processors
Supports four lanes with up to 12.5 Gbaud per lane
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
S
P
I
I
C
2
GPIO
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Packet
DMA
Multicore Navigator
Queue
Manager
MSMC
MSM
SRAM
Memory Subsystem
C66x™
CorePac
L1P
Cache/RAM
L1D
Cache/RAM
Application-Specific
Coprocessors
HyperLink
TeraNet
Miscellaneous
Network Coprocessor
1 to 8 Cores @ up to 1.25 GHz
L2 Memory Cache/RAM
DDR3 EMIF
Debug/Trace
Packet
Accelerator
Security
Accelerator
Device Specific I/O
Device Specific I/O
Notes: 17
NEW

## Slide 18: KeyStone I Miscellaneous Elements
Boot ROM
Semaphore module provides atomic access to shared chip-level resources.
Power Management
Three on-chip PLLs:
  PLL1 for CorePacs, except
  PLL2 for DDR3
  PLL3 for Packet Acceleration
Three EDMA controllers
Eight 64-bit timers
Inter-Processor Communication (IPC) Registers
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
S
P
I
I
C
2
GPIO
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Packet
DMA
Multicore Navigator
Queue
Manager
MSMC
MSM
SRAM
Memory Subsystem
1 to 8 Cores @ up to 1.25 GHz
C66x™
CorePac
L1P
Cache/RAM
L1D
Cache/RAM
L2 Memory Cache/RAM
Application-Specific
Coprocessors
HyperLink
TeraNet
Network Coprocessor
Power
Boot ROM
Semaphore
x3
PLL
EDMA
x3
Management
DDR3 EMIF
Debug/Trace
Packet
Accelerator
Security
Accelerator
Device Specific I/O
Device Specific I/O
Notes: 18
NEW

## Slide 19: KeyStone Central Interrupt Controller
CIC0
CIC1
CIC2
Events
C66x CorePac0
C66x CorePac1
C66x CorePac2
C66x CorePac3
C66x CorePac4
C66x CorePac5
C66x CorePac6
C66x CorePac7
HyperLink
EDMA CC0
EDMA CC1
EDMA CC2
EDMA CC3
EDMA CC4
ARM A15
CorePac
Peripherals
Notes: 19
3 interrupt controllers each one connected to specific corePacs or peripherals in the system. Apart from each corePac have a interrupt controller we have a centralized controleer to map events generated in one block to another block in the system.

## Slide 20: Diagnostic Enhancements
Embedded Trace Buffers (ETB) enhance the diagnostic capabilities of the CorePac.
CP Monitor enables diagnostic capabilities on data traffic through the TeraNet switch fabric.
Automatic statistics collection and exporting (non-intrusive)
Monitor individual events for better debugging
Monitor transactions to both memory end point and Memory-Mapped Registers (MMR)
Configurable monitor filtering capability based on address and transaction type
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
S
P
I
I
C
2
GPIO
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Packet
DMA
Multicore Navigator
Queue
Manager
MSMC
MSM
SRAM
Memory Subsystem
C66x™
CorePac
L1P
Cache/RAM
L1D
Cache/RAM
Application-Specific
Coprocessors
HyperLink
TeraNet
Miscellaneous
Network Coprocessor
1 to 8 Cores @ up to 1.25 GHz
L2 Memory Cache/RAM
DDR3 EMIF
Debug/Trace
Packet
Accelerator
Security
Accelerator
Device Specific I/O
Device Specific I/O
Notes: 20
NEW

## Slide 21: KeyStone II Architecture
ARM Cortex-A15 CorePac
Performance/Throughput Improvements

## Slide 22: Keystone II Architecture Example

## Slide 23: KeyStone II Device Architecture
HyperLink Bus
External Interfaces
10 Gigabit Ethernet (10 GBE)
Network Coprocessor
ARM A15 CorePac
Memory Subsytem
C66x CorePac
TeraNet Switch Fabric
Multicore Navigator
Miscellaneous
Notes: 23
We added ARM A15 Core into the mix.
This helps the customer to implement additional blocks of their system.
This integration helps them to reduce the power foot print of the system and also able to provide a cheaper solution by reducing a bill of materials.
Another key addition is the 10 Giga bit ethernet SS that can help to provide high packet based data rate.
As we move along opening these blocks we can also see that we increased the instances of some of these peripherals to further enhance the SoC experience for the customers.
Also as we proceed through the presentation, I will emphasize on some key design features or enhancements that we made in KS II as opposed to KS I.

## Slide 24: ARM Cortex-A15 CorePac
Single, Dual, or Quad-ARM A15 CorePac operating at up to 1.4 GHz.
  Full implementation of ARMv7-A architecture instruction set
  Integrated Neon and Vector Floating-Point Unit
L1 Memory: 32KB L1 per ARM A15 for caching program and data
  L2 Memory:
  Shared L2 Cache Memory with full cache coherency using Snoop Control Unit (SCU)
  4 MB L2 Cache is shared between the 1 to 4 ARM A15 core(s).
The AMBA 4.0 AXI Coherency Extension (ACE) master port is connected directly to the MSMC2 for short-path access to shared MSMC SRAM.
The ACE also provides IO-coherent access to the shared memory and external memory connected through the EMIF.
Cluster-level and core-level power management and low-power standby modes (also known as WFI/WFE modes)
Notes: 24
Contains an ARM cluster with one, two or 4 ARMs in it.
Running at 1.4GHz.
Two levels of memory just like DSP.
But L2 is shared for cache coherency.
Connected to the MSMC through ACE also provided cachec coherency with other peripheral masters.
Power management.(Wait for Interrupt/ Wait for Event).
BootROM.

## Slide 25: KeyStone II Memory Subsystem: MSM/MSMC
  Multicore Shared Memory (MSM SRAM)
  2-6 MB shared among the C66x and ARM A15 CorePacs.
  May contain program and data
  Multicore Shared Memory Controller (MSMC version 2.0)
  Arbitrates access of C66x and ARM A15 CorePac and SoC masters to shared and external memory through DDR3 EMIF
  Provides error detection and correction for all shared memory
  Memory protection and address extension to 64 GB (36 bits)
  Provides multi-stream pre-fetching capability
  Support for ARM coherency with EDMA/peripheral masters in DDR3A and MSMC SRAM space
  8 SRAM banks
  Runs at the DSP frequency, thereby increasing memory access by fourfold compared to previous MSMC v1.0
Notes: 25
MSMC is another block in the architecture which got a face lift in KS II.
Increased the SRAM in some devices to 6MB.
Also this memory is shared across DSP and ARM.
MSMC controller provides access to the DDR3 through EMIF.
Address extension to 64GB.
ARM cache coherency with EDMA and peripheral masters.
Depending of the device variation we have 2 – 8 SRAM banks.
Key improvement is CPU/1 frequency.

## Slide 26: KeyStone II Memory Subsystem: DDR3
  Up to two DDR3 subsystem(s) per device:
  The first DDR3 subsystem (DDR3A) supports up to 8 GB memory addresses and is connected to the CorePac(s) through the MSMC.
  When present, the second DDR3 subsystem (DDR3B) supports up to 2GB memory address and is connected directly to the TeraNet.
  Each DDR consists of a 64b/72b EMIF controller:
  Supports 16-bit, 32-bit, and 64-bit modes .
  Operates at up to 1600 MT/s
  Supports power down of unused pins when using 16-bit or 32-bit width
Notes: 26
Based on the device selected, we might have 1 or 2 DDR3 interface.
First DDR3 interface supports 8GB
Second DDR3 interface supports 2GB
Each interface is 72b EMIF controller with 8b EC.
Separate access for ARM and peripheral masters and also provides additional bandwidth.
No Cache coherency in the second DDR3 interface.

## Slide 27: KeyStone II Multicore Navigator
Consists of the following:
  2x Queue Manager
  Multiple, dedicated Packet DMA engines
  2x infrastructure DMAs
Provides seamless inter-core communications (messages and data exchanges) between cores, IP, and peripherals. “Fire and forget.”
Low-overhead processing and routing of packet traffic to and from peripherals and cores
Supports dynamic load optimization
Data transfer architecture designed to minimize host interaction while maximizing memory and bus efficiency
Supports up to 16K hardware queues and 1M descriptors (32K internal).
Notes: 27
Enhanced QMSS.
Some variations will have two QM wit 2 Infrastructure DMAs.
As usual each peripheral that supports packetization has a PktDMA.
Off loads most of the routing from the cores.
Can also be used for dynamic load balancing by providing specialized PDSP (More friendlier than KS I).

## Slide 28: KeyStone II Multicore Navigator Architecture
TeraNet

## Slide 29: KeyStone II Network Coprocessor (NETCP)
Consists of one or two Network Coprocessor(s)
Provides hardware accelerators to perform L2, L3, and L4 processing and encryption that was previously done in software
Packet Accelerator (PA)
  Single IP address option
  UDP (and TCP) checksum and selected CRCs
  L2/L3/L4 support
  Quality of Service (QoS)
  Multicast to multiple queues
  Timestamps
Security Accelerator (SA)
  Hardware encryption, decryption, and authentication
  Supports IPsec ESP, IPsec AH, SRTP, and 3GPP protocols
  2x 5-port Ethernet switches (depending on number of instances of NETCP) with 4-8 ports connecting to 4-8 SGMII ports and one port connecting to the Packet and Security Accelerators.
Notes: 29
Same as KS I except we have a 5 port switch inside the NetCP instead of a 3 port switch.
Some device variation we might have 2 instance of the netCp to increase the supported BW.
PA and SA are same.

## Slide 30: KeyStone II External Interfaces
8x SGMII ports support 10/100/1000M Ethernet through 1-2x 5-port Ethernet switch(es).
2x XGMII ports support up to 10G Ethernet through a 3-port Ethernet switch.
4x high-bandwidth Serial RapidIO (SRIO v2.1) lanes for inter-DSP applications
2x PCIe at 5 Gbps
2x USB 3.0
3x SPI modules with up to four chip selects per module.
2x UART for development/testing
3x I2C at 400 Kbps
32 GPIO pins
EMIF 16
Device-specific interfaces
Notes: 30
SGMII
XGMII
SRIO
PCIe
SPI
UART for debug.
USB – for connecting to solid state devices.
I2C
GPIO
EMIF16

## Slide 31: KeyStone II HyperLink Bus
Provides TI-propriety, high-speed interconnects termed HyperLink.
Up to 2x HyperLink modules with 4 lanes each.
Provides the capability to expand the device to include hardware acceleration or other auxiliary processors
Supports up to 12.5 Gbaud per lane
Notes: 31
Have two instances in some variations.
TI propriety.

## Slide 32: KeyStone II Miscellaneous Elements
ARM- and DSP-driven Boot ROM:
  C66x CorePacs support booting from SRIO, PCIe, I2C Master, I2C Slave, SPI, Ethernet, XIP, and HyperLink.
  ARM CorePacs support booting from UART, NAND, XIP, SPI, Ethernet, PCIe, I2C, SRIO and HyperLink.
  Support varies by peripheral availability
Semaphore module provides atomic access to shared chip-level resources.
Secure Mode (1-time burn security key)
Power Management:
  Manages power- and clock-switching of individual IPs and CorePac(s).
  Supports Dynamic Power Switching (DPS):
    Power-state hibernation modes 1 and 2
    Manages each C66x CorePac, each ARM core, and/or the entire ARM CorePac
  Reset isolation capability on select peripherals
  SmartReflex Class 0 and Class 3
Up to 5 on-chip PLLs:
  One Main PLL
  One PLL for DDR3A
  One PLL for DDR3B
  One PLL for ARM CorePac
  One PLL for Packet Accelerator
5x EDMA controllers
20x 64-bit timers
Inter-Processor Communication (IPC) Registers
Notes: 32
2 bootROM.
Semaphore help to manage shared memory access.
Secure Mode. – provides secure boot.
Provides access to secure memory from masters.
Disabling debug and JTAG capabilities .
One Time programming memory for customer to burn the security keys.
Power management.
PLL
Timers
IPC interrupts for core to core messaging.

## Slide 33: KeyStone Platform
Device-Specific Offerings

## Slide 34: Device-Specific: C6670 for Wireless Apps
Device-specific Coprocessors:
  2x FFT Coprocessor (FFTC)
  Turbo Decoder/Encoder Coprocessor (TCP3d/3e)
  4x Viterbi Coprocessor (VCP2)
  Bit-rate Coprocessor (BCP)
  2x Rake Search Accelerator (RSA)
Device-specific Interfaces:
  6x Antenna Interface 2 (AIF2)
4 Cores @ 1.0 GHz / 1.2 GHz
FFTC
TCP3d
C6670
MSMC
2MB
MSM
SRAM
64-Bit
DDR3 EMIF
TCP3e
x2
x2
Coprocessors
VCP2
x4
Power
Management
Boot ROM
Semaphore
Memory Subsystem
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
A
I
F
2
x6
S
P
I
I
C
2
Packet
DMA
Multicore Navigator
Queue
Manager
x3
32KB L1P
Cache/RAM
32KB L1D
Cache/RAM
1024KB L2 Cache/RAM
RSA
RSA
x2
PLL
EDMA
x3
HyperLink
TeraNet
Network Coprocessor
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
BCP
GPIO
C66x™
CorePac
x2
Debug/Trace
Packet
Accelerator
Security
Accelerator
Notes: 34
NEW

## Slide 35: Device-Specific: C667x General Purpose
Device-specific Interfaces:
2x Telecommunications Serial Port (TSIP)
  Asynchronous Memory Interface (EMIF16):
  Connects memory up to 256 MB
  Three modes:
    Synchronized SRAM
    NAND flash
    NOR flash
1 to 8 Cores @ up to 1.25 GHz
Power
Management
Boot ROM
Semaphore
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
T
S
I
P
x2
S
P
I
I
C
2
Packet
DMA
Multicore Navigator
Queue
Manager
G
P
I
O
x3
PLL
EDMA
x3
E
M
I
F
1
6
C6671/C6672 C6674/C6678
4MB
MSM
SRAM
64-Bit
DDR3 EMIF
MSMC
512KB L2 Cache/RAM
TeraNet
TeraNet
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Memory Subsystem
HyperLink
Network Coprocessor
C66x™
CorePac
32KB L1P
Cache/RAM
32KB L1D
Cache/RAM
Debug/Trace
Packet
Accelerator
Security
Accelerator
Notes: 35
NEW

## Slide 36
Device-Specific: C665x General Purpose
Device-specific Coprocessors:
  Turbo Decoder Coprocessor (TCP3d)
  2x Viterbi Coprocessor (VCP2)
Device-specific Interfaces:
  Asynchronous Memory Interface (EMIF16)
  Universal Parallel Port (UPP)
  2x Multichannel Buffered Serial Ports (McBSP)
Device-specific Memory:
  1 MB Multicore Shared Memory (MSM SRAM)
  32-bit DDR3 Interface
1 or 2 Cores @ up to 1.25 GHz
C66x™
CorePac
C6655/57
MSMC
1MB
MSM
SRAM
32-Bit
DDR3 EMIF
Memory Subsystem
Packet
DMA
Multicore Navigator
Queue
Manager
x2
PLL
EDMA
VCP2
TCP3d
x2
Coprocessors
HyperLink
TeraNet
Ethernet
MAC
SGMII
S
R
I
O
x4
S
P
I
U
A
R
T
x2
P
C
I
e
x2
I2C
U
P
P
McBSP
x2
G
P
I
O
Boot ROM
Debug/Trace
Power
Management
Semaphore
Security /
Key Manager
Timers
2nd core, C6657 only
32KB L1P
Cache/RAM
32KB L1D
Cache/RAM
1024KB L2 Cache
EMIF16
Notes: 36
NEW

## Slide 37
Device-Specific: C665x Power Optimized
Device-specific Interfaces:
  Asynchronous Memory Interface (EMIF16)
  Universal Parallel Port (UPP)
  2x Multichannel Buffered Serial Ports (McBSP)
Device-specific Memory:
  32-bit DDR3 Interface
1 Core @ 850 MHz
C66x™
CorePac
C6654
MSMC
32-Bit
DDR3 EMIF
Memory Subsystem
Packet
DMA
Multicore Navigator
Queue
Manager
PLL
EDMA
TeraNet
Ethernet
MAC
SGMII
S
P
I
U
A
R
T
x2
P
C
I
e
x2
I2C
U
P
P
M
c
B
S
P
x2
G
P
I
O
EMIF16
Boot ROM
Debug/Trace
Power
Management
Semaphore
Security /
Key Manager
Timers
32KB L1P
Cache/RAM
32KB L1D
Cache/RAM
1024KB L2 Cache
x2
Notes: 37
NEW

## Slide 38: KeyStone C665x: Key HW Variations
HW Feature | C6654 | C6655 |  | C6657
CorePac Frequency (GHz) | 0.85 | 1 @ 1.0, 1.25 | 2 @ 0.85, 1.0, 1.25 | 
Multicore Shared Memory (MSM) | No | 1024KB SRAM |  | 
DDR3 Maximum Data Rate | 1066 | 1333 |  | 
Serial Rapid I/O Lanes | No | 4x |  | 
HyperLink | No | Yes |  | 
Viterbi Coprocessor (VCP) | No | 2x |  | 
Turbo Coprocessor Decoder (TCP3d) | No | Yes |  | 
Network Coprocessor (NETCP) | No | No |  | 

## Slide 39: KeyStone II Part Numbering

## Slide 40: K2H (K2K) Compared to K2E
Platform | C66x DSP | ARM A15 | Max Clock Ghz | MSMC Shared Memory – MB | Navigator Queues | DDR3 EMIF 72-bit 1600 MT/s | 5-Port 1GB Switch | 3-Port 10GB Switch | USB 3.0 | HyperLink | SRIO x4 | PCIe x2 | TSIP
K2E | 0x to 1x | 1x to 4x | ARM = 1.4 DSP = 1.4 | 2 | 8K | 1x | 1x to 2x | 2x | 2x | 1x | -- | 2x | 1x
K2H | 4x to 8x | 2x to 4x | ARM = 1.4 DSP = 1.2 | 6 | 16K | 2x | 1x | -- | 1x | 2x | 1x | 1x | --

## Slide 41: K2K Platform Device Variations
The K2K platform has two variations:
TCI6634K2K
  8x C66x CorePacs
  16x Rake/Search Accelerators (RSA)
  2x Queue Managers support up to 16K queues
  1x USB3.0 to support solid state drive
  6x Antenna Interface 2 (AIF2)
  1x 3 port 10GBE Switch Subsystem
  1x Network Coprocessor (NETCP)
  4x Receive Acceleration Coprocessors (RAC)
  Transmit Acceleration Coprocessor (TAC)
  4x Turbo Decoder/Encoder Coprocessors (TCP3d/3e)
  8x Viterbi Coprocessors (VCP2)
  6x FFT Coprocessors (FFTC)
  Bit-rate Coprocessor (BCP)
Notes: 41
NEW

## Slide 42: K2K Platform Device Variations
The K2K platform has two variations:
TCI6634K2K
  8x C66x CorePacs
  16x Rake/Search Accelerators (RSA)
  2x Queue Managers support up to 16K queues
  1x USB3.0 to support solid state drive
  6x Antenna Interface 2 (AIF2)
  1x 3 port 10GBE Switch Subsystem
  1x Network Coprocessor (NETCP)
  4x Receive Acceleration Coprocessors (RAC)
  Transmit Acceleration Coprocessor (TAC)
  4x Turbo Decoder/Encoder Coprocessors (TCP3d/3e)
  8x Viterbi Coprocessors (VCP2)
  6x FFT Coprocessors (FFTC)
  Bit-rate Coprocessor (BCP)
TCI6638K2K
  Same as TCI6634K2K plus …
  Quad-ARM A15 CorePac
Notes: 42
NEW

## Slide 43: K2H Platform Device Variations
The K2H platform has two variations:
66AK2H12
  8x C66x CorePacs
  Quad-ARM A15 CorePac
  2x Queue Managers support up to 16K queues
  1x Network Coprocessor (NETCP)
  1x USB3.0 to support solid state drive
  10GBE interface is NOT available.
Notes: 43
NEW

## Slide 44: K2H Platform Device Variations
The K2H platform has two variations:
66AK2H12
  8x C66x CorePacs
  Quad-ARM A15 CorePac
  2x Queue Managers support up to 16K queues
  1x Network Coprocessor (NETCP)
  1x USB3.0 to support solid state drive
  10GBE interface is NOT available
66AK2H06
  Scaled-down version of 66AK2H12
  4x C66x CorePacs
  Dual-ARM A15 CorePac
Notes: 44
NEW

## Slide 45: K2E Platform Device Variations
The K2E platform has four variations:
AM5K2E04
  First ARM-only TI multicore device
  Quad-ARM A15 CorePac
  1x Queue Manager supports up to 8K queues
  1x Network Coprocessors (NETCP)
  1x 3 port 10GBE Switch Subsystem
  Telecommunications Serial Port (TSIP)
  2x USB 3.0 to support solid state drive
  No SRIO
Notes: 45
NEW

## Slide 46: K2E Platform Device Variations
The K2E platform has four variations:
AM5K2E04
  First ARM-only TI multicore device
  Quad-ARM A15 CorePac
  1x Queue Manager supports up to 8K queues
  1x Network Coprocessors (NETCP)
  1x 3 port 10GBE Switch Subsystem
  Telecommunications Serial Port (TSIP)
  2x USB 3.0 to support solid state drive
  No SRIO
AM5K2E02
  Scaled-down version of AM5K2E04
  Dual-ARM A15 CorePac
  1x Network Coprocessor
  10GBE not included
Notes: 46
NEW

## Slide 47: K2E Platform Device Variations
The K2E platform has four variations:
AM5K2E04
  First ARM-only TI multicore device
  Quad-ARM A15 CorePac
  1x Queue Manager supports up to 8K queues
  1x Network Coprocessors (NETCP)
  1x 3 port 10GBE Switch Subsystem
  Telecommunications Serial Port (TSIP)
  2x USB 3.0 to support solid state drive
  No SRIO
AM5K2E02
  Scaled-down version of AM5K2E04
  Dual-ARM A15 CorePac
  1x Network Coprocessor
  10GBE not included
66AK2E05
  Same as AM5K2E04 with a single C66x CorePac added
Notes: 47
NEW

## Slide 48: K2E Platform Device Variations
The K2E platform has four variations:
AM5K2E04
  First ARM-only TI multicore device
  Quad-ARM A15 CorePac
  1x Queue Manager supports up to 8K queues
  1x Network Coprocessors (NETCP)
  1x 3 port 10GBE Switch Subsystem
  Telecommunications Serial Port (TSIP)
  2x USB 3.0 to support solid state drive
  No SRIO
AM5K2E02
  Scaled-down version of AM5K2E04
  Dual-ARM A15 CorePac
  1x Network Coprocessor
  10GBE not included
66AK2E05
  Same as AM5K2E04 with a single C66x CorePac added
66AK2E02
  Same as AM5K2E02 except with a single-ARM A15 CorePac and a single C66x CorePac added
Notes: 48
NEW

## Slide 49: KeyStone I Compared to KeyStone II
IP block | KeyStone I | KeyStone II
ARM Cortex-A15 core | No | 4x
MSMC | Ver1.0 | Ver2.0
DDR3 EMIF (64-bit) | 1x | 2x
MSMC SRAM | 2 Mbytes | 6 Mbytes
DDR3A memory (max) | 8 Gbytes | 8 Gbytes
DDR3B memory (max) | No | 2 Gbytes (for ARM and DSP cores) 512 Mbytes (system masters)
ARM Boot ROM | No | 256 Kbytes
OTP memory | No | 4 Kbits
Queue Manager Subsystem + PKTDMA | 1x | 2x
EDMA3CC | 3x | 5x
EDMA3TC | 10x | 14x
HyperLink | 1 x 4 | 2 x 4
10 Gigabit Ethernet (10GBE) | No | 1 x 2
UART | 1x | 2x
SPI | 1x | 3x
I2C | 1x | 3x
GPIO | 1x 16 | 1x 32
Timer64 | 8x | 20x
USB3 | No | 1x to 3x
PLL controller + On-chip PLLs | 3x | 5x
ARM Subsystem ETB (16 KB) | No | 1x
DSP TETB (4 KB) | 4x | 8x
Tracer | 16x | 32x
MPU | 6x | 15x
Security Manager | No | 1x

## Slide 50: For More Information
Device-specific Data Manuals for the KeyStone SoCs can be found at TI.com/multicore.
Multicore articles, tools, and software are available at Embedded Processors Wiki for the KeyStone Device Architecture.
View the complete C66x Multicore SOC Online Training for KeyStone Devices, including details on the individual modules.
For questions regarding topics covered in this training, visit the support forums at the TI E2E Community website.