## Slide 1: McBSP
Copyright © 2012 Texas Instruments. All rights reserved.
Technical Training
Organization
T TO
C6657 Workshop

## Slide 2: Outline
McBSP Overview (data Ch on DSK)
Technical Training
Organization
T TO

## Slide 3: McBSP Block Diagram
CPU
EDMA
I n t e r n a l
B u s
D
X
R
DX
XSR
CLKR
FSR
CLKX
FSX
CLKS
R
B
R
D
R
R
32
DR
RSR
Expand (optional)
Compress (optional)
McBSP Control
Registers
SPCR
RCR
XCR
PCR
SRGR
McBSP = Multi-channel Buffered Serial Port
DRR = Data Rcv Reg, DXR = Data Xmt Reg, RBR = Rcv Buffer Reg
RSR = Rcv Shift Reg, XSR = Xmt Shift Reg
Technical Training
Organization
T TO
Let’s look at some basic definitions…

## Slide 4: Basic Definitions - Bit, Word
CLK
b7
b6
b5
b4
b3
b2
b1
b0
Word
FS
a1
a0
Bit
D
“Word” or “channel” contains #bits specified by WDLEN1 (8, 12, 16, 20, 24, 32)
“Bit” - one data bit per SP clock period
SP Ctrl (SPCR)
Rcv Ctrl (RCR)
Xmt Ctrl (XCR)
Rate (SRGR)
Pin Ctrl (PCR)
Serial Port
RWDLEN1
XWDLEN1

## Slide 5: Basic Definitions - Frame
SP Ctrl (SPCR)
Rcv Ctrl (RCR)
Xmt Ctrl (XCR)
Rate (SRGR)
Pin Ctrl (PCR)
Serial Port
“Frame” - contains one or multiple words
w0
w1
w2
w3
w4
w5
w6
w7
Frame
Word
w6
w7
D
FS
RFRLEN1
XFRLEN1
FRLEN1 specifies #words per frame (1-128)
RWDLEN1
XWDLEN1

## Slide 6: EDMA Sync Events from McBSP
“Ready to Read”
EDMA
C O D E C
REVT1
RRDY=1
DRR
RBR
RSR
DXR
XSR
Receive Event (REVT1)
When value reaches DRR, sync event sent to EDMA.
This can be used to trigger an EDMA transfer.
SP Ctrl (SPCR)
Rcv Ctrl (RCR)
Xmt Ctrl (XCR)
Rate (SRGR)
Pin Ctrl (PCR)
Serial Port
XRDY=1
“Ready to Write”
XEVT1
Transmit Event (XEVT1)
Sent to EDMA when DXR is emptied (and ready to receive another value)
XRDY
RRDY

## Slide 7: AIC23 Audio CODEC Example
Control
Channel
Data
Channel (Stereo)
24-bit resolution (90db SNR ADC, 100db SNR DAC)
Multiple Digital transfer widths (16-bits, 20-bits, 24-bits, 32-bits)
Programmable frequency (8K, 16K, 24K, 32K, 44.1K, 48K, 96K)
AIC23 has two serial ports:
  Control: reads/writes AIC23’s control registers
  Data: Bidirectional pin to transfer data from A/D and to D/A converters
Technical Training
Organization
T TO
2-wire
SPI
Right Justified
Left Justified
I2S
DSP Mode
C6657: I2C
C6657 : McBSP1

## Slide 8: SCR & McBSP
EDMA3
TC0
TC1
TC2
TC3
EMAC HPI PCI
SRIO
TCP2
VCP2
McBSP PCI Utopia
DDR2
L2 Mem Ctrl
L2
L1P
L1D
D
S
M
L
D
S
M
L
CPU
C64x+ MegaModule
M
S
S
M
M
S
IDMA
L1P Mem Ctrl
L1D Mem Ctrl
AET
DATA
SCR
CFG
SCR
EMIF
128
128
Cfg
PERIPH
M
S
M
S
Master
Slave
McBSP is a slave on the DATA SCR
DRR/DXR (data) registers are accessed via the DATA SCR
McBSP configuration registers are accessed via the CFG SCR
32
PERIPH =
All peripheral’s
Cfg registers
SCR = Switched Central Resource
32
External Mem Cntl
CC
Notes: This is somewhat of a simplification of the SCRs and megamodule diagrams in the datasheet.

## Slide 9
ti
Technical Training
Organization
TTO
Technical Training
Organization
T TO