## Slide 1: Extended Memory Controller and the MPAX registers
Multicore programming and Applications
February 19, 2013

## Slide 2: Agenda
A little reminder of the 6678
Purpose of MPAX part of XMC
CorePac MPAX registers
CorePac MAR registers
Teranet Access MPAX registers
Real code examples

## Slide 3: KeyStone and C66 CorePac
1 to 8 C66x CorePac DSP Cores operating at up to 1.25 GHz
  Fixed- and floating-point operations
  Code compatible with other C64x+ and C67x+ devices
L1 Memory
  Can be partitioned as cache and/or RAM
  32KB L1P per core
  32KB L1D per core
  Error detection for L1P
  Memory protection
Dedicated L2 Memory
  Can be partitioned as cache and/or RAM
  512 KB to 1 MB Local L2 per core
  Error detection and correction for all L2 memory
Direct connection to memory subsystem
C66x™
CorePac
L1P
Cache/RAM
L1D
Cache/RAM
L2 Memory Cache/RAM
Application-Specific
Coprocessors
Multicore Navigator
Network Coprocessor
HyperLink
Memory Subsystem
TeraNet
External Interfaces
Miscellaneous
1 to 8 Cores @ up to 1.25 GHz
Notes: 3
NEW

## Slide 4: KeyStone I Memory Subsystem
  Multicore Shared Memory (MSM SRAM)
  1 to 4 MB
  Available to all cores
  Can contain program and data
  All devices except C6654
Multicore Shared Memory Controller (MSMC)
  Arbitrates access of CorePac and SoC masters to shared memory
  Provides a connection to the DDR3 EMIF
  Provides CorePac access to coprocessors and IO peripherals
  Provides error detection and correction for all shared memory
  Memory protection and address extension to 64 GB (36 bits)
  Provides multi-stream pre-fetching capability
DDR3 External Memory Interface (EMIF)
  Support for 16-bit, 32-bit, and (for C667x devices) 64-bit modes
  Specified at up to 1600 MT/s
  Supports power down of unused pins when using 16-bit or 32-bit width
  Support for 8 GB memory address
  Error detection and correction
MSMC
MSM
SRAM
DDR3 EMIF
Memory Subsystem
C66x™
CorePac
L1P
Cache/RAM
L1D
Cache/RAM
Application-Specific
Coprocessors
Multicore Navigator
Network Coprocessor
HyperLink
TeraNet
External Interfaces
Miscellaneous
L2 Memory Cache/RAM
1 to 8 Cores @ up to 1.25 GHz
Notes: 4
NEW

## Slide 5: TeraNet Switch Fabric
A non-blocking switch fabric that enables fast and contention-free internal data movement
Provides a configured way – within hardware – to manage traffic queues and ensure priority jobs are getting accomplished while minimizing the involvement of the CorePac cores
Facilitates high-bandwidth communications between CorePac cores, subsystems, peripherals, and memory
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
S
P
I
I
C
2
GPIO
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Packet
DMA
Multicore Navigator
Queue
Manager
MSMC
MSM
SRAM
Memory Subsystem
C66x™
CorePac
L1P
Cache/RAM
L1D
Cache/RAM
Application-Specific
Coprocessors
HyperLink
TeraNet
Miscellaneous
Network Coprocessor
1 to 8 Cores @ up to 1.25 GHz
L2 Memory Cache/RAM
DDR3 EMIF
Packet
Accelerator
Security
Accelerator
Device Specific I/O
Device Specific I/O
Notes: 5
NEW

## Slide 6: KeyStone I TeraNet Data Connections
QMSS
MSMC
DDR3
Shared L2
S
S
Core
S
PCIe
S
TAC_BE
S
SRIO
PCIe
QMSS
M
M
M
TPCC
16ch QDMA
M
TC0
M
TC1
M
M
DDR3
XMC
M
DebugSS
M
TPCC
64ch
QDMA
M
TC2
M
TC3
M
TC4
M
TC5
TPCC
64ch
QDMA
M
TC6
M
TC7
M
TC8
M
TC9
Network
Coprocessor
M
HyperLink
M
HyperLink
S
AIF / PktDMA
M
FFTC / PktDMA
M
RAC_BE0,1
M
TAC_FE
M
SRIO
S
S
RAC_FE
S
TCP3d
S
TCP3e_W/R
S
VCP2 (x4)
S
M
EDMA_0
EDMA_1,2
Core
S
M
Core
S
M
L2 0-3
S
M
Facilitates high-bandwidth communication links between DSP cores, subsystems, peripherals, and memories.
Supports parallel orthogonal communication links
CPUCLK/2
256bit TeraNet
FFTC / PktDMA
M
TCP3d
S
RAC_FE
S
VCP2 (x4)
S
VCP2 (x4)
S
VCP2 (x4)
S
RAC_BE0,1
M
CPUCLK/3
128bit TeraNet
S
S
S
S
Notes: CPT see physical addresses. In MSMC, one CPT per bank.

## Slide 7: Memory Translation
All address buses inside CorePac and the Teranet are 32 bit wide
Devices support up to 8GB external memory, requires at least 33 bits (in addition to 2GB of internal memory space)
The solution – translation from logical (32 bit) to physical (36 bit) address. This is done by the Memory Protection and extension/translation unit

## Slide 8: A page from the 6678 memory map Translation memory
**The external memory physical address limit is up to 9 ffff ffff

## Slide 9: MPAX Registers in keyStone devices CorePac
Each C66x Core has a set of 16 MPAX 64-bit registers that are used for direct access to the MSMC
Each 64-bit register translates a logical segment into physical segment, from 32 bits to 36 bits
In addition, the MPAX registers control the access permissions for the memory segment

## Slide 10: Structure of the MPAX registers (from the CorePac User Guide)
Segment size can be between 4KB to 4GB (power of 2)
Permissions are for user mode (read, write, execute) and for supervisor mode (read, write, execute)
(Mode is assigned by the operating system, default is supervisor)

## Slide 11: The MPAX Address configuration
Each register translates logical memory into physical memory for the segment.
  Logical base address (up to 20 bits) is the upper bits of the logical segment base address. The lower N bits are zero where N is determined by the segment size:
    For segment size 4K, N = 12 and the base address uses 20 bits.
    For segment size 8k, N=13 and the base address uses only 19 bits.
    For segment size 1G, N=30 and the base address uses only 2 bits.
  Physical (replacement address) base address (up to 24 bits) is the upper bits of the physical (replacement) segment base address. The lower N bits are zero where N is determined by the segment size:
    For segment size 4K, N = 12 and the base address uses up to 24 bits.
    For segment size 8k, N=13 and the base address uses up to 23 bits.
    For segment size 1G, N=30 and the base address uses up to 6 bits.

## Slide 12: MPAX: Typical Use Cases
Speeds up processing by making shared L2 MSMC cached by private L2 (L3 shared).
Uses the same logical address in all cores; Each one points to a different physical memory.
Uses part of shared L2 to communicate between cores. So makes part of shared L2 non-cacheable, but leaves the rest of shared L2 cacheable.
Utilizes 8G of external memory; 2G for each core with some over-lapping.

## Slide 13: CorePac MPAX Reset Values
The XMC configures MPAX segments 0 and 1 so that C66x CorePac can access system memory
Segment 0 power up configure it to address all internal memories (up to address 0x7fff ffff) to the same memory
The power up configuration is that segment 1 remaps 8000_0000 – FFFF_FFFF in C66x CorePac’s address space to 8:0000_0000 – 8:7FFF_FFFF in the system address map
This corresponds to the first 2GB of address space dedicated to EMIF by the MSMC controller

## Slide 14: The MPAX Registers
MPAX (Memory Protection and Extension) Registers:
Translate between physical and logical address
16 registers (64 bits each) control (up to) 16 memory segments.
Each register translates logical memory into physical memory for the segment.
FFFF_FFFF
8000_0000
7FFF_FFFF
0:8000_0000
0:7FFF_FFFF
1:0000_0000
0:FFFF_FFFF
C66x CorePac
Logical 32-bit Memory Map
System
Physical 36-bit Memory Map
0:0C00_0000
0:0BFF_FFFF
0:0000_0000
F:FFFF_FFFF
8:8000_0000
8:7FFF_FFFF
8:0000_0000
7:FFFF_FFFF
0C00_0000
0BFF_FFFF
0000_0000
Segment 1
Segment 0
MPAX Registers

## Slide 15: The protection Part
What happen if the application tries to access logical memory that the MPAX register does not have?
A fault event will be generated – Software decide what to do

## Slide 16: The MAR Registers
MAR (Memory Attributes) Registers:
256 registers (32 bits each) control 256 memory segments:
  Each segment size is 16MBytes, from logical address 0x0000 0000 to address 0xFFFF FFFF.
  The first 16 registers are read only. They control the internal memory of the core.
Each register controls the cacheability of the segment (bit 0) and the prefetchability (bit 3). All other bits are reserved and set to 0.

## Slide 17: Teranet and CorePac Access MSMC
CorePac
2
Shared RAM
2048 KB
CorePac
Slave Port
CorePac
Slave Port
System
Slave Port
for Shared SRAM
(SMS)
System Slave Port for External Memory
(SES)
MSMC System
Master Port
MSMC EMIF
Master Port
MSMC Datapath
Arbitration
256
256
256
Memory
Protection &
Extension
Unit
(MPAX)
256
256
Events
Memory
Protection &
Extension
Unit
(MPAX)
MSMC Core
To SCR_2_B
and the DDR
TeraNet
TeraNet
256
Error Detection & Correction (EDC)
256
256
256
CorePac
Slave Port
CorePac
Slave Port
256
256
XMC
MPAX
CorePac
3
XMC
MPAX
CorePac
0
XMC
MPAX
CorePac
1
XMC
MPAX

## Slide 18: A note about Privilege ID in keyStone devices
Each C66x Core is assigned a unique privilege ID (PrivID) value
Data I/O masters are assigned one PrivID, with the exception of the EDMA, which inherits the PrivID value of the master that configures it for each transfer.
There are 16 total PrivID values supported in KeyStone devices.

## Slide 19: Privilege ID Settings

## Slide 20: Access the MSMC from the Teranet (MSMC slave ports)
SES (slave port External Memory) access addresses 0x8000 0000 to address 0xffff ffff
SMS (slave port Shared SRAM) access addresses 0x0c000 0000 to 0x7fff ffff
For access via the TeraNet, there are 16 sets of MPAX registers for System Slave Memory port and 16 sets of MPAX register for System Slave External port. Each set has 8 registers (8 for SES set and 8 for SMS set)
Each one set of the 16 sets corresponds to a different Privilege ID .

## Slide 21: SES and SMS PMAX Reset Values
At reset, the MPAX segment 0 register pair has initial values that set up unrestricted access to the full MSMC SRAM address space and 2 GB of the EMIF address space.
All other segments come up with the permission bits and size set to 0
For each PrivID, SMS_MPAXH[0] is reset to 0x0C000017 and SMS_MPAXL[0] is reset to 0x00C000BF, (i.e., segment 0 is sized to 16 MB and matches any accesses to the address range 0x0CXXXXXX).
For each PrivID, SES_MPAXH[0] is reset to 0x8000001E and SES_MPAXL[0] is reset to 0x800000BF, (i.e., the segment 0 is sized to 2 GB and matches any accesses to the address range 0x8XXXXXXX). This 2 GB space starts at the external memory base address of 0x80000000.
SMS_MPAXH and SMS_MPAXL for segments 1 through 7 come out of reset as 0x0C000000 and 0x00C00000 respectively. SES_MPAXH and SES_MPAXL for segments 1 through 7 come out of reset as all zeros.

## Slide 22: Configure the MPAX registers – actual code
// Map 1 MB from 0x8810_0000 to 0x0_0C00_0000 (XMC)
// Use segment 3 – can use any segment
lvMpaxh.segSize = 0x13; // 1 MB see table 7-4
lvMpaxh.bAddr = 0x88100; // 32-bit address >> 12
CSL_XMC_setXMPAXH(3,&lvMpaxh);
lvMpaxl.ux = 1;
lvMpaxl.uw = 1;
lvMpaxl.ur = 1;
lvMpaxl.sx = 1;
lvMpaxl.sw = 1;
lvMpaxl.sr = 1;
lvMpaxl.rAddr = 0x00C000; // 36-bit address >> 12
CSL_XMC_setXMPAXL(3,&lvMpaxl);
FFFF_FFFF
881F_FFFF
8810_0000
0:8000_0000
0:7FFF_FFFF
1:0000_0000
0:FFFF_FFFF
C66x CorePac
Logical 32-bit Memory Map
System
Physical 36-bit Memory Map
0:0C00_0000
0:0BFF_FFFF
0:0000_0000
F:FFFF_FFFF
8:8000_0000
8:7FFF_FFFF
8:0000_0000
7:FFFF_FFFF
0C00_0000
0BFF_FFFF
0000_0000
Segment 1
Segment 0
MPAX Registers
0:0C10_0000

## Slide 23: Configure the MPAX registers – actual code
// Map 4 KB from 0x2100_0000 to 0x1_0000_0000 (XMC)
// Use segment 2 or any other segment
lvMpaxh.segSize = 0xB; // 4 KB – see table 7-4 of CorePac
lvMpaxh.bAddr = 0x21000; // 32-bit address >> 12
CSL_XMC_setXMPAXH(2,&lvMpaxh);
lvMpaxl.ux = 1;
lvMpaxl.uw = 1;
lvMpaxl.ur = 1;
lvMpaxl.sx = 1;
lvMpaxl.sw = 1;
lvMpaxl.sr = 1;
lvMpaxl.rAddr = 0x100000; // 36-bit address >> 12
CSL_XMC_setXMPAXL(2,&lvMpaxl);

## Slide 24: Configure MPAX registers for 1GB for each core
// Map 1 GB from 0x8000_0000 to 8 different addresses in the external memory
// The purpose is to give each core different physical address but have the same logical address
lvSesMpaxh.segSz = 0x1D; // 1GB
lvSesMpaxh.baddr = 0x2; // 0x8000 0000 32-bit address >> 30
CSL_MSMC_setSESMPAXH(10,2,&lvSesMpaxh);
// For each core chose a different setting, start at core 0
lvSesMpaxl.raddr = 0x20; // 8 0000 0000 36-bit >> 30 core 0
lvSesMpaxl.raddr = 0x21; // 8 4000 0000 36-bit >> 30 core 1
lvSesMpaxl.raddr = 0x22; // 8 8000 0000 36-bit >> 30 core 2
lvSesMpaxl.raddr = 0x23; // 8 C000 0000 36-bit >> 30 core 3
…
lvSesMpaxl.raddr = 0x27; // 9 C000 0000 36-bit >> 30 core 7
CSL_MSMC_setSESMPAXL(10,2,&lvSesMpaxl);

## Slide 25: Configure the SES MPAX registers for Non cached 1M of MSMC shared memory– actual code
// Map 1 MB from 0x8800_0000 to 0x0_0C10_0000 (MSMC)
// The purpose is to reach MSMC that is not cacheable or pre-fetch
//See MAR registers later
lvSesMpaxh.segSz = 0x13;
lvSesMpaxh.baddr = 0x88100; // 32-bit address >> 12
CSL_MSMC_setSESMPAXH(10,2,&lvSesMpaxh);
lvSesMpaxl.ux = 1;
lvSesMpaxl.uw = 1;
lvSesMpaxl.ur = 1;
lvSesMpaxl.sx = 1;
lvSesMpaxl.sw = 1;
lvSesMpaxl.sr = 1;
lvSesMpaxl.raddr = 0x00C000; // 36-bit address >> 12
CSL_MSMC_setSESMPAXL(10,2,&lvSesMpaxl);

## Slide 26: Configure the MAR registers – actual code
lvMarPtr = (volatile uint32_t*)0x018480030; // MAR12 (0x0C00_0000:0x0CFF_FFFF)
// Set MAR attributes for MAR12
lvMar = 1;
#ifdef MY_ENABLE_PREFETCH
lvMar = lvMar | 8;
#endif
*lvMarPtr = lvMar;

## Slide 27: Configure the MAR registers – actual code
// Set MAR attributes for MAR136:MAR143 (0x8800_0000:0x8FFF_FFFF)
//This is the region that
for (i=0; i<8; i++)
{
lvMar = 0;
*lvMarPtr = lvMar;
lvMarPtr++;
//CACHE_disableCaching(136+i);
}

## Slide 28: Memory Read Performance - Summary
Prefetching reduces the latency gap between local memory and shared (internal/external) memories.
  Prefetching in XMC helps reducing stall cycles for read accesses to MSMC and DDR.
Improved pipeline between DMC/PMC and UMC significantly reduces stall cycles for L1D/L1P cache misses.
Performance hit when both L1 and L2 caches contain victims
  Shared memory (MSMC or DDR) configured as Level 3 (SL3) have a potential “double victim” performance impact
When victims are in the cache, burst reads are slower than single reads
  Reads have to wait for victim writes to complete
MSMC configured as Level 3 (SL3) is slower than Level 2 (SL2)
  There is a “double victim” impact
DDR configured as Level 3 (SL3) is slower than Level 2 (SL2) in case of L2 cache misses
  There is a “double victim” impact
  If DDR does not have large cacheable data, it can be configured as Level 2 (SL2).

## Slide 29: Discussion and Questions