## Slide 1: More About Cache

## Slide 2: XMC – External Memory Controller
The XMC is responsible for the following:
Address extension/translation
Memory protection for addresses outside C66x
Shared memory access path
Cache and pre-fetch support
User Control of XMC:
MPAX (Memory Protection and Extension) Registers
MAR (Memory Attributes) Registers
Each core has its own set of MPAX and MAR registers!

## Slide 3: The MPAX Registers
MPAX (Memory Protection and Extension) Registers:
Translate between physical and logical address
16 registers (64 bits each) control (up to) 16 memory segments.
Each register translates logical memory into physical memory for the segment.
FFFF_FFFF
8000_0000
7FFF_FFFF
0:8000_0000
0:7FFF_FFFF
1:0000_0000
0:FFFF_FFFF
C66x CorePac
Logical 32-bit Memory Map
System
Physical 36-bit Memory Map
0:0C00_0000
0:0BFF_FFFF
0:0000_0000
F:FFFF_FFFF
8:8000_0000
8:7FFF_FFFF
8:0000_0000
7:FFFF_FFFF
0C00_0000
0BFF_FFFF
0000_0000
Segment 1
Segment 0
MPAX Registers

## Slide 4: The MAR Registers
MAR (Memory Attributes) Registers:
256 registers (32 bits each) control 256 memory segments:
  Each segment size is 16MBytes, from logical address 0x0000 0000 to address 0xFFFF FFFF.
  The first 16 registers are read only. They control the internal memory of the core.
Each register controls the cacheability of the segment (bit 0) and the prefetchability (bit 3). All other bits are reserved and set to 0.
All MAR bits are set to zero after reset.

## Slide 5: XMC: Typical Use Cases
Speeds up processing by making shared L2 cached by private L2 (L3 shared)
Uses the same logical address in all cores; Each one points to a different physical memory
Uses part of shared L2 to communicate between cores. So makes part of shared L2 non-cacheable, but leaves the rest of shared L2 cacheable
Utilizes 8G of external memory; 2G for each core

## Slide 6: Cache Sizes and More
Cache | Maximum Size | Line Size | Ways
L1p | 32K Bytes | 32Bytes | One
L1D | 32K Bytes | 64Bytes | Two
L2 | 512K Bytes | 128Bytes | Four

## Slide 7: Memory Read Performance
 |  |  |  |  | CPU stalls |  |  | 
 |  |  |  |  | Single Read |  | Burst Read | 
 | Source | L1 cache | L2 cache | Prefetch | No victim | Victim | No victim | Victim
 | ALL | Hit | NA | NA | 0 | NA | 0 | NA
 | Local L2 RAM | Miss | NA | NA | 7 | 7 | 3.5 | 10
 | MSMC RAM (SL2) | Miss | NA | Hit | 7.5 | 7.5 | 7.4 | 11
 | MSMC RAM (SL2) | Miss | NA | Miss | 19.8 | 20.1 | 9.5 | 11.6
 | MSMC RAM (SL3) | Miss | Hit | NA | 9 | 9 | 4.5 | 4.5
 | MSMC RAM (SL3) | Miss | Miss | Hit | 10.6 | 15.6 | 9.7 | 129.6
 | MSMC RAM (SL3) | Miss | Miss | Miss | 22 | 28.1 | 11 | 129.7
 | DDR RAM (SL2) | Miss | NA | Hit | 9 | 9 | 23.2 | 59.8
 | DDR RAM (SL2) | Miss | NA | Miss | 84 | 113.6 | 41.5 | 113
 | DDR RAM (SL3) | Miss | Hit | NA | 9 | 9 | 4.5 | 4.5
 | DDR RAM (SL3) | Miss | Miss | Hit | 12.3 | 59.8 | 30.7 | 287
 | DDR RAM (SL3) | Miss | Miss | Miss | 89 | 123.8 | 43.2 | 183
SL2 – Configured as Shared Level 2 Memory (L1 cache enabled, L2 cache disabled)
SL3 – Configured as Shared Level 3 Memory (Both L1 cache and L2 cache enabled)

## Slide 8: Memory Read Performance - Summary
Prefetching reduces the latency gap between local memory and shared (internal/external) memories.
  Prefetching in XMC helps reducing stall cycles for read accesses to MSMC and DDR.
Improved pipeline between DMC/PMC and UMC significantly reduces stall cycles for L1D/L1P cache misses.
Performance hit when both L1 and L2 caches contain victims
  Shared memory (MSMC or DDR) configured as Level 3 (SL3) have a potential “double victim” performance impact
When victims are in the cache, burst reads are slower than single reads
  Reads have to wait for victim writes to complete
MSMC configured as Level 3 (SL3) is slower than Level 2 (SL2)
  There is a “double victim” impact
DDR configured as Level 3 (SL3) is slower than Level 2 (SL2) in case of L2 cache misses
  There is a “double victim” impact
  If DDR does not have large cacheable data, it can be configured as Level 2 (SL2).

## Slide 9: Memory Write Performance
 |  |  |  |  | CPU stalls |  |  | 
 |  |  |  |  | Single Write |  | Burst Write | 
 | Source | L1 cache | L2 cache | Prefetch | No victim | Victim | No victim | Victim
 | ALL | Hit | NA | NA | 0 | NA | 0 | NA
 | Local L2 RAM | Miss | NA | NA | 0 | 0 | 1 | 1
 | MSMC RAM (SL2) | Miss | NA | Hit | 0 | 0 | 2 | 2
 | MSMC RAM (SL2) | Miss | NA | Miss | 0 | 0 | 2 | 2
 | MSMC RAM (SL3) | Miss | Hit | NA | 0 | 0 | 3 | 3
 | MSMC RAM (SL3) | Miss | Miss | Hit | 0 | 0 | 6.7 | 14.6
 | MSMC RAM (SL3) | Miss | Miss | Miss | 0 | 0 | 6.7 | 16.7
 | DDR RAM (SL2) | Miss | NA | Hit | 0 | 0 | 4.7 | 4.7
 | DDR RAM (SL2) | Miss | NA | Miss | 0 | 0 | 5 | 5
 | DDR RAM (SL3) | Miss | Hit | NA | 0 | 0 | 3 | 3
 | DDR RAM (SL3) | Miss | Miss | Hit | 0 | 0 | 16 | 114.3
 | DDR RAM (SL3) | Miss | Miss | Miss | 0 | 0 | 18.2 | 115.5
SL2 – Configured as Shared Level 2 Memory (L1 cache enabled, L2 cache disabled)
SL3 – Configured as Shared Level 3 Memory (Both L1 cache and L2 cache enabled)

## Slide 10: Memory Write Performance - Summary
Improved write merging and optimized burst sizes reduce the stalls from/to external memory.
  DMC merges writes to any (not only L2 RAM) address that is allowed to be cached (MAR.PC==1).
One to four word writes do not have latency due to write merging.
MSMC prefetch does not have too much write performance impact.
Writes do not have major “double victim” performance impact.

## Slide 11: Cache Coherency

## Slide 12: A Coherency Issue
CPU
L2
RcvBuf
L1D
RcvBuf
RcvBuf
XmtBuf
XmtBuf
CorePac2
CorePac2
Another CorePac reads the buffer from shared memory.
The buffer resides in cache, not in external memory.
So the other CorePac reads whatever is in external memory; probably not what you wanted.
There are two solutions to data coherency ...
Shared (DDR3/ Shared Local)
CorePac1

## Slide 13: Solution 1: Flush & Clear the Cache
CPU
L2
L1D
RcvBuf
XmtBuf
RcvBuf
RcvBuf
XmtBuf
When the CPU is finished with the data (and has written it to XmtBuf in L2), it can be sent to external memory with a cache writeback.
A writeback is a copy operation from cache to memory, writing back the modified (i.e. dirty) memory locations – all writebacks operate on full cache lines.
Use CSL CACHE_wbL1d to force a writeback.
No writeback is required if the buffer is never read (L1 cache is read allocate only).
writeback
Core2
Core2
Shared (DDR3/SL)
CorePac1

## Slide 14: Another Coherency Issue
CPU
L2
Shared (DDR3/SL)
L1D
RcvBuf
XmtBuf
RcvBuf
RcvBuf
XmtBuf
CorePac2
Another CorePac writes a new RcvBuf buffer to shared memory
When the current CorePac reads RcvBuf a cache hit occurs since the buffer (with old data) is still valid in cache
Thus, the current CorePac reads the old data instead of the new data
CorePac1

## Slide 15: Another Coherency Solution (Using CSL)
CPU
L2
L1D
RcvBuf
XmtBuf
RcvBuf
RcvBuf
XmtBuf
To get the new data, you must first invalidate the old data before trying to read the new data (clears cache line’s valid bits)
CSL provides an API to writeback with invalidate:
  It writes back modified (i.e. dirty) data,
  Then invalidates cache lines containing the buffer CACHE_wbInvL2((void *)RcvBuf, bytecount, CACHE_WAIT);
CorePac2
Shared (DDR3/SL)
CorePac1

## Slide 16: Solution 2: Keep Buffers in L2
CPU
L2
L1D
RcvBuf
RcvBuf
XmtBuf
EDMA
Configure some of L2 as RAM.
Use EDMA or PKTDMA to transfer buffers in this RAM space.
Coherency issues do not exist between L1D and L2.
EDMA
Adding to Cache Coherency...
CorePac1
Shared (DDR3/MSMC)

## Slide 17: Prefetching Coherency Issue
CPU
L2
Shared (DDR3/SL)
L1D
Buf
Buf
Buf
The Expanded Memory Controller (XMC) contains a pre-fetch buffer(s), controlled by a bit in MAR, used for data reading speed-up
This buffer is not used for writing data
A read/write/read sequence applied to the same buffer can cause the second read operation to read old data
preFetch
write
read
CorePac1

## Slide 18: Coherence Summary (1)
Internal (L1/L2) Cache Coherency is Maintained
Coherence between L1D and L2 is maintained by cache controller.
No CACHE operations needed for data stored in L1D or L2 RAM.
L2 coherence operations implicitly operate upon L1 as well.
Simple Rules for Error Free Cache
Before the DSP begins reading a shared external INPUT buffer, it should first BLOCK INVALIDATE the buffer.
After the DSP finishes writing to a shared external OUTPUT buffer, it should initiate an L2 BLOCK WRITEBACK.

## Slide 19: Coherence Summary (2)
There is no hardware cache coherency maintenance between the following:
  L1/L2 caches in CorePacs and MSMC memory
  XMC prefetch buffers and MSMC memory
  CorePac to CorePac via MSMC
EDMA/PKTDMA transfers between L1/L2 and MSMC are coherent.
Methods for maintaining coherency:
  Write back after writing and cache invalidate before reading.
  Use EDMA/PktDMA for L2MSMC, MSMCL2 or L2L2 transfers.
  Use MPAX registers to alias shared memory and use MAR register to disable shared memory caching for the aliased space.
  Disable the MSMC prefetching feature.

## Slide 20: Message Passing Example
Slave (Core0) passes a message to Master (Core1)
L1D cache only
Core 0 Code:
  #include <ti/csl/csl_cacheAux.h>
  // align and place in the shared memory the message buffer
  #pragma DATA_SECTION(slaveToMasterMsg,".msmc")
  #pragma DATA_ALIGN(slaveToMasterMsg,64)
  Int32 volatile slaveToMasterMsg[16];
  // Write the message
  slaveToMasterMsg[2] = slaveMsg;
  // Write-back (no need to wait for completion )
  CACHE_wbL1d((void *)slaveToMasterMsg, 64, CACHE_NOWAIT);
Core 1 Code:
  extern Int32 volatile slaveToMasterMsg[16];
  // Invalidate (wait for completion)
  CACHE_invL1d((void *)slaveToMasterMsg, 64, CACHE_WAIT);
  // Read the message
  slaveMsg = slaveToMasterMsg[2];

## Slide 21: Cache Alignment
False Addresses
False Addresses
Buffer
Buffer
Buffer
Cache Lines
Problem: How can I invalidate (or writeback) just the buffer?
In this case, you can’t
Definition: False Addresses are ‘neighbor’ data in the cache line, but outside the buffer range
Why Bad: Writing data to buffer marks the line ‘dirty’, which will cause entire line to be written to external memory, thus:
External neighbor memory could be overwritten with old data
Avoid “False Address” problems by aligning buffers to cache lines (and filling entire line):
  Align memory to 128-byte boundaries*
  Allocate memory in multiples of 128 bytes
  * If only L1 cache is used, 64-byte alignment is sufficient
#define BUF 128
#pragma DATA_ALIGN (in, BUF)
short in[2][20*BUF];

## Slide 22: "Turn Off" the Cache (MAR)
CPU
L2
External
L1D
RcvBuf
XmtBuf
EDMA
Memory Attribute Registers (MARs) enable/disable caching or pre-fetching for a memory range.
Don’t use MAR to solve basic cache coherency – performance will be too slow.
Use MAR when you have to always read the latest value of a memory location, such as a status register in an FPGA, or switches on a board or shared memory location.
MAR is like “volatile”. You must use both to always read a memory location: MAR for cache; volatile for the compiler.

## Slide 23: Shared Local Memory and MAR
The whole Internal Shared Memory is controlled by only one Memory Attribute Register (MAR).
The internal Shared Memory may need to be split into three regions:
  enabled cache/enabled prefetch (default)
  enabled cache/disabled prefetch
  disabled cache/disabled prefetch
Use MPAX registers to create multiple logical memory ranges for the same physical internal shared memory.
For each logical memory range we can set different MAR attributes.
Care must be taken when defining memory regions in the linker command file, so we do not overlap physical memory regions.