## Slide 1: C66x CorePac Improvements Over C64x+
Wider internal bus
  64 bit for the .L and .S functional units
  128 bit for the .M functional unit
Wider cross path
  64 bit for each direction
4x number of multipliers
  More SIMD instructions
Enhanced instruction set
  More than 100 new instructions added (compared to c64+)

## Slide 2: Enhanced C66x Instruction Set
New SIMD instructions:
  QMPY32 – 4-way SIMD of MYP32
  DDOTP4H – 2-way SIMD of DOTP4H
  DPACKL2 – SIMD version of PACKL2
  DAVGU4 – Average of 8 packed unsigned bytes
New floating-point instructions:
  MPYDP – Double Precision Multiplication
  FMPYDP – Fast Double Precision multiplication
  DINTSP – 2-Way SIMD Convert 32-bits Unsigned Integer to Single Precision Floating Point

## Slide 3: Interesting New C66x Instructions
MFENCE (Memory Fence) Stall instruction pipeline until memory system is done.
RCPSP (Single-Precision Floating-Point Reciprocal Approximation)
RSQRSP (Single-Precision Floating-Point Square-Root Reciprocal Approximation)