## Slide 1: Introduction to KeyStone Software ECO

## Slide 2: Agenda
Characteristics of modern operating system and development environment
TI traditional support for development
  DSP BIOS
  Frameworks, utilities and drivers
  The ECO system
Multicores development support
  MCSDK
  Multicores ECO system

## Slide 3: Think about Your Favorite Operating System
Provide scheduling – multiple thread co-exist
Provide standard API for utilities
  Print
  Networking (sockets)
  Time, and many more
Hides the hardware and driver details from the application
But if you look under the hood:
  There are actual hardware modules and interfaces (the manufacturer)
  A set of LLD to talk to the hardware
  One or more layers of utilities APIs that connect the application to the LLd
And when you develop code:
  IDE
  Libraries

## Slide 4: TI traditional Support
DSP BIOS Real-Time operating system
  Scheduling (Hardware interrupt, SWI, task)
  Memory management
  Communications
  Performances monitoring
Standard API and optimized libraries
Frameworks
  Easy access to peripherals and other resources (dma)
  Hiding hardware implementation from the application (CSL)
IDE
  Code composer studio
  Code generation tools
  Debug, emulation, monitoring, profiling

## Slide 5: KeyStone Architecture Challenges
Even though KeyStone has a lot
  Advanced core performances
  Support multicores architecture
  Multiple internal resources
  Many peripherals and co-processors
The challenge
Make it easy for the programmer to develop optimized application

## Slide 6: Software development Ecosystem

## Slide 7: Improvements to the IDE
Eclipse based CCS 5 supports multiple cores and multiple devices
  Multiple windows
  Open source – third party plug in
  Three run conditions
  Advance debugging, monitoring and profiling
Optimized compiler/optimizer/assembler/linker
openMP support
Multiple configurations for the same project, can generate single executable or multiple executable for the same project
GUI interface for SysBios, project based system to build drivers and utilities for user target system

## Slide 8: Operating System and Utilities
Individual core full services operating system – SysBios
Large set of utilities in framework
Multiple layers of software hide hardware and implementation details from the applications
High layer provides synchronization, message exchange and data sharing between cores
Optimized libraries provide optimized code for a wide range of generic applications
OEM provides priority based multi-core scheduling system