## Slide 1: IPC Using Shared Memory and Navigator
Difference in the cfg file
  Adding QMSS and CPPI packages to config
  Define MessageQ.SetupTransportProxy as QMSS and not as shared memory
  Adding transport QMSS parameters
Difference in the code
  Adding include files for QMSS and CPPI
  Adding QMSS parameters (descriptors, etc.)
  Calling systemInit to configure QMSS and CPPI
  Adding Qmss_device and Cppi_device files (link or copy)

## Slide 2: Adding QMSS and CPPI packages to config
/* QMSS/CPPI memory settings */
/* Load and use the CPPI and QMSS packages */
var Cppi = xdc.loadPackage('ti.drv.cppi');
var Qmss = xdc.loadPackage('ti.drv.qmss');
Program.sectMap[".qmss"] = new Program.SectionSpec();
Program.sectMap[".qmss"] = "MSMCSRAM";
Program.sectMap[".cppi"] = new Program.SectionSpec();
Program.sectMap[".cppi"] = "MSMCSRAM";
Program.sectMap[".desc"] = new Program.SectionSpec();
Program.sectMap[".desc"] = "MSMCSRAM";

## Slide 3: Define MessageQ.SetupTransportProxy as QMSS and not as shared memory (1)
In shared memory we have:
/* Use shared memory IPC */
Notify.SetupProxy = xdc.module('ti.sdo.ipc.family.c647x.NotifyCircSetup'); // Do we really need it?
MessageQ.SetupTransportProxy = xdc.module('ti.sdo.ipc.transports.TransportShmNotifySetup');

## Slide 4: Define MessageQ.SetupTransportProxy as QMSS and not as shared memory (2)
In QMSS we have:
/* use IPC over QMSS */
MessageQ.SetupTransportProxy = xdc.useModule(Settings.getMessageQSetupDelegate());// Do we need it?
var TransportQmssSetup = xdc.useModule('ti.transport.ipc.qmss.transports.TransportQmssSetup');
MessageQ.SetupTransportProxy = TransportQmssSetup;

## Slide 5: Adding transport QMSS parameters
TransportQmssSetup.descMemRegion = 0;
Program.global.descriptorMemRegion = TransportQmssSetup.descMemRegion;
Program.global.numDescriptors = 8192;
Program.global.descriptorSize = cacheLineSize; // multiple of cache line size
TransportQmss.numDescriptors = Program.global.numDescriptors;
TransportQmss.descriptorIsInSharedMem = true;
TransportQmss.descriptorSize = Program.global.descriptorSize;
TransportQmss.useAccumulatorLogic = false;
TransportQmss.pacingEnabled = false;
TransportQmss.intThreshold = 1;
TransportQmss.timerLoadCount = 0; // timer ticks. This value only has effect when the packingEnabled is true.
TransportQmss.accuHiPriListSize = 2100; // this number should be >= twice the threshold+2

## Slide 6: Adding include files for QMSS and CPPI
/* QMSS LLD*/
#include <ti/drv/qmss/qmss_drv.h>
#include <ti/drv/qmss/qmss_firmware.h>
/* CPPI LLD */
#include <ti/drv/cppi/cppi_drv.h>
#include <ti/transport/ipc/examples/common/bench_common.h>
#include <ti/transport/ipc/qmss/transports/TransportQmss.h>
/************************ EXTERN VARIABLES ********************/
/* QMSS device specific configuration */
extern Qmss_GlobalConfigParams qmssGblCfgParams;
/* CPPI device specific configuration */
extern Cppi_GlobalConfigParams cppiGblCfgParams;
/**************************************************************/

## Slide 7: Adding QMSS parameters (descriptors, etc.)
#define NUM_MONOLITHIC_DESC numDescriptors
#define SIZE_MONOLITHIC_DESC descriptorSize
#define MONOLITHIC_DESC_DATA_OFFSET 16
#pragma DATA_SECTION (monolithicDesc, ".desc");
#pragma DATA_ALIGN (monolithicDesc, 16)
UInt8 monolithicDesc[SIZE_MONOLITHIC_DESC * NUM_MONOLITHIC_DESC];

## Slide 8: Calling systemInit to configure QMSS and CPPI
Int32 systemInit (Void)
{
Qmss_InitCfg qmssInitConfig; /* QMSS configuration */
Qmss_MemRegInfo memInfo; /* Memory region configuration information */
Qmss_Result result;
UInt32 coreNum;
And in main:
if (selfId == 0)
{
/* QMSS, and CPPI system wide initializations are run on
* this core */
result = systemInit();
if (result != 0)
{
System_printf("Error (%d) while initializing QMSS\n", result);
}
}

## Slide 9: Adding Qmss_device and Cppi_device files (link or copy)