## Slide 1: PRU in Sitara Device
Programmable Real-Time Unit (PRU) Subsystem
Interconnect
INTC
Peripherals
PRU0 I/O
Inst. RAM
Shared RAM
DataRAM
Inst. RAM
DataRAM
PRU1 I/O
Shared
Memory
Peripherals
Peripherals
GP I/O
L4 Interconnect
ARM Subsystem
Cortex-A8
L1 Instruction Cache
L1 Data Cache
L2 Data Cache
PRU0 (200MHz)
PRU1 (200MHz)
L3 Interconnect
L3 Interconnect
Notes: ARM + PRU + memories + peripherals = SoC
PRU works as a co-processor in system-level implementation, or
- PRU works independently

## Slide 2: PRU – Programmable real-time ICSS – Industrial Communication Sub-system

## Slide 3: PRU features
OCP – open core protocol – master port and slave port
2 PRUs, each had private memory
  8K data
  8K program
In between there Is scratch pad memory SPAD (3 banks, 30 32-bit registers)
Shared memory:
  Shared ram 12k

## Slide 4: PRU features
Interrupt Controller
  64 input events
  10 interrupt channels – hardware priorities
  16 software events can be generated by 2 PRU
Two MII ports, one MDIO port
IEP (Industrial Ethernet peripheral) for harsh conditions (Fiber?)

## Slide 5: PRU features
Enhanced Capture Module n(ECAP)
Memory is parity protected

## Slide 6: PRU-ICSS

## Slide 7: PRU Local memories – Program memory

## Slide 8: PRU Memory Map (local)
Each PRU sees his RAN at 0x000 0000 and the other one at 0x0000 2000

## Slide 9: PRU Memory Map (Global)
This is the host view of the PRU memories

## Slide 10: PRU Attributes