## Slide 1: Agenda
AM437x Silicon Overview
  Processors
  Peripherals
  Buses and Memory
  A little about the system
Software Overview
AM437x EVMs
AM437x Docs and Tools

## Slide 2: AM437X Applications
Patient Monitoring
  Security Applications
Bar Code Scanners
Navigation Equipment
Point of Service
Industrial Automation
Portable Mobile Radio
Portable Data Terminals
Test And Measure
Any other broad market EP applications
Notes: EPOS - Electronic point of sale
SK – Software Kit
IDK – Industrial Development Kit
HS- High Security

## Slide 3: AM437x Cortex™-A9 based processors
Benefits
Performance
  High performance Cortex-A9 up to 1GHz
  display system
  Security Engine
  PRU-ICSS
  Multiple system services
Peripherals and Connectivity
  Variety of peripherals
  Multiple high bit rate interfaces for data IO
  Multiple interfaces for boot and control/monitor
Power Targets
  Total Power: <1000mW
  Deep sleep: ~4mW
  RTC-only mode: <0.03mW
Software and development tools
  Free Linux SDK directly from TI
  RTOS (QNX, Nucleus, Green Hills, etc) from partners
  Full featured and low cost development board options (EVM, SK, IDK)
Schedule and packaging
Samples and Dev. Tools: 2Q 2014
Production: 4Q 2014
Package: 17x17mm, 0.65 VCA, 0.8mm-pitch effective routing
Graphics Acceleration
SGX530
Display
Subsystem
24bit LCD
Debug
WDT
RTC
EDMA
System Services
12 Timers
2 12-bit ADCs(1)
Simple Pwr Seq
SyncTimer32K
Connectivity and IOs
PWM x6
NAND
/NOR (16bit ECC)
3 MMC/ SD/SDIO
CAN x2
USB2 OTG +PHY x2
eCAP/
eQEP x3
EMAC
2-port switch 10/100/1G w/1588
HDQ
QSPI
Touch Screen Controller(1)
Processing
Overlay, Resizing, Color Space Conversion, etc.
Camera I/F (2x Parallel)
McASP x2
GPIO
UART x6
SPI x5
I2C x3
Security AccelerationPac
Crypto, Secure boot
256KB L3 Shared RAM
32-bit LPDDR2/DDR3/DDR3L(2)
PRU
Industrial
Communication Subsystem EtherCAT®,PROFINET®, EtherNET/IP™ + Motor Feedback
Protocols +
Sigma Delta
32K/32K L1
256K L2 / L3
64K RAM
ARM®
Cortex A9
Up to 1 GHz

## Slide 4: AM437x Silicon Overview Processors and Co-processors
Notes:   SGX530 – graphics Accelerator - features pixel, vertex, and geometry shader hardware, supporting OpenGL ES - 7M Triangles and 200M Pixels 1.6GFLOPS
OpenGL for Embedded Systems (OpenGL ES or GLES) is a subset of the OpenGL computer graphics rendering application programming interface (API) for rendering 2D and 3D computer graphics such as those used by video games, typically hardware-accelerated using a graphics processing unit (GPU).
Crypto

## Slide 5: Cortex-A9 (AM437x) vs Cortex-A8 (AM335x)
VFP Fully Pipelined ~10x floating point speed up
Out of order processing and other performance improvements giving 2.5 DMIPS/MHz (~16% in actual tests
External PL310 cache controller
L2 Cache can be used as generic SRAM (SRAM or Cache - no mixing)
Interrupts (more interrupts, 224)
  Generic Interrupt Controller
  Wakeup Gen
local counter, watchdog timer
Up to 1GHz MPU clock

## Slide 6: Cortex A-19 Features
Superscalar architecture:
  2 ALU, 2 shifts, branch unit, multiply and divide, load store
  2 concurrent decoded
Full implementation of ARMv7-A architecture instruction set:
  More MAC instructions (normalization and rounding)
  Integer divide
Pipeline optimization:
  Speculating dynamic pipeline, 8-11 stages to issue
  Out-of-order pipeline (8-11 stages) execution
Notes: 8 issues:
2 for Neon- VFP
2 for load and store
4 for the other (ALU, Shift, multiply)

## Slide 7: Cortex A-9 Features
Dynamic branch prediction – Loop prediction and indirect branch predictor
  Branch Target Address cache (BTAC)
  Global History Buffer (GHB) has three arrays:
    Taken array
    Not taken array
    Selector array
  Return Stack

## Slide 8: SIMD Engine NEON
64/128-bit data instructions
Fully integrated into the main pipeline
32x 64-bit registers that can be arranged as 128-bit registers
Data can be interpreted as follows:
  Byte
  Half-word (16-bit)
  Word
  Long

## Slide 9: NEON Registers
NEON registers load and store data into 64-bit registers from memory with on-the-fly interleave, as shown in this diagram.
Source: ARM Compiler Toolchain Assembler Reference; DUI0489C

## Slide 10: Vector Floating Point (VFP)
Fully integrated into the main pipeline
32 DP registers for FP operations
Native (hardware) support for all IEEE-defined floating-point operations and rounding modes; Single- and double-precision
Supports fused MAC operation (e.g., rounding after the addition or after the multiplication)
Supports half-precision (IEEE754-2008); 1-bit sign, 5-bit exponent, 10-bit mantissa

## Slide 11: Memory Management Unit (MMU)
Logical-to-physical memory translation:
  User protected
  Hardware manages the actual memory
Page size – 16MB to 4KB
CorePac
MMU
TLB
Memory
…
Page 1
Page 2
Page 3
Page 4
Page 5
Logical
Address
Physical
Address
Notes: The translation between virtual address to physical address is done via two or three steps
32 L1 Instructions
2 by 32 data L1
4 ways 512-entry L2 TLB (for each processor)

## Slide 12: Programmable Real-Time Unit (PRU) Subsystem
Programmable Real-Time Unit (PRU) is a low-latency microcontroller subsystem
Two independent PRU execution units
  32-Bit RISC architecture
  200MHz – 5ns per instruction
  Single cycle execution - No pipeline
  Dedicated instruction and data RAM per core
  Shared RAM
Includes Interrupt Controller for system event handling
Fast I/O interface
  Up to 30 inputs and 32 outputs on external pins per PRU unit
Master I/F (to SoC interconnect)
Slave I/F (from SoC interconnect)
AM335x PRU Subsystem Block Diagram
32 GPO
30 GPI
Events to ARM INTC
Events from Peripherals + PRUs
32 GPO
30 GPI
Scratchpad
Interrupt Controller (INTC)
PRU1 Core
(8KB IRAM)
PRU0 Core
(8KB IRAM)
DRAM0
(8K Bytes)
DRAM1
(8K Bytes)
shared
(12K Bytes)
MII1 RX/TX
MII0 RX/TX
32-bit Interconnect bus
IEP (Timer)
eCAP
MPY/MAC
UART
Industrial Ethernet
Industrial Ethernet
MDIO
Notes: Notes:
  AM335x:
  - 8K Byte instruction RAM (2K instructions) per core
  - 8K Bytes data RAM per core
  - 12K Bytes shared RAM
Although PRU can only run from IRAM, it can be reset and new code can be loaded. This allows you to use the PRU for multiple functions.
Each PRU has a total of 32 output pins and 30 input pins. Pins are multiplexed with other peripherals at the system level so there are pin muxing considerations to be kept in mind.
Main point:
The PRU subsystem has key features and dedicated resources that help solve real-time problems.
Key features:
2 PRU cores – each with dedicated instruction RAM
- RISC processors

## Slide 13: Display Subsystem (DSS)
Getting input data from frame buffer, sending output image or video to external display
Notes: VENC -

## Slide 14: Display Subsystem (DSS)
Display Subsystem
Up to 100MHz pixel clock
Up to 2048x2048 resolution, highly dependent on frame rate, bpp, etc.
Display Controller :
Input modes :
  Programmable pixel display modes (1, 2, 4, 8, 12, 16, 18 and 24 bit-per-pixel modes, YUV and 24 bits RGB)
  256 x 24-bit entry palette in RGB
Display support :
  Passive & Active Matrix panel.
  Remote Frame Buffer support through the RFBI module.
Signal processing :
  Overlay support for Graphics,Video1 and Video2
  Video resizer : upsampling (up to x8) downsampling (down to 1/4)
  Transparency color key (source and destination)
  Programmable video color space conversion YcbCr 4:2:2 into RGB
  Gamma curve support
  Programmable Color Phase Rotation (CPR)
Notes: VENC - Composite Video, S-Video
Passive active Matrix Panel – supply the voltage to the LCD
Transparency color key - mixing multiple colors
  Gamma curve support - compensate for the way the eye sees things
  Programmable Color Phase Rotation – changing the phase of presentation of color (2 values, radius and phase)

## Slide 15: Graphic Accelerator SGX530 (Imagination Technologies)
2D and 3D graphics
Tile-based architecture
Universal scalable shader engine (USSE™) – multithreaded engine incorporating pixel and vertex shader functionality
Industry-standard API support: OpenGL ES 1.1 and 2.0, OpenVG v1.0.1
Advanced geometry direct memory access (DMA)
Programmable high-quality image anti-aliasing

## Slide 16: Crypto Hardware Accelerator
offload cryptographic processing from the ARM core
OpenSSL
Crypto
Secure Boot
Notes: OpenSSL is an open-source implementation of the SSL and TLS protocols.
The core library, written in the C programming language, implements basic cryptographic functions and provides various utility functions.

## Slide 17: AM437x Silicon Overview Peripherals

## Slide 18: Camera Subsystem (2x)
Dual Port 8/10bit BT656 interface
Single port 12-bit interface
YUV422/RGB422, BT656, RAW input formats
Up to 75MHz input pixel clock
Bar code scanner
PREVIEW
Parallel camera
C C D C
MMU
REGISTERS
VPFE
processing sub module
L3
L4
Timing control
Camera clock
and
synchronization signal
Notes: VPFE – Video Port Front End
BT 656 – digital video Protocol for streaming uncompressed PAL or NTSC
CCD – Charged Couple device (digital camera)
CCDC – Charge Couple device controller
75MHZ input pixel clock (2Kx1Kx30fps)

## Slide 19: Camera Subsystem
Notes: VPFE – Video Port Front End
BT 656 – digital video Protocol for streaming uncompressed PAL or NTSC
CCD – Charged Couple device (digital camera)
CCDC – Charge Couple device controller
For 16 bits interface, two VPFE are connected together
Row data - color filter array (CFA or RGB color space Foveon X3 sensors

## Slide 20: EMAC – Ethernet Media Access Controller switch
Two 10/100/1000Mb external ports, 3 port Ethernet switch
Supports standard Media Independent Interface (MII), Reduced Media Independent Interface (RMII), Gig Reduced Media Independent Interface (RGMII) to physical layer device (PHY)
Layer 2 switch (1024 addresses LUT)
Includes MDIO interface to control/communicate with PHY
Reset Isolation
EXTDEV PLL to provide clock to external PHY
AM437x
Port1
Port0
Port2
Dual MAC mode
AM437x
Port1
Port0
Port2
Switch mode
New feature vs. AM335x
Notes: (Ipv4, Ipv6, 802.3x) - software support
MDIO – Management Data Input-Output serial link to talk to the physical front end

## Slide 21
Added capability to derive REFCLK for Ethernet PHY from AM437x
  Added Low Jitter EXTDEV PLL
  Saves cost of external crystal or oscillator for PHY
    25MHz REFCLK for other PHYs
    50MHz REFCLK for RMII PHY clock (default for ROM for boot)
Separated voltage domains of MDIO clk/data and Ethernet I/F in all I/O sets
  Compliant to IEEE Ethernet Vmin=2.0V spec
Expanded pinmux options
  NAND + Dual Ethernet supported
IEEE1588 TimeStamp
  Provides accurate time based control over Ethernet
  Ability to provide separate PLL (reusing Display PLL) with Fractional M multiplier for time stamping
  IPV6 time stamping. Now supporting Annex D, E , F
Added support for Ethernet operation in CORE OPP50
Internal TX Delay mode supported by default to enable RGMII boot
AM437x
CLKOUTx
Ethernet
PHY
Ethernet: changes from AM335x
New feature vs. AM335x

## Slide 22: USB 2.0 – Universal Serial Bus
Benefit: 2x xHCI DRD (dual role device) USB controllers with embedded DMA and integrated PHYs provide a mechanism that complies with the USB2.0 standard for data transfer between USB devices up to 480 Mbps. Its dual-role feature allows the capability to operate as a host or peripheral.
2 ports (USB0 and USB1)
Both ports bootable
  USB0 as peripheral,
  USB1 as host. Can boot off of a MSD (ie, flash drive)
  Swappable DP/DM to facilitate clock routing
AM335x
Mentor OTG controller
AM437x
xHCI controller
New generation xHCI provides industry standard register definition for USB host controllers supported by open-source drivers
AM437x adds capabilities to xHCI for peripheral mode
New feature vs. AM335x
20+% performance improvement
Notes: eXtensible Host Controller Interface (xHCI) is a computer interface specification
DM/DP differential physical interface, data plus data minus
Super Speed – 5G not supported
Internal DMA controller
– Descriptor caching and data pre-fetching ensures high performance
– Dynamic FIFO memory allocation for all endpoints
OCP – open Core Protocol

## Slide 23: USB 2.0 – Universal Serial Bus
Operating as a host, it compiles with USB2.0 standard for high-speed, full-speed and low-speed operation with a peripheral
Operating as a peripheral, it compiles with USB2.0 standard for high-speed and full-speed operation with a host
SuperSpeed is not supported! (Did not integrate SuperSpeed PHY)
Supports all modes of transfers (control, bulk, interrupt, and isochronous)
Supports 15 simultaneous Transmit (TX) and 15 Receive (RX) endpoints, in addition to endpoint 0
All new devices (Keystone, Vayu, etc.) going forward will be using xHCI controller (driver compatibility)
Notes: eXtensible Host Controller Interface (xHCI) is a computer interface specification
DM/DP differential physical interface, data plus data minus
Super Speed – 5G not supported
Internal DMA controller
– Descriptor caching and data pre-fetching ensures high performance
– Dynamic FIFO memory allocation for all endpoints
OCP – open Core Protocol )additional P – Presence - assertions and constraints
UTMI, USB 2.0 Transceiver Macrocell Interface

## Slide 24: External memory interfaces
Features of the MMC/SD include support for:
  3 MMC/SD ports
  Multimedia card (MMC v4.3/ SD 2.0 ), supports >2GB capacity on eMMC boot on MMC0
  Card detect and write protect on each MMCSD port
  48 MHz maximum I/O clock rate (up to SDR25 speeds)
Features of the GPMC include:
  8-bit and 16-bit wide data bus
  Programmable cycle timings for each chip select
  Up to 16-bit ECC support for NAND Flash using BCH code (t=4, 8 or 16) or Hamming code for 8-bit or 16-bit NAND-flash
  Integrated ELM (Error Locator Module) to provide ECC calculation (up to 16b) for NAND support. Supports 4-bit, 8-bit and 16-bit per 512byte block error location based on BCH algorithms
  used to connect NAND, NOR (async and sync), FPGAs, etc
Features of the QSPI:
Supports up to 4bit read, 1bit write
Up to 48MHz clock, Master only
Supports eXecute-In-Place (XIP) from serial NOR flash
Primarily intended for fast boot from quad-SPI flash devices
New feature vs. AM335x

## Slide 25: AM437x has numerous serial peripherals…
12 GP Timers & 1 watchdog timer
  Free-running 32-bit upward counter. Runs off 32KHz or 19.2, 24, 25, 26 MHz system clock.
  WDT: MPU Watchdog (runs off of 32KHz system clock)
1 Sync Timer (32KHz)
  Special always on 32K timer for OS
I2C (3)
  3 I2C ports compliant with Philips I2C specification version 2.1
  Support for standard (up to 100K bits/s) and fast (up to 400K bits/s) modes
General-Purpose I/O (GPIO) Interface (6 banks, each 32 GPIO)
  Synchronous interrupt requests in active mode from each channel are processed by GIC (General Interrupt Controller) in MPUSS.
  Asynchronous wake-up request
  192 total GPIOs muxed with other signals
Multichannel Audio Serial Port Interface (2)
  Data Clock 50 MHz ,
  Two Clock Zones and up to 4 Serial Data Pins per McASP port
  Supports TDM, I2S and Similar Formats
  Supports DIT mode
  48K, 96K and 192K sample rate, 8 to 32 bits per sample, 384 time slots
Universal Asynchronous Receiver Transmitters (UART) (6)
  UART1 will support full Modem Control (CTS,RTS,DTR, DSR, DCD, RIN)
  All UARTs support IrDA, CIR and RTS, CTS flow control.
  Supports baud rate up-to 3.6M bits/s.
New feature vs. AM335x
Notes: WDT – Watchdog Timer
MPU – Microprocessor Unit
McASP - general-purpose audio serial port optimized for the needs of multichannel audio applications. The McASP is useful for time-division multiplexed (TDM) stream, Inter-Integrated Sound (I2S) protocols, and intercomponent digital audio interface transmission (DIT). 384 time slots, each 8,12,16,20,24,28,32 bit, 2 to 32 streams
CTS RTS DTR DSR DCD RIN -RTS / CTS Flow Control is another flow control mechanism that is part of the RS232 standard Transmission Initialization bit (TIN) and
the Receive Initialization bit (RIN)
Sync Timer -32 bits on 32KHZ (falling edge). Go from zero to pre-define value and continue from zero

## Slide 26: AM437x has numerous serial peripherals (cont.)…
PWM Subsystem
  eCAP (3)
    Up to Three 32-bit enhanced Capture Modules – configurable as 3 capture inputs or 3 auxiliary PWM outputs
  eHRPWM (6)
    Up to Six Enhanced High Resolution PWM modules (eHRPWM) – with dedicated 16-bit time base counter with time and frequency controls.
  eQEP (3)
    Up to Three 32-bit enhanced Quadrature Pulse Encoder modules
HDQ/1-wire
  For connection to battery gauges
DCAN (2)
  Same as AM335x
McSPI (5)
  Master/Slave operation, 48MHz clock
  Up to 4 channels for each McSPI0,1, two channels on McSPI2,3
New feature vs. AM335x
Notes: PWM - Pulse Width Modulation
The Pulse-Width Modulation Subsystem (PWMSS) consists of an instance of Enhanced High Resolution Pulse Width Modulator (eHRPWM),
Enhanced Capture (eCAP), and Enhanced Quadrature Encoded Pulse (eQEP) modules.
1-Wire is a device communications bus system designed by Dallas Semiconductor Corp. that provides low-speed data, signaling, and power over a single signal.[1] 1-Wire is similar in concept to I²C, but with lower data rates and longer range.
HDQ –HDQ communication between host and slave single wire open-drain, The protocol is asynchronous
DCAN Control Area Network - The Controller Area Network is a serial communications protocol which efficiently supports distributed
realtime control with a high level of security. The DCAN module supports bitrates up to 1 Mbit/s and is
compliant to the CAN 2.0B protocol specification. The core IP within DCAN is provided by Bosch.
This device includes two instantiations of the DCAN controller: DCAN0 and DCAN1
McSPI – Multichannel Serial Interface

## Slide 27: AM437x: Two ADCs
AM335x
ADC0 (Touchscreen)
  12-bit Successive Approximation Register (SAR) ADC
  867KSPS
  8 analog inputs
  Can be configured as a Touchscreen Controller. When configured as TSC, it takes away pins/channels for general purpose ADC use.
ADC1
  12-bit Successive Approximation Register (SAR) ADC with preamp
  867KSPS
  8 analog inputs
ADC0
ADC0
ADC1
Simultaneous mode
ADC1 controls ADC0 AFE
2 16bit results can be read from one 32bit register inputs converted to 32bit value
FIFO0
FIFO1
AFE
AFE
8inputs
8inputs
16bits
16bits
32bits
AM437x
ADC0
ADC1
New feature vs. AM335x
Notes: Successive Approximation register
KSPS – k signals per second?
AFE-

## Slide 28: Memories and Buses
Programmable Real-Time Unit (PRU) Subsystem
Interconnect
INTC
Peripherals
PRU0 I/O
Inst. RAM
Shared RAM
DataRAM
Inst. RAM
DataRAM
PRU1 I/O
Shared
Memory
Peripherals
Peripherals
GP I/O
L4 Interconnect
ARM Subsystem
Cortex-A8
L1 Instruction Cache
L1 Data Cache
L2 Data Cache
PRU0 (200MHz)
PRU1 (200MHz)
L3 Interconnect
L3 Interconnect
Notes: ARM + PRU + memories + peripherals = SoC
PRU works as a co-processor in system-level implementation, or
- PRU works independently

## Slide 29: Buses and Memories
PMU Internal memories
  32K L1P, 32K L1D, 256K L2/L3, 64K RAM
PRU Internal memory
  Data and Instruction RAM per PRU, Shared RAM
L3 Shared RAM (OCMC)
  256KB shared memory
External Memory
  32-bit LPDDR2/DDR3/DDR3L
Notes: PMU – Programming Multi-channel Unit (The ARM module)
LPDDR - Low Power Double Data Rate memory 266MHZ
DDR3 – 400MHZ
DDR3L – low voltage DDR3
OCMC – On chip memory controller

## Slide 30: AM437x Memory interface (LPDDR2/DDR3)
Features of the EMIF4D include:
  Frequency Targets
    LPDDR2: 266 MHz Clock (532 MHz Data Rate)
    DDR3 (1.5V) /DDR3L (1.35V): 400 MHz Clock (800 MHz Data Rate)
  16 or 32 bit data bus
  2GB total addressable space
  Supported Memory configurations
    1 load (x32 device)
    2 loads (x16 devices)
    4 loads (x8 devices)
  Supports a maximum of 4 address loads DDR3, 2 data loads for LPDDR2 and 1 data load for DDR3
AM437x
LPDDR2 (x32)
AM437x
DDR3
(x16)
AM437x
DDR3
(x16)
DDR3
(x16)
AM437x
DDR3
(x16)
DDR3
(x16)
D[31:16]
D[15:0]
Addr/Ctrl
T topology
Point to point
Fly-by topology
VTT
New feature vs. AM335x
Notes: Fly-by Topology – interleaving between the two memories (time delay)

## Slide 31: AM437x DDR3 Low Power
AM437x
DDR3
New feature vs. AM335x
Low power enhancements for DDR3
  Fail Safe I/O for DDR_RESET: Facilitates external pull-up to keep DDR in self-refresh during RTC+DDR.
  PMIC: Load Switch facilitates separation of DDR voltage to AM437x and DDR memory
  Added extra signaling in hardware to facilitate suspend/resume sequencing
DDR_CKE
DDR_RESET
VDDS_DDR
AM437x
DDR3
DDR_CKE
DDR_RESET
DeepSleep
RTC + DDR
WKUP
VDDS_DDR
VDDS_DDR
VDDS_DDR
Notes: PMIC – Power Management integrated circuit

## Slide 32: Buses and Memories- Inter-Connect
L3 – High performance Interconnect
  Packet based protocol based on a Network-On-Chip (NoC) interconnect infrastructure
  Connect all high bit rate peripherals and IP

## Slide 33: Buses and Memories-Inter-Connect
L4 - low latency low bandwidth access inter-connect
  non-blocking peripheral interconnect
  Up to 4 Masters (Initiators) and up to 63 slave (targets)

## Slide 34: Clocks
Input Clocks to device
  19.2, 24, 25, 26 MHz system clock
  RTC Clock - 32kHz clock. From Crystal or PER PLL
6 PLLs to generate various system clocks:
  MPU PLL - ARM MPU subsystem
  DDR PLL – for DDR interface
  PER low jitter PLL - USB & Peripherals (MMC/SD, UART, SPI, I2C, etc.)
  CORE PLL - L3, L4, Ethernet, SGX
  Display PLL – DSS Pixel Clock and IEEE1588
  EXT low jitter PLL – drives external devices through CLKOUTx
New feature vs. AM335x

## Slide 35: AM437x ROM (Boot ROM)
Boot from a number of sources, selectable with SYSBOOT pins
  Memory boot
    SD cards
    eMMC – support for >2GB on either MMC0 or MMC1
    NOR flash – support for muxed and non-muxed XIP boot
    NAND flash - 8 or 16 bit
    SPI EEPROMs
    QSPI - XIP boot from serial flash
    USB Host (USB1) – USB mass storage devices, USB thumb drives, great for product upgrades
  Peripheral boot
    Ethernet – support for MII, RMII, and RGMII boot.
    USB client (USB0)
    UART
Boot occurs in MPU and CORE OPP50 in all modes
New feature vs. AM335x
Notes: Memory Booting: booting the device by executing firmware stored on permanent memories like flashmemory
or memory cards. This process usually occurs after a cold or warm reset of the device.
• Peripheral Booting: booting the device by downloading the executable code over a communication
interface such as UART, USB, or Ethernet. This process is can also be used to flash a device.
eMMC – e Multi Media card
Opp50 – certain voltage

## Slide 36: AM437x: A scalable platform with 4 pin-to-pin compatible devices
ARM Cortex-A9
(MHz)
Graphics
Package
Programmable Real-time Unit & Industrial Communication Sub-System (PRU-ICSS)∆
17x17/0.65mm †
800/1000*
17x17/0.65mm †
800/1000*
3D graphics
17x17/0.65mm †
800/1000*
17x17/0.65mm †
800/1000*
Pin-to-Pin Compatible
Software Compatible
AM4379
AM4378
AM4377
AM4376
PRU-ICSS + EtherCAT® slave
∆ PRU-ICSS is commonly used for slave industrial communication protocols such as PROFIBUS, PROFINET®, Powerlink, Ethernet/IP™ and EnDat
† Via Channel Array technology provides 0.8mm-pitch effective layout routing rules.
*pending silicon characterization
3D graphics
PRU-ICSS
PRU-ICSS
PRU-ICSS + EtherCAT® slave

## Slide 37: AM437x – Differentiation vs. AM335x
ARM®
Cortex A9
Up to 1 GHz
Graphics Acceleration
SGX530
Display
Subsystem
24bit LCD
Debug
WDT
RTC
EDMA
System Services
12 Timers
Security AccelerationPac
Crypto, Secure boot
2x 12-bit ADCs
Simple Pwr Seq
SyncTimer32K
Connectivity and IOs
PWM x6
NAND
/NOR (16bit ECC)
3 MMC/ SD/SDIO
CAN x2
USB2 OTG +PHY x2
eCAP/
eQEP x3
EMAC
2-port switch 10/100/1G w/1588
HDQ
QSPI
45nm
Touch Screen Controller
32K/32K L1
Processing:
Overlay, Resizing, Color Space Conversion, etc.
Camera I/F (2x Parallel)
McASP x2
GPIO
UART x6
SPI x5
I2C x3
256K L2 / L3
64K RAM
256KB L3 Shared RAM
32-bit LPDDR2/DDR3/DDR3L
Improved vs.
AM335x
Cortex-A9 delivers up to 2500 DMIPs
20% higher than Cortex-A8
VFP unit 10 times faster than Cortex-A8
256KB RAM configurable as either L2 cache or L3 SRAM, providing up to 512KB of internal L3 RAM
Secure boot enables IP protection, anti-cloning, and take-over protection
QSPI interface enables execute-in-place (XIP) from low-cost NOR flash
Enables DDR-less applications
Simplified power sequencing for flexible power design
System cost savings
Increased L3 RAM (AM335x has 64KB)
32b DDR memory interface increases bandwidth (vs 16b in AM335x)
Single/Dual camera port
For apps such as data terminals, barcode scanners, etc.
Increased SPI, Timers, PWMs, and ADC inputs
New HDQ/1-Wire interface for sensors and battery monitor
PRU-ICSS
Industrial
Communications + Motor Feedback
Protocols +
Sigma Delta
Display processing off-loads CPU from tasks such as overlay, etc.
Contributes to higher performance than AM335x
ICSS for industrial protocol acceleration - enables simultaneous industrial Ethernet protocols and motor feedback protocols.

## Slide 38: System enhancements over AM335x
I/O Cell Power Management
  I/O Daisy chaining - Allows for wakeup from any GPIO, not just wakeup domain GPIO0
  I/O Isolation – more control with low power pad configuration
MPU auto clock gating
  MPU will automatically be clock gated in WFI
  Wakeup via interrupts
New feature vs. AM335x
Simplified power sequencing
  Provide 1.8V bias voltage from 3.3V rail.
    Simplifies power up/down sequencing for discrete power solutions

## Slide 39: System enhancements over AM335x
Improved CLKOUT performance
  Output buffers are on separate voltage domain to reduce noise
  Provided low jitter PLL for Ethernet, modem applications
  Added different input options (MPU clock, EXT PLL)
  CLKOUT1 path is optimized
New feature vs. AM335x

## Slide 40: Package
ZDN Package:
  17x17 mm 0.65 pitch via channel array [0.8 routable] package
  Separate VDD_MPU and VDD_CORE

## Slide 41: Software Overview

## Slide 42: EVMs and Tools

## Slide 43: Get to market fast with AM437x dev. tools
TMDXEVM437X
TMDXSK437X
AM4378 – Up to 1GHz
AM4378 – Up to 1GHz
AM4379 – Up to 1GHz
2GB DDR3
1GB DDR3L
1GB DDR3
7” Cap Touch / LCD
4.3” Cap Touch / LCD
None
2Q 2014
4Q 2014
3Q 2014
2x Camera modules
1x Gb Ethernet port
NAND/eMMC
2x DCAN
HDMI/LCD
In/Out audio
1x Camera module
2x Gb Ethernet ports
QSPI-NOR Flash
No DCAN
LCD only
In/Out audio
1x Camera module
QSPI-NOR Flash
1x Gb Ethernet
PWM & ADC
No display
2x Industrial Ethernet
Linux
Linux
SYS/BIOS
CPU-Freq
Memory
Display
Software
Available
Key Features
Target: $599
Target: $299
Target: $329
TPS65218
TPS65218
Discrete solution
PMIC
TMDXIDK437X
Connector for WiLink8
Connector for WiLink8
N/A
WLAN/BT

## Slide 44: EVM design approaches
Limited muxing options on each board
  Facilitated modularization of interfaces (easier for customers to reference)
  All I/F not available on one board.
Several different DDR layout references
  GP EVM: 4 devices (x8) DDR3 fly-by topology with VTT termination
  SK: 2 devices (x16) T- topology, no VTT termination
  IDK: 2 devices (x16) fly by topology, with VTT termination
PMIC
  GP EVM: TPS65218, DDR3=1.5V
    includes external 1.8V LDO to demo RTC only mode (workaround for PMIC errata pre V2.0)
  StarterKit: TPS65218, DDR3L=1.35V
    no 1.8V LDO (plan to use PMIC v2.0)
  IDK: Discrete solution, not optimal cost.
    Power efficiency was key goal (single stepdown converters from 24V).
    Demos power sequencing optimizations (uses 1.8V internal LDO)

## Slide 45
Peripheral support on AM437x GP EVM
4 x8 Fly-by DDR3
AM437x
SYSBOOT
eMMC (4GB)
NAND (4Gb)
DCAN #1
PMIC
uSD
Audio codec
USB JTAG
ADC header

## Slide 46
HDMI
Audio in
Gigabit
Ethernet
Audio out
USB 2.0
Micro USB 2.0
UART #0
DCAN #0
Power switch
+5V
20-pin ARM
JTAG Connector
Camera #1
connector
Camera 2Mp
Power LEDs
WLAN/BT COM
connector
7” LCD
800x480
Touchscreen
User LEDs
User Buttons

## Slide 47: GP EVM: design features
GP EVM: Power Management features
Measurement points for key voltage rails
I2C Power monitor captures realtime measurements
GPIO control of external peripherals for system low power
TPS65218 PMIC: reference for all voltage rails and power control

## Slide 48: AM437x Industrial Development Kit (IDK) Motor control with communications
Single axis motor control
  3x PWM with ADC feedback
  Expansion to dual axis
Industrial Comm Protocols
  2x 10/100 Eth PHYs
Gb Eth for diag and monitoring
USB and ARM JTAG
Boot from QSPI or uSD
Expansion via capes
DCAN

## Slide 49: AM437x documentation
http://ap-fpdsp-swapps.dal.design.ti.com/index.php/AM437x_Collaterals
  EVM
    Schematics, Board files (layout), PCB design specs, H/W users guide
  AM437x
    TRM and datasheet
By RTM
  Errata: PG1.2 production, errata will mention PG1.1
  EVMs: Diagnostic Code, Symbols and Footprints
  Schematic review checklist, Migration Guides
  Tools: Clock Tree Tool (CTT), Pinmux tool, Power Estimation Tool (PET)
  Layout Guidelines for DDR and USB
  Throughput app notes
  Power Consumption summaries
  BSDL and IBIS models

## Slide 50: AM335x Pinmux

## Slide 51: Pinmux tool for AM437x
Package view of pins used
Choose I/F to be used, tool will automatically select pinmux
Choose any available pin or fix a pin
Choose I/F voltage
I/O set automatically chosen
Automatically optimizes pin selection as user adds interfaces
Conflicts are identified
Outputs Starterware header files (device tree files coming soon!)
Standard tool for other devices (AM335x, Vayu AM57x, Galileo, etc.)

## Slide 52: Pinmux tool demo

## Slide 53
Patient Monitoring
Bar Code Scanners
Navigation Equipment
Point of Service
Industrial Automation
Portable Mobile Radio
Portable Data Terminals
Test And Measure