## Slide 1: KeyStone ARM-DSP Interaction
KeyStone Training
Multicore Applications
Literature Number: SPRP###

## Slide 2: Agenda
MPM
Memory management
ARM-DSP Communication Architecture
Resource management

## Slide 3: Typical Keystone II model
MPM – Multi-processor manager

## Slide 4: MPM Operation
MPM server daemon maintains a state machine for each slave core
MPM command line (or client) utility provides a command line interface to MPM server. Can be called from a terminal or from an application
MPM can reset a core, load a core with executable, run a core, collect messages from a core, and collect information after core crash (if there is an exception)

## Slide 5: Core state machine

## Slide 6: Managing a core
From a terminal
  mpmcl load dsp0 program.out
  Must be in elf format
  Part of the lab exercises
From an application
  Include file is part of MCSDK release at /mpm_2_00_01_01/include/mpmclient.h
  Library is part of MCSDK release at /mpm_2_00_01_01/lib/libmpmclient.a

## Slide 7: DSP Image requirements
DSP image must be in ELF format
MPM must know about the memories that the image uses, and it must not overwrite ARM dedicated memories
  More about memory management later
Special sections must be defined to facilitate communications between DSP core and ARM
  This is done by the RTSC tools if IPC or MPM used var Resource = xdc.useModule('ti.ipc.remoteproc.Resource');
  The next slide shows a project map file with the resource section

## Slide 8: Mpm_example map file

## Slide 9: ARM accessing core information
MPM server monitor the resource table section
System_printf writes messages to resource table
The user (or application) can access the messages in /sys/kernel/debug/remoteproc/remoteprocN/trace0
  Where N is the DSP core number

## Slide 10: ARM accessing core Dump
MPM can monitor crash events from DSP and get core dump
  The DSP code needs exception hook
  Defined a special memory section
Fault sample test application is part of pdk release at pdk_keystone2_3_00_04_18/packages/ti/instrumentation/fault_mgmt/test

## Slide 11: MPM Configuration
The file mpm_config.json is a Java Script Object Notation file that describes the DSP access memory segments to the ARM.
10 memory segments are defined:
  Eight segments are for each DSP core l2 local memory
  One segment for MSM memory
  One segment for the part of DDR that is used by the MPM as shared memory
mpm_config.json definition of Core 0 L2 memory:
{
"name": "local-core0-l2",
"localaddr": "0x00800000",
"globaladdr": "0x10800000",
"length": "0x100000",
"devicename": "/dev/dsp0"
},

## Slide 12: MPM Configuration
The two shared memory definitions show that the DSP dedicated memory in DDR starts at 0xa0000000 and has a size of 512M (-1K) bytes (TI default)
1K of memory is needed for the MPM management
{
"name": "local-msmc",
"globaladdr": "0x0c000000",
"length": "0x600000",
"devicename": "/dev/dspmem"
},
{
"name": "local-ddr",
"globaladdr": "0xa0000000",
"length": "0x1FFFFC00",
"devicename": "/dev/dspmem"
}

## Slide 13: Last word about MPM
U-BOOT variable mem_reserve define the DDR area that is used by MPM to load DSP image
  More about it later

## Slide 14: Agenda
MPM
Memory management
ARM-DSP Communication Architecture
Resource management

## Slide 15: Managing Keystone II Memories
KeyStone ARM-DSP Interaction

## Slide 16: Disclaimer
The following slides show how the TI implementation that runs on the TCIEVM6638K2K works.
Other implementations may be different

## Slide 17: Keystone II shared memories Physical Addresses
For a complete description of possible memory aliasing see the device data manual
DDR3A_REMAP_EN pin determines the mapping of 00 0800 0000 to DDRA or DDRB

## Slide 18: Translating Logical memory to physical memory
DSP and all other TeraNet masters – MPAX registers
  Static translation (until the MPAX register is changes)
ARM – LPAE
  MMU Dynamic translation to 40 bits, can access 8G of DDRA
  Controlled by U-boot environment variable mem_lpae=1 (default)
ARM NO LPAE
  Disabled MMU, static, can access only 2G of DDRA
  Controlled by U-boot environment variable mem_lpae=0

## Slide 19: DDRA Size for the ARM
U-boot environment variable ddr3a_size tells the system how much memory is available
  0: 2GB (default)
  4: 4GB
  8: 8GB
Memory is used by Linux Kernel, Linux Users domain and DSP cores. The next slides describe TI partition of the DDRA memory
U_BOOT uses device tree and the parameters to create memory segments
More information how to configure system with 8GB see http://processors.wiki.ti.com/index.php/MCSDK_UG_Chapter_Exploring#Using_more_than_2GB_of_DDR3A_memory

## Slide 20: DDR3A partition
DDR3A is partitioned into two segments
Memory size of 8G
  The first segment starts at physical address 0x08 0000 0000 and size of 2G.
  The second segment starts at 0x08 8000 0000 and size 6G.
  Part of the first segment of memory is reserved for the DSP memory. This is used to load programs and data from the ARM user’s domain to the DSP memory
  Part of the first segment is used by the kernel
Smaller DDR3A size may have different partition (see next slides)

## Slide 21: 6638K2K Memory Architecture (8G DDRA)

## Slide 22: 6638K2K Memory Architecture (2G DDRA –larger DSP memory)

## Slide 23: 6638K2K Memory Architecture (1G DDRA) (32bit DDR)

## Slide 24: Define Memories Available To MMU
TI LINUX u-boot Keystone source release (git) u-boot-keystone/board/ti/tci6638_evm has the file board.c. This file sets the memory architecture for the Linux
The same directory has other files that are used to configure DDR3A and DDR3B and POST code
The next slides show parts of the file board.c
Kernel Drivers get information about resources (including memories) from the device tree. Device tree will be discuss later

## Slide 25: Board.c (1)
/*
* Copyright (C) 2012 Texas Instruments Inc.
*
* TCI6638 EVM : Board initialization
*
* See file CREDITS for list of people who contributed to this
* project.
*
* This program is free software; you can redistribute it and/or modify
* it under the terms of the GNU General Public License as published by
* the Free Software Foundation; either version 2 of the License, or
* (at your option) any later version.
*
* This program is distributed in the hope that it will be useful,
* but WITHOUT ANY WARRANTY; without even the implied warranty of
* MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the
* GNU General Public License for more details.
*
* You should have received a copy of the GNU General Public License
* along with this program; if not, write to the Free Software
* Foundation, Inc., 675 Mass Ave, Cambridge, MA 02139, USA.
*/

## Slide 26: Board.c (2)
#if defined(CONFIG_OF_LIBFDT) && defined(CONFIG_OF_BOARD_SETUP)
#define K2_DDR3_START_ADDR 0x80000000
void ft_board_setup(void *blob, bd_t *bd)
{
u64 start[2];
u64 size[2];
char name[32], *env, *endp;
int lpae, nodeoffset;
u32 ddr3a_size;
int nbanks;
env = getenv("mem_lpae");
lpae = env && simple_strtol(env, NULL, 0);
ddr3a_size = 0;
if (lpae) {
env = getenv("ddr3a_size");
if (env)
ddr3a_size = simple_strtol(env, NULL, 10);
if ((ddr3a_size != 8) && (ddr3a_size != 4))
ddr3a_size = 0;
}

## Slide 27: Board.c (3)
nbanks = 1;
start[0] = bd->bi_dram[0].start;
size[0] = bd->bi_dram[0].size;
/* adjust memory start address for LPAE */
if (lpae) {
start[0] -= K2_DDR3_START_ADDR;
start[0] += CONFIG_SYS_LPAE_SDRAM_BASE;
} // segment 0
if ((size[0] == 0x80000000) && (ddr3a_size != 0)) {
size[1] = ((u64)ddr3a_size - 2) << 30;
start[1] = 0x880000000;
nbanks++;
}// segment 1

## Slide 28: Linux Device Tree
Linux Device tree is an ASCII file XX.dts that describes the resources available to Linux. A compiled version of the file XX.dtb is used by the Linux kernel.
Device tree source code has a well-defined syntax
The information in the device tree is used by device drivers

## Slide 29: Standard Device Tree Example
k2hk-evm.dts is from the public git server
/dts-v1/;
/include/ "keystone.dtsi"
/include/ "k2hk.dtsi"
/ {
compatible = "ti,k2hk-evm", "ti,keystone";
aliases {
ethernet1 = &interface1;
mdio-gpio0 = <&mdiox0>;
};

## Slide 30: Device Tree Defines Available CPU
cpus
{ interrupt-parent = <&gic>;
cpu@0 {
compatible = "arm,cortex-a15";
};
cpu@1 {
compatible = "arm,cortex-a15";
};
cpu@2 {
compatible = "arm,cortex-a15";
};
cpu@3 {
compatible = "arm,cortex-a15";
};
};

## Slide 31: Memory Defined in Device Tree
The device tree defines which memory is used by the Linux and which is used by the DSP
The Device Tree for the EVMK2H is k2hk-evm.dts. This tree defines several memories, including the total logical memory and what part of it will be used by the kernel. It also defines what memories will be reserved for the DSP.

## Slide 32: Memory Definitions for 6638K2K- Device Tree
dspmem: dspmem
{
compatible = "linux,rproc-user";
mem = <0x0c000000 0x000600000 0xa0000000 0x20000000>;
label = "dspmem";
};
memory
{
reg = <0x00000000 0x80000000 0x00000000 0x20000000>;
};
NOTES:
linux-keystone/arch/arm/boot/dts /k2hk-evm.dts includes two files, keystone.dtsi and k2hk.dtsi. The memories are defined in these files
The start address of the DSP DDR is determined by the U-BOOT parameters.
When building DSP code, one must be aware what is the start DDR address for DSP

## Slide 33: DSP Definition in Device Tree
For each C66x CorePac, seven memory definitions:
  Address of Core control registers (boot address, power)
  L1 P global memory address
  L1 D global memory address
  L2 global memory address
In addition, the MSM memory address and DDR addresses that are dedicated to DSP usage are defined.
DSP code that uses DDR must use ONLY the DDR addresses that are assigned to it.

## Slide 34: Memory Definitions from 6638K2K Device Tree
dsp7: dsp7
{
compatible = "linux,rproc-user";
reg = <0x0262005C 4
0x02350858 4
0x02350a58 4
0x0262025C 4
0x17e00000 0x00008000
0x17f00000 0x00008000
0x17800000 0x00100000>;
reg-names = "boot-address", "psc-mdstat", "psc-mdctl", "ipcgr", "l1pram", "l1dram", "l2ram";

## Slide 35: U-BOOT and mem_reserve
The size of the DSP DDR reserve memory is defined in UBOOT as mem_reserve. The default size is 512M – 0x2000 0000
To change the size of the reserve memory, the value mem_reserve should be changed in the UBOOT using setenv mem_reserve value
NOTE: The UBOOT code uses the function ustrtoul to convert the ASCII value into a numeric value. It understands notations such as 512M.

## Slide 36: U-BOOT and mem_reserve
Question: Is changing the mem_reserve value in UBOOT enough to change the memory segment that is dedicated to the DSPs for MPM?
  The file mpm_config.json tells MPM what memories are available. It must agree with the device tree and the UBOOT

## Slide 37: Building DSP Code for MPM
DSP projects that use RTSC must define a platform.
The standard TI platform (standard = in the release) was not built to work with MPM if DDR is used by the DSP.
If the DSP code uses only L2 memory, no action is needed. But if the DSP code uses DDR, a new platform must be defined.
Projects that do not use RTSC must have a linker command to define the memory structure. The linker command must be modified to work with MPM.

## Slide 38: Standard K2H Platform Definition for DSP RTSC Build

## Slide 39: Define New DSP Platform: 2G DDR, 512M Dedicated ARM Memory

## Slide 40: Agenda
MPM
Memory management
ARM-DSP Communication Architecture
Resource management

## Slide 41: ARM-DSP Communication Architecture
KeyStone ARM-DSP Interaction

## Slide 42: ARM-DSP Collaboration
MPM: Managing the DSP cores from the ARM
  DSP executables are in the ARM file system
  ARM can reset, load, run, and get messages and dump core out of a DSP core
IPC: Exchanging data and messages between ARM and DSP
  User Space libraries
  Applications that use IPC – OpenCL, openMP

## Slide 43: User Mode ARM and DSP IPC Issues
Logical and physical Memory
  Continuous Memory
  Different translation types
Linux Protection
  By-pass the MMU, get physical address from kernel space
Linux and DSP Coherency
  There is not coherency between the ARM memory and the DSP direct access
Free messages and data
  How does the ARM know when it can re-use the memory?

## Slide 44: Current solution (release 4_18)- IPCv3
From ARM to DSP
  Copy the data from user space to kernel space memory
  Copy the data from Kernel space memory to share memory DSP
    Solve memory issues
    Solve coherency issues on ARM (DSP does not have hardware coherency anyhow)
    Solve protection issue
  Needs close loop protocol to re-use shared memory
  Involves two copies, requires CPU resources – Control Path

## Slide 45: IPC Types: IPCv3
Control Path: IPCv3
  Standard APIs agree with older versions of IPC
  General purpose control path supports reliable delivery
  Designed to deliver short messages, but can be used for “unlimited” data movement
  Uses RPMSG kernel driver for clean partition between user and kernel space

## Slide 46: HPC solution (release 4_19)- Data path
Used under-the-hood for openCL and openMP systems
Use cmem – get a continuous buffer to user domain
Use the Navigator to move data – one copy by the navigator PktDMA
Navigator takes care of free memory
Faster than IPCv3 solution

## Slide 47: Future solution Navigator based IPCv3
Use the system that was developed in HPC release for genuine IPC messages between ARM and DSP
Will be available in future releases (as of July 2014)

## Slide 48: Support for User Develop IPC
Fast Path: PktIO and QMSS
Continuous memory is provided by cmem
On the ARM side, there is a library netapi that supports creating, sending, and receiving packets from the ARM user space.
Fire and forget (send) polling (ARM) for receive. On DSP, receive is polling, or interrupt, or accumulators (using QMSS DLL)
Navigator-based transaction, sending packets (descriptors). Up to 64 memory regions can be defined in KeyStone II

## Slide 49: ARM IPC Support
Remote Processor Messaging (RPMsg) is an open-source friendly Inter Processor Communication (IPC) framework
SysLink (Part of the IPC release) is a runtime library that provides software connectivity between multiple processors. Each processor may run either an HLOS (such as Linux, QNX, etc.) or an RTOS (such as SYS/BIOS).

## Slide 50
IPC Options

## Slide 51: IPC Examples
MCSDK release has several examples that show IPC properties
Instructions how to install IPC and build these examples on the Linux side and the DSP side are given in the release.
The out-of-box example is described in the next few slides.

## Slide 57: Release IPC Examples

## Slide 58: Agenda
MPM
Memory management
ARM-DSP Communication Architecture
Resource management

## Slide 59: Managing Peripherals and IP in a Heterogeneous Device
KeyStone ARM-DSP Interaction

## Slide 60: Configure and Use peripherals In Heterogeneous Device
DSP - Chip Support Library (CSL) and Low-Level Drivers (LLD) on DSP
ARM- LINUX drivers on the ARM
Sharing resource configuration, control, and usage between different cores is done by Resource management
  Protect resources from conflict usage

## Slide 61: DSP View of Peripherals and IP
Chip support Library (CSL) provides access to the peripherals and other IP
  CSL translates physical MMR locations into symbols, and provides functions to manipulate the MMR
Low level drivers (LLD) is an abstraction layer that simplified the usage of peripherals
Some peripherals have high layer libraries (on the top of LLD) to further abstract peripherals usage details from the application

## Slide 62: DSP: Interface via LLD and CSL Layers

## Slide 63: Linux Control Peripherals and IP
MMU controls memory access for user mode in Linux. Applications do not see physical addresses.
Device drivers can be called by the applications. They can access physical memory.
Linux Device Drivers provide:
  Modularity
  Standard interface
  Standard structure
Linux kernel modularity scheme enables new device drivers to be easily added to the kernel

## Slide 64: Linux Application API
Device drivers can be loaded during boot time or loaded (as modules) during run time.
Driver classification:
  Character device
  Block device
  Network interface
Each driver type has standard API. For example, character devices will have open and close as well as read and write functions.

## Slide 65: KeyStone Drivers Structure Example - SRIO

## Slide 66: Linux Drivers
linux-keystone/drivers (cloned from the public git)

## Slide 67: Resource Management
KeyStone ARM-DSP Interaction

## Slide 68: Keystone II RM: Major Requirements
Dynamically manage resources
Enable management of resources at all levels within system software architecture
  Core, task, application component (LLD)
  During initialization and during run time, from any thread
Runtime modification of resource permissions.
Automate reservation of resources taken by Linux kernel
Use generic, processor-independent transport interface that allows RM instances to communicate regardless of device hardware architecture

## Slide 69: Keystone II RM – Overview (1)
Instance-based Client/Server Architecture:
  Three instance hierarchy:
    RM Server – Global management of resources and permission policies
    RM Client – Provide resource services to system software elements
    RM Client Delegate (CD)
      Offloads management of resource subsets from Server
      Manages a sub-pool of resources
  Resource services provided via instance service API
RM Instances Communication Over Generic Transport Interface
  Application must setup data paths between RM instances
  Allows RM to run on any device architecture without modification to RM source

## Slide 70: Keystone II RM – Overview (2)
RM server is a Linux process.
Two files define the behavior of the RM; The global resource list and the policy file.
Both files are written in the same syntax as device tree and are compiled the same way
From user point of view, the RM calls are transparent (meaning, when you call open, init and so on, RM is called implicitly)

## Slide 71: Keystone II RM – Overview (3)
Global Resource List (GRL)
  GRL captures all resources that will be tracked for a given device
  Facilitates automatic extraction of resources used by ARM Linux from Linux DTB
Policies specify RM instance resource privileges
  Resource initialization, usage, and exclusive right privileges assigned to RM instances
  Runtime modification of policy privileges
    APIs and Linux CLI (Planned)

## Slide 72: Keystone II RM: Overview
ARM/DSP n+2
RM Client Instance
ARM/DSP n
Transport-Specific Data Path
ARM/DSP n+1
ARM  DSP Transport
Transport API
RM CD Instance
Resources Allocated from Server
CD Service Transaction Handler
Client Service Transaction Handler
RM Server Instance
Resource Allocators
PA
QMSS
Allocation policies
CPPI
QMSS
Etc
User Mode (ARM)
Available resources are inverse of Linux DTB
Resource Policies
Transport API
PA
CPPI
QMSS
Etc
Memory Allocator
CPPI
PA
Mem Alloc
Etc
ARM/DSP n+3
RM Client Instance
QMSS
CPPI
PA
Mem Alloc
Etc
Service
Port
Service
Port
Transport API
Client Service Transaction Handler
DSP  DSP Transport
DSP  DSP Transport
Service
Port
ARM  DSP Transport
Transport API
CD Service Transaction Handler
Service
Port
Global Resource List (GRL)
Linux DTB
DSP  DSP Transport

## Slide 73: Keystone II RM: Services
RM Services:
  Allocate (initialization, usage)
  Free
  Map resource(s) to NameServer name
  Get resource(s) tied to existing NameServer name
  Unmap resource(s) from existing NameServer name
Non-blocking service requests directly return result
Blocking service requests return ID to system

## Slide 74: Keystone II RM: Global Resource List (GRL)
Specified in Device Tree Source (DTS) format
  Open source, dual GPL/BSD-licensed LIBFDT used for parsing GRL
Input to server on initialization
Server instantiates allocator for each resource specified in GRL
A GRL specification for a resource includes:
  Resource name
  Resource range (base + length)
  Linux DTB alias path (if applicable)
  Resource NameServer assignments (if applicable)
Permissions not specified in GRL; In the policies

## Slide 75: GRL Example
An example of the Global Resource List and policy files can be found in the MCSDK:
/MCSDK_3_00_00_XX/pdk_keystone2_1_00_00_XX/packages/ti/drv/rm/device/k2h
The first few lines of the file are shown in next slide.
In the same directory there are two policy files:
  policy_dsp_arm.dts
  policy_dsp-only.dts

## Slide 76: global-resource-list-arm-dsp.dts
/dts-v1/;
/ {
/* Device resource definitions based on current supported QMSS, CPPI, and
* PA LLD resources */
qmss {
/* Number of descriptors inserted by ARM */
ns-assignment = "ARM_Descriptors", <0 4096>;
/* QMSS in joint mode affects only -qm1 resource */
control-qm1 {
resource-range = <0 1>;
};
control-qm2 {
resource-range = <0 1>;
};
/* QMSS in joint mode affects only -qm1 resource */
linkram-control-qm1 {
resource-range = <0 1>;
};

## Slide 77: Policy Example: policy_dsp_arm.dts (1)
/dts-v1/;
/* Keystone II policy containing reserving resources used by Linux Kernel */
/ {
/* Valid instance list contains instance names used within TI example projects
* utilizing RM. The list can be modified as needed by applications integrating
* RM. For an RM instance to be given permissions the name used to initialize it
* must be present in this list */
valid-instances = "RM_Server",
"RM_Client0",
"RM_Client1",
"RM_Client2",
"RM_Client3",
"RM_Client4",
"RM_Client5",
"RM_Client6",
"RM_Client7";

## Slide 78: Policy Example: policy_dsp_arm.dts (2)
qmss {
control-qm1 {
assignments = <0 1>, "iu = (*)";
};
control-qm2 {
assignments = <0 1>, "iu = (*)";
};
linkram-control-qm1 {
assignments = <0 1>, "(*)"; /* Used by Kernel */
};
linkram-control-qm2 {
assignments = <0 1>, "(*)"; /* Used by Kernel */
};
linkram-qm1 {
assignments = <0x00000000 0xFFFFFFFF>, "iu = (*)";
};
linkram-qm2 {

## Slide 79: For More Information
Software downloads and device-specific Data Manuals for the KeyStone II SoCs can be found at TI.com/multicore.
For articles related to multicore software and tools, refer to the Embedded Processors Wiki for the KeyStone Device Architecture.
For questions regarding topics covered in this training, visit the support forums at the TI E2E Community website.

## Slide 80: Backup – PktLib Utility Libraries

## Slide 81: Packet Library (PktLib)
Purpose: High-level library to allocate packets and manipulate packets used by different types of channels.
Enhance capabilities of packet manipulation
Enhance Heap manipulation

## Slide 82: Heap Allocation
Heap creation supports shared heaps and private heaps.
Heap is identified by name. It contains Data buffer Packets or Zero Buffer Packets
Heap size is determined by application.
Typical pktlib functions:
  Pktlib_createHeap
  Pktlib_findHeapbyName
  Pktlib_allocPacket

## Slide 83: Packet Manipulations
Merge multiple packets into one (linked) packet
Clone packet
Split Packet into multiple packets
Typical pktlib functions:
  Pktlib_packetMerge
  Pktlib_clonePacket
  Pktlib_splitPacket

## Slide 84: PktLib: Additional Features
Clean up and garbage collection (especially for clone packets and split packets)
Heap statistics
Cache coherency

## Slide 85: For More Information
Software downloads and device-specific Data Manuals for the KeyStone SoCs can be found at TI.com/multicore.
Multicore articles, tools, and software are available at Embedded Processors Wiki for the KeyStone Device Architecture.
View the complete C66x Multicore SOC Online Training for KeyStone Devices, including details on the individual modules.
For questions regarding topics covered in this training, visit the support forums at the TI E2E Community website.