## Slide 1: Implementation of AMAT/ProDrive Model
Ran Katzur 10-8-2014

## Slide 2: Agenda
Demo Model
Shannon Copy Implementation details
  Shannon DDR Partition
  Shannon DSP Core copy considerations
  Shannon Cores MPAX configuration
  Hyperlink look-up table configuration
66AK2H12 Configuration
  Memory management
  MPAX configuration
Implementation pseudo Code

## Slide 3: Basic Card

## Slide 4: Management Communication
Message Types:
Data Address for the next load
Finish Loading
Message Media:
SRIO type 11
SRIO DirectIO
Ethernet

## Slide 5: SRIO
Short messages – less than 256 bytes
  Message type (2 Bytes)
  Sender ID (2 bytes)
  Destination ID (2 bytes)
  Destination address (4 bytes)
  Other information needed
Type 11
  up to 64 mailboxes and 4 letters (single packet model)
  Hardware protected messages- each message has acknowledgment
  Access through sockets
  Each ARM thread can have its own mailbox - socket
Direct IO
  Need to define protocol structure

## Slide 6: IPC Control Communication
From ARM thread to DSP core:
Copy my memory to your memory
Copy your memory to my memory
Execute a function
From DSP core to ARM:
Finish Copying
Finish processing with results

## Slide 7: IPC over Hyperlink - Simple Model
Each thread is associated with one DSP core
Simple “messageQ” type model, single writer
No interrupts, messages are always pulled
Double buffering for messages, simple state machine for the write side and the read side
Each side of the transection keeps score what buffer it should read next and what buffer it should write next
Each side takes care of cache coherency
Communicating with the DSP that are on 66AK2H12
  Same algorithm, uses direct read and write with cache coherency

## Slide 8: ARM Thread – DSP Core Messages
Thread sends a message to DSP Core
DSP reads and execute the message
DSP send acknowledgment to thread
  Buffer 0 is released
Thread send the next message to DSP
  Can be before step 3
DSP reads and processes the message
DSP send acknowledgment to thread
  Buffer 1 is released
Note: The number of message buffers is the depth of processing queue. The Arm thread keeps track on number of available (free) messages

## Slide 9: Copy Data From Thread to DSP Core
DSP core gets a message from the thread with source logical address and physical logical address
DSP initiates EDMA transfer via the Hyperlink and waits for the EDMA completion
At the completion of the transfer the DSP send a message to the thread
MPAX and Hyperlink configuration will be discuss later

## Slide 10: Copy Data From DSP Core to Thread
DSP core gets a message from the thread with source logical address and physical logical address
DSP initiates EDMA transfer via the Hyperlink and waits for the EDMA completion
At the completion of the transfer the DSP send a message to the thread
MPAX and Hyperlink configuration will be discuss later

## Slide 11: DSP Core Real-time State Machine
DSP wait for a new message to arrive
When message arrive the DSP executes the function that is associated with the message
Upon completion of execution the DSP sends message back to the thread, and updates the buffer number for the next message (Both directions)
DSP returns to the waiting state. If there is a message waiting it continue with step 2, otherwise continue waiting

## Slide 12: The Thread Real-time Algorithm Assume ARM manages DSP Data Memory
Thread checks if a new message from FPGA arrived
  If a message arrived, it processes the message and then checks for new message from the DSP core
  If no message arrive, checks to see if a new message arrived from the DSP
Thread checks if a new message from DSP arrived
  If a message arrived, it processes the message and then checks for new message from the FPGA core
  If no message arrive, checks to see if a new message arrived from the FPGA

## Slide 13: Processing FPGA message Assume ARM manages DSP Data Memory
Messages to DSP includes source logical address and scratch logical address if needed
Logical scratch address is managed by the ARM thread and is used for post processing (post mortem)

## Slide 14: Processing DSP Message Assume ARM manages DSP Data Memory

## Slide 15: Thread Post-Processing Assume ARM manages DSP Data Memory

## Slide 16: Agenda
Demo Model
Shannon Copy Implementation details
  Shannon DDR Partition
  Shannon DSP Core copy considerations
  Shannon Cores MPAX configuration
  Hyperlink look-up table configuration
66AK2H12 Configuration
  Memory management
  MPAX configuration
Implementation pseudo Code

## Slide 17: C6678 Memory Management

## Slide 18: C6678 Memory Segment
Physical Address | Size | description | Logical address for the core | Comment
0x0 0c00 0000 | 4MB | MSMC shared memory | 0x0c00 0000 | Use for IPC, all DSP cores can see this memory
0x8 8000 0000 | 384MB | DSP 0 private memory | 0x8000 0000 | Access only by DSP 0
0x8 9800 0000 | 384MB | DSP 1 Private memory | 0x8000 0000 | Access only by DSP 1
0x8 b000 0000 | 384MB | DSP 2 private memory | 0x8000 0000 | Access only by DSP 2
0x8 c800 0000 | 384MB | DSP 3 Private memory | 0x8000 0000 | Access only by DSP 3
0x8 e000 0000 | 384MB | DSP 4 private memory | 0x8000 0000 | Access only by DSP 4
0x8 f800 0000 | 384MB | DSP 5 Private memory | 0x8000 0000 | Access only by DSP 5
0x9 1000 0000 | 384MB | DSP 6 private memory | 0x8000 0000 | Access only by DSP 6
0x9 2800 0000 | 384MB | DSP 7 Private memory | 0x8000 0000 | Access only by DSP 7
0x9 4000 0000 | 1GB | Shared Memory for all cores | 0xc000 0000 | Accessed by all cores, will have code, constants and so on
0x8 8000 0000** (For each core the start address will be different, the implementation will be describe in the MPAX implementation section) | 1GB – 384M = 0x2800 0000 | No core has access except to its own region | 0x9800 0000 | This segment will have no permission to read, write or execute for any core. This is done to prevent one core overwrite the data of another core

## Slide 19: MPAX registers – Shannon side
Each DSP core master has its own set of MPAX registers
Teranet has multiple sets of SES and SMS MPAX registers
Since EDMA inherent the PrivID of the DSP core that initiates the transfer, each core will configure its own MPAX registers and the SES and SMS MPAX registers that are associated with its PrivID.
Multiple MPAX registers may map the same Logical address, each one to a different physical address. It that case the actual translation is done based on the MPAX register with the higher ID number. This feature will be used to prevent DSP core from accessing private memory of another core.
The default setting of the MPAX registers uses MPAX register 0 to map all internal device addresses (logical memory MSB is 0x0) to internal memory ), just add 4 bits of zero as the MSB, and maps 2G of external memory (MSB is 0x1) to 2G physical addresses starting with address 0x8 8000 0000. The SES and SMS default registers are similar. These registers will not be modified.

## Slide 20: C6678 MPAX Registers
Value | MPAX2 | MPAX3 | MPAX4 | MPAX5
Logical | 0x800000 | 0x800000 | 0x900000 | 0xc00000
Physical | 0x8800000 | 0x8800000 + I * 0x180000 where I is the core number | 0x8900000 + I * 0x180000 where I is the core number | 0x9400000
Size | 0x1E (1G) | 0x1c (256M) | 0xb (128MB) | 0x1E (1G)
Permission | 0x00 | 0x3f | 0x3f | 0x3f
Comment | Permission are all zero, cannot read, write or execute | Configure the private memory, Overwrite MPAX 2 | Configure the private memory, Overwrite MPAX 2 | For the shared memory
The setting of MPAX registers for DSP core I, i=0. 7 (C6678 only)

## Slide 21: C6678 MPAX Registers
Value | SES 1 for PrivID i | SES 2 for PrivID i | SES 3 for PrivID i | SES 4 for PrivID i
Logical | 0x800000 | 0x800000 | 0x900000 | 0xc00000
Physical | 0x8800000 | 0x8800000 + I * 0x180000 where I is the PrivID number | 0x8900000 + I * 0x180000 where I is the PrivID number | 0x9400000
Size | 0x1E (1G) | 0x1c (256M) | 0xb (128MB) | 0x1E (1G)
Permission | 0x00 | 0x3f | 0x3f | 0x3f
Comment | Permission are all zero, cannot read, write or execute | Configure the private memory, Overwrite MPAX 2 | Configure the private memory, Overwrite MPAX 2 | For the shared memory
The setting of SES registers for PriviID I, i=0. 7 (C6678 only)

## Slide 22: C6678 MPAX Registers
The setting of SMS registers for PriviID I, i=0.7 stays as the default

## Slide 23: Hyperlink Considerations
Each CorePac can access up to 256MB of memory (128M Hyperlink 1 on 66AK2H12)
Using ARM thread to move data to an from Shannon limits the data to 256MB (128MB) for all the 8 cores (No run-time re-configure of Hyperlink please)
When the system uses Shannon cores to move data to and from the 66AK2H12, each core can address up to 256MB
If two Shannons use Hyperlink to access remote memory, DDR accessible memory is limited to 2G (31 bits address, the MSB is always 1) in addition to internal-device MMR and memories (MSMC, L2, L1, MMR)

## Slide 24: Hyperlink Considerations (2)
To increase efficiency and reduce complexity it is very important to allow parallel data movements to and from 66AK2H12 DDR
8 ARM threads may exchange data between the ARM and DSP cores within 66AK2H12. This work does not cover internal data move
16 threads move data via the Hyperlink, thus the size limit of Hyperlink is very important

## Slide 25: Hyperlink Considerations (3)
Messages buffer are located on the MSMC memory. All MSMC memory can be accessed by Hyperlink
2G of DDR memory can be access by Hyperlink
Each DSP core can access up to 128M (2G/16)
In the following slides we analyze the Hyperlink configuration that is needed to support Shannon access to 66AK2H12 memories
66AK2H12 access into Shannon (for messages) will be discussed later

## Slide 26: Hyperlink Considerations (4)
We assume that messages reside in MSMC memory
In order to get 128MB DDR for each core, PriviID must be overlay on the look-up table index
The following figure shows the structure of the address value for 4 buffers, 32MB each for each DSP core

## Slide 27: C6678 Hyperlink Address structure

## Slide 28
Tx Address Overlay Control Register
User configures PrivID / Security bit overload in this register
Register is at address HyperLinkCfgBase + 0x1c. For 6678 that is 0x2140_001c
If using HyperLink LLD, hyplnkTXAddrOvlyReg_s represents this register
31 | 20 | 19 | 16 | 15 | 12 | 11 | 8 | 7 | 4 | 3 | 0
Reserved |  | txsecovl |  | Reserved |  | txprividovl |  | Reserved |  | txigmask | 
R |  | R/W |  | R |  | R/W |  | R |  | R/W | 
Address Manipulation: Tx Side Registers
Register Configuration
txsecovl = o – security bit not overlay
txprividovl = 12 (bit 31 to 28)
txigmask = 11 (mask = 0x0fff ffff)

## Slide 29
31 | 26 | 25 | 24 | 23 | 20 | 19 | 16 | 15 | 12 | 11 | 8 | 7 | 4 | 3 | 0
Reserved |  | rxsechi | rxseclo | Reserved |  | rxsecsel |  | Reserved |  | rxprividsel |  | Reserved |  | rxsegsel | 
R |  | R/W | R/W | R |  | R/W |  | R |  | R/W |  | R |  | R/W | 
Rx Address Selector Control Register
Register is at address HyperLinkCfgBase + 0x2c. For 6678, that is 0x2140_002c
If using HyperLink LLD, hyplnkRXAddrSelReg_s represents this register
Address Translation: Rx Side Registers
Register Configuration
rxsechi, rxseclo, and rxsecsel are all zero
rxprividsel = 12 (Bits 31 to 28)
rxsegsel = 9 (bits 30 to 25)

## Slide 30: Hyperlink Look-up Table
Each Shannon core will have 8 lines in the look-up table (there are 64 lines in each Hyperlink, and 8 cores)
4 lines point to 4 segment of remote memory, 32MB memory each, fifth segment is the MSMC memory
The last 3 lines are empty (can configure to non-existing memory to prevent non-core masters access to the 66AK2H12)
Translation from logical addresses to physical addresses will be done by the 66AK2H12 Hyperlink MPAX registers (set E)

## Slide 31: Hyperlink Look-up Table Shannon 0
Line (index) | CorePac | Logical base Address | Size | Purpose
000000 to line 000111 | 0 | 0x8000 0000, 0x8200 0000 0x8400 0000 0x8600 0000 0x0c00 0000 | 24 (32MB) for the first 4 segments, 21 (4MB) for the last segment dedicated to IPC | First 4 segment are for data copy and will be mapped to DDR physical memory by SES MPAX, last segment
000000 to line 001111 | 1 | 0x8000 0000, 0x8200 0000 0x8400 0000 0x8600 0000 0x0c00 0000 | 24 (32MB) for the first 4 segments, 21 (4MB) for the last segment dedicated to IPC | First 4 segment are for data copy and will be mapped to DDR physical memory by SES MPAX, last segment
000000 to line 010111 | 2 | 0x8000 0000, 0x8200 0000 0x8400 0000 0x8600 0000 0x0c00 0000 | 24 (32MB) for the first 4 segments, 21 (4MB) for the last segment dedicated to IPC | First 4 segment are for data copy and will be mapped to DDR physical memory by SES MPAX, last segment
000000 to line 011111 | 3 | 0x8000 0000, 0x8200 0000 0x8400 0000 0x8600 0000 0x0c00 0000 | 24 (32MB) for the first 4 segments, 21 (4MB) for the last segment dedicated to IPC | First 4 segment are for data copy and will be mapped to DDR physical memory by SES MPAX, last segment

## Slide 32: Hyperlink Look-up Table Shannon 0
000000 to line 100111 | 4 | 0x8000 0000, 0x8200 0000 0x8400 0000 0x8600 0000 0x0c00 0000 | 24 (32MB) for the first 4 segments, 21 (4MB) for the last segment dedicated to IPC | First 4 segment are for data copy and will be mapped to DDR physical memory by SES MPAX, last segment
000000 to line 101111 | 5 | 0x8000 0000, 0x8200 0000 0x8400 0000 0x8600 0000 0x0c00 0000 | 24 (32MB) for the first 4 segments, 21 (4MB) for the last segment dedicated to IPC | First 4 segment are for data copy and will be mapped to DDR physical memory by SES MPAX, last segment
000000 to line 110111 | 6 | 0x8000 0000, 0x8200 0000 0x8400 0000 0x8600 0000 0x0c00 0000 | 24 (32MB) for the first 4 segments, 21 (4MB) for the last segment dedicated to IPC | First 4 segment are for data copy and will be mapped to DDR physical memory by SES MPAX, last segment
000000 to line 111111 | 7 | 0x8000 0000, 0x8200 0000 0x8400 0000 0x8600 0000 0x0c00 0000 | 24 (32MB) for the first 4 segments, 21 (4MB) for the last segment dedicated to IPC | First 4 segment are for data copy and will be mapped to DDR physical memory by SES MPAX, last segment

## Slide 33: Hyperlink Look-up Table Shannon 1
Line (index) | CorePac | Logical base Address | Size | Purpose
000000 to line 000111 | 0 | 0xc000 0000, 0xc200 0000 0xc400 0000 0xc600 0000 0x0c00 0000 | 24 (32MB) for the first 4 segments, 21 (4MB) for the last segment dedicated to IPC | First 4 segment are for data copy and will be mapped to DDR physical memory by SES MPAX, last segment
000000 to line 001111 | 1 | 0xc000 0000, 0xc200 0000 0xc400 0000 0xc600 0000 0x0c00 0000 | 24 (32MB) for the first 4 segments, 21 (4MB) for the last segment dedicated to IPC | First 4 segment are for data copy and will be mapped to DDR physical memory by SES MPAX, last segment
000000 to line 010111 | 2 | 0xc000 0000, 0xc200 0000 0xc400 0000 0xc600 0000 0x0c00 0000 | 24 (32MB) for the first 4 segments, 21 (4MB) for the last segment dedicated to IPC | First 4 segment are for data copy and will be mapped to DDR physical memory by SES MPAX, last segment
000000 to line 011111 | 3 | 0xc000 0000, 0xc200 0000 0xc400 0000 0xc600 0000 0x0c00 0000 | 24 (32MB) for the first 4 segments, 21 (4MB) for the last segment dedicated to IPC | First 4 segment are for data copy and will be mapped to DDR physical memory by SES MPAX, last segment

## Slide 34: Hyperlink Look-up Table Shannon 1
000000 to line 100111 | 4 | 0xc000 0000, 0xc200 0000 0xc400 0000 0xc600 0000 0x0c00 0000 | 24 (32MB) for the first 4 segments, 21 (4MB) for the last segment dedicated to IPC | First 4 segment are for data copy and will be mapped to DDR physical memory by SES MPAX, last segment
000000 to line 101111 | 5 | 0xc000 0000, 0xc200 0000 0xc400 0000 0xc600 0000 0x0c00 0000 | 24 (32MB) for the first 4 segments, 21 (4MB) for the last segment dedicated to IPC | First 4 segment are for data copy and will be mapped to DDR physical memory by SES MPAX, last segment
000000 to line 110111 | 6 | 0xc000 0000, 0xc200 0000 0xc400 0000 0xc600 0000 0x0c00 0000 | 24 (32MB) for the first 4 segments, 21 (4MB) for the last segment dedicated to IPC | First 4 segment are for data copy and will be mapped to DDR physical memory by SES MPAX, last segment
000000 to line 111111 | 7 | 0xc000 0000, 0xc200 0000 0xc400 0000 0xc600 0000 0x0c00 0000 | 24 (32MB) for the first 4 segments, 21 (4MB) for the last segment dedicated to IPC | First 4 segment are for data copy and will be mapped to DDR physical memory by SES MPAX, last segment

## Slide 35: C6678 Hyperlink Address structure