## Slide 1: MMI Applications Team October 2011
KeyStone C66x Multicore SoC Overview
Notes: 1
NEW

## Slide 2: KeyStone Overview
KeyStone Architecture
CorePac & Memory Subsystem
Interfaces and Peripherals
Coprocessors and Accelerators
Debug
Notes: NEW

## Slide 3: Enhanced DSP core
Preliminary Information under NDA - subject to change
100% upward object code compatible
4x performance improvement for multiply operation
32 16-bit MACs
Improved support for complex arithmetic and matrix computation
Native instructions for IEEE 754, SP&DP
Advanced VLIW architecture
2x registers
Enhanced floating-point add capabilities
100% upward object code compatible with C64x, C64x+, C67x and c67x+
Best of fixed-point and floating-point architecture for better system performance and faster time-to-market.
Advanced fixed-point instructions
Four 16-bit or eight 8-bit MACs
Two-level cache
SPLOOP and 16-bit instructions for smaller code size
Flexible level one memory architecture
iDMA for rapid data transfers between local memories
C66x ISA
C64x+
C64x
C67x
C67x+
FLOATING-POINT VALUE
FIXED-POINT VALUE
Performance improvement
C674x
Notes: 3

## Slide 4
1 to 8 Cores @ up to 1.25 GHz
MSMC
MSM
SRAM
64-Bit
DDR3 EMIF
Application-Specific
Coprocessors
Power
Management
Debug & Trace
Boot ROM
Semaphore
Memory Subsystem
Network Coprocessor
S
w
i
t
c
h
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
A
p
p
l
i
c
a
t
i
o
n
-
S
p
e
c
i
f
i
c
I
/
O
S
P
I
I
C
2
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Packet
Accelerator
Packet
DMA
Multicore Navigator
Queue
Manager
O
t
h
e
r
s
x3
Security
Accelerator
PLL
EDMA
x3
C66x™
CorePac
L1
P-Cache
L1
D-Cache
L2 Cache
HyperLink
TeraNet
KeyStone Device Features
C66x CorePac
  1 to 8 C66x Fixed/Floating-Point CorePac DSP Cores at up to 1.25 GHz
  Backward-compatible with C64x+ and C67x+ cores
  Fixed and Floating Point Operations
  RSA instruction set extensions
    Chip-rate processing (downlink & uplink)
    Reed-Muller decoding (CorePac 1 and 2 only)
Memory Subsystem
  Up to 1 MB Local L2 memory per core
  Up to 4 MB Multicore Shared Memory (MSM)
  Multicore Shared Memory Controller (MSMC)
  Boot ROM, DDR3-1600 MHz (64-bit)
Application-Specific Coprocessors
  2x TCP3d: Turbo Decoder
  TCP3e: Turbo Encoder
  2x FFT (FFT/IFFT and DFT/IDFT) Coprocessor
  4x VCP2 for voice channel decoding
Multicore Navigator
  Queue Manager
  Packet DMA
Network Coprocessor
  Packet Accelerator
  Security Accelerator
Interfaces
  High-speed Hyperlink bus
  4x Serial RapidIO Rev 2.1
  2x 10/100/1000 Ethernet SGMII ports w/ embedded switch
  2x PCIe Generation II
  Six-lane Antenna Interface (AIF2) for Wireless Applications
    WCDMA, WiMAX, LTE, GSM, TD-SCDMA, TD-LTE
    Up to 6.144-Gbps
  Additional Serials: I2C, SPI, GPIO, UART
Embedded Trace Buffer (ETB) & System Trace Buffer (STB)
Smart Reflex Enabled
40 nm High-Performance Process
Notes: 4
NEW

## Slide 5: CorePac & Memory Subsystem
1 to 8 Cores @ up to 1.25 GHz
MSMC
MSM
SRAM
64-Bit
DDR3 EMIF
Application-Specific
Coprocessors
Power
Management
Debug & Trace
Boot ROM
Semaphore
Memory Subsystem
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
A
p
p
l
i
c
a
t
i
o
n
-
S
p
e
c
i
f
i
c
I
/
O
S
P
I
I
C
2
Packet
DMA
Multicore Navigator
Queue
Manager
O
t
h
e
r
s
x3
Network Coprocessor
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Packet
Accelerator
Security
Accelerator
PLL
EDMA
x3
C66x™
CorePac
L1
P-Cache
L1
D-Cache
L2 Memory (cache/RAM)
HyperLink
TeraNet
1 to 8 C66x CorePac DSP Cores operating at up to 1.25 GHz
  Fixed and Floating Point Operations
  Code compatible with other C64x+ and C67x+ devices
L1 Memory can be partitioned as cache or SRAM
  32KB L1P per core
  32KB L1D per core
  Error Detection for L1P
  Memory Protection
Dedicated and Shared L2 Memory
  512 KB to 1 MB Local L2 per core
  2 to 4 MB Multicore Shared Memory (MSM)
  Multicore Shared Memory Controller (MSMC)
  Error detection and correction for all L2 memory
  MSM available to all cores and can be either program or data
Boot ROM
CorePac & Memory Subsystem
Notes: 5
NEW

## Slide 6: Memory Expansion
Memory Expansion
CorePac & Memory Subsystem
Multicore Shared Memory Controller (MSMC)
  Arbitrates CorePac and SoC master access to shared memory
  Provides a direct connection to the DDR3 EMIF
  Provides CorePac access to coprocessors and IO peripherals
  Memory protection and address extension to 64 GB (36 bits)
  Provides multi-stream pre-fetching capability
DDR3 External Memory Interface (EMIF)
  Support for 1x 16-bit, 1x 32-bit, and 1x 64-bit modes
  Supports up to 1600 MHz
  Supports power down of unused pins when using 16-bit or 32-bit width
  Support for 8 GB memory address
  Error detection and correction
EMIF-16 (Media Applications Only)
  Three modes:
    Synchronized SRAM
    NAND flash
    NOR flash
  Can be used to connect asynchronous memory (e.g., NAND flash) up to 256 MB.
1 to 8 Cores @ up to 1.25 GHz
MSMC
MSM
SRAM
64-Bit
DDR3 EMIF
Application-Specific
Coprocessors
Power
Management
Debug & Trace
Boot ROM
Semaphore
Memory Subsystem
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
A
p
p
l
i
c
a
t
i
o
n
-
S
p
e
c
i
f
i
c
I
/
O
S
P
I
I
C
2
Packet
DMA
Multicore Navigator
Queue
Manager
O
t
h
e
r
s
x3
Network Coprocessor
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Packet
Accelerator
Security
Accelerator
PLL
EDMA
x3
C66x™
CorePac
L1
P-Cache
L1
D-Cache
L2 SRAM
HyperLink
TeraNet
Notes: 6
NEW

## Slide 7: Multicore Navigator
Queue Manager and Packet DMA
Low-overhead processing and routing of packet traffic
Simplified resource management
Effective inter-processor communications
Abstracts physical implementation from application host software
Virtualization to enable dynamic load balancing and provide seamless access to resources on different cores
8K hardware queues and 16K descriptors
  More descriptors can reside in any shared memory
10 Gbps pre-fetching capability
Memory Expansion
Multicore Navigator
CorePac & Memory Subsystem
1 to 8 Cores @ up to 1.25 GHz
MSMC
MSM
SRAM
64-Bit
DDR3 EMIF
Application-Specific
Coprocessors
Power
Management
Debug & Trace
Boot ROM
Semaphore
Memory Subsystem
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
A
p
p
l
i
c
a
t
i
o
n
-
S
p
e
c
i
f
i
c
I
/
O
S
P
I
I
C
2
Packet
DMA
Multicore Navigator
Queue
Manager
O
t
h
e
r
s
x3
Network Coprocessor
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Packet
Accelerator
Security
Accelerator
PLL
EDMA
x3
C66x™
CorePac
L1
P-Cache
L1
D-Cache
L2 SRAM
HyperLink
TeraNet
Notes: 7
NEW

## Slide 8: Network Coprocessor
Packet Accelerator (PA)
  Support for single or multiple IP addresses
  1 Gbps wire-speed throughput at 1.5 Mpps
  UDP Checksum processing
  IPSec ESP and AH tunnels with fast path fully offloaded
  L2 support: Ethernet, Ethertype, and VLAN
  L3/L4 Support: IPv4/IPv6 and UDP port-based raw Ethernet or IPv4/6 and SCTP port-based routing
  Multicast to multiple queues
  QoS capability: Per channel/flow to individual queue towards DSP cores and support for TX traffic shaping per device
Security Accelerator (SA)
  Support for IPSec, SRTP, 3GPP and WiMAX Air Interface, and SSL/TLS security
  Support for simultaneous wire-speed security processing on 1 Gbps Ethernet transmit and receive traffic.
  Encryption Modes: ECB, CBC, CTR, F8, A5/3, CCM, GCM, HMAC, CMAC, and GMAC
  Encryption Algorithms: AES, DES, 3DES, Kasumi, SNOW 3g, SHA-1, SHA-2, and MD5
Memory Expansion
Multicore Navigator
CorePac & Memory Subsystem
Network Coprocessor
1 to 8 Cores @ up to 1.25 GHz
MSMC
MSM
SRAM
64-Bit
DDR3 EMIF
Application-Specific
Coprocessors
Power
Management
Debug & Trace
Boot ROM
Semaphore
Memory Subsystem
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
A
p
p
l
i
c
a
t
i
o
n
-
S
p
e
c
i
f
i
c
I
/
O
S
P
I
I
C
2
Packet
DMA
Multicore Navigator
Queue
Manager
O
t
h
e
r
s
x3
Network Coprocessor
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Packet
Accelerator
Security
Accelerator
PLL
EDMA
x3
C66x™
CorePac
L1
P-Cache
L1
D-Cache
L2 SRAM
HyperLink
TeraNet
Notes: 8
NEW

## Slide 9: External Interfaces
SGMII allows two 10/100/1000 Ethernet interfaces
Four high-bandwidth Serial RapidIO (SRIO) lanes for inter-DSP applications
SPI for boot operations
UART for development/testing
Two PCIe at 5 Gbps
I2C for EPROM at 400 Kbps
Application-specific Interfaces:
  Antenna Interface 2 (AIF2) for wireless applications
  Telecommunications Serial Port (TSIP) x2 for media applications
Memory Expansion
Multicore Navigator
CorePac & Memory Subsystem
External Interfaces
Network Coprocessor
1 to 8 Cores @ up to 1.25 GHz
MSMC
MSM
SRAM
64-Bit
DDR3 EMIF
Application-Specific
Coprocessors
Power
Management
Debug & Trace
Boot ROM
Semaphore
Memory Subsystem
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
A
p
p
l
i
c
a
t
i
o
n
-
S
p
e
c
i
f
i
c
I
/
O
S
P
I
I
C
2
Packet
DMA
Multicore Navigator
Queue
Manager
O
t
h
e
r
s
x3
Network Coprocessor
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Packet
Accelerator
Security
Accelerator
PLL
EDMA
x3
C66x™
CorePac
L1
P-Cache
L1
D-Cache
L2 SRAM
HyperLink
TeraNet
Notes: 9
NEW

## Slide 10: TeraNet Switch Fabric
1 to 8 Cores @ up to 1.25 GHz
MSMC
MSM
SRAM
64-Bit
DDR3 EMIF
Application-Specific
Coprocessors
Power
Management
Debug & Trace
Boot ROM
Semaphore
Memory Subsystem
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
A
p
p
l
i
c
a
t
i
o
n
-
S
p
e
c
i
f
i
c
I
/
O
S
P
I
I
C
2
Packet
DMA
Multicore Navigator
Queue
Manager
O
t
h
e
r
s
x3
Network Coprocessor
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Packet
Accelerator
Security
Accelerator
PLL
EDMA
x3
C66x™
CorePac
L1
P-Cache
L1
D-Cache
L2 Cache
HyperLink
TeraNet
TeraNet is a process controller
  Channel Controller
  Transfer Controller
TeraNet provides a configured way – within hardware – to manage traffic queues and ensure priority jobs are getting accomplished while minimizing the involvement of the DSP cores.
TeraNet facilitates high-bandwidth communications between CorePac cores, subsystems, peripherals, and memory.
TeraNet Switch Fabric
Memory Expansion
Multicore Navigator
CorePac & Memory Subsystem
External Interfaces
Network Coprocessor
Notes: 10
NEW

## Slide 11: Diagnostic Enhancements
Embedded Trace Buffers (ETB) enhance the diagnostic capabilities of the CorePac.
CP Monitor enables diagnostic capabilities on data traffic through the TeraNet switch fabric.
Automatic statistics collection and exporting (non-intrusive)
Monitor individual events for better debugging
Monitor transactions to both memory end point and MMRs (memory mapped Regi)
Configurable monitor filtering capability based on address and transaction type
Diagnostic Enhancements
TeraNet Switch Fabric
Memory Expansion
Multicore Navigator
CorePac & Memory Subsystem
External Interfaces
Network Coprocessor
1 to 8 Cores @ up to 1.25 GHz
MSMC
MSM
SRAM
64-Bit
DDR3 EMIF
Application-Specific
Coprocessors
Power
Management
Debug & Trace
Boot ROM
Semaphore
Memory Subsystem
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
A
p
p
l
i
c
a
t
i
o
n
-
S
p
e
c
i
f
i
c
I
/
O
S
P
I
I
C
2
Packet
DMA
Multicore Navigator
Queue
Manager
O
t
h
e
r
s
x3
Network Coprocessor
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Packet
Accelerator
Security
Accelerator
PLL
EDMA
x3
C66x™
CorePac
L1
P-Cache
L1
D-Cache
L2 Cache
HyperLink
TeraNet
Notes: 11
NEW

## Slide 12: HyperLink Bus
Provides the capability to expand the C66x to include hardware acceleration or other auxiliary processors
Four lanes with up to 12.5 Gbps per lane
HyperLink Bus
Diagnostic Enhancements
TeraNet Switch Fabric
Memory Expansion
Multicore Navigator
CorePac & Memory Subsystem
External Interfaces
Network Coprocessor
1 to 8 Cores @ up to 1.25 GHz
MSMC
MSM
SRAM
64-Bit
DDR3 EMIF
Application-Specific
Coprocessors
Power
Management
Debug & Trace
Boot ROM
Semaphore
Memory Subsystem
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
A
p
p
l
i
c
a
t
i
o
n
-
S
p
e
c
i
f
i
c
I
/
O
S
P
I
I
C
2
Packet
DMA
Multicore Navigator
Queue
Manager
O
t
h
e
r
s
x3
Network Coprocessor
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Packet
Accelerator
Security
Accelerator
PLL
EDMA
x3
C66x™
CorePac
L1
P-Cache
L1
D-Cache
L2 Cache
HyperLink
TeraNet
Notes: 12
NEW

## Slide 13: Miscellaneous Elements
Semaphore2 provides atomic access to shared chip-level resources.
Boot ROM
Power Management
Eight 64-bit timers
Three on-chip PLLs:
  PLL1 for CorePacs
  PLL2 for DDR3
  PLL3 for Packet Acceleration
Three EDMA
Miscellaneous
HyperLink Bus
Diagnostic Enhancements
TeraNet Switch Fabric
Memory Expansion
Multicore Navigator
CorePac & Memory Subsystem
External Interfaces
Network Coprocessor
1 to 8 Cores @ up to 1.25 GHz
MSMC
MSM
SRAM
64-Bit
DDR3 EMIF
Application-Specific
Coprocessors
Power
Management
Debug & Trace
Boot ROM
Semaphore
Memory Subsystem
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
A
p
p
l
i
c
a
t
i
o
n
-
S
p
e
c
i
f
i
c
I
/
O
S
P
I
I
C
2
Packet
DMA
Multicore Navigator
Queue
Manager
O
t
h
e
r
s
x3
Network Coprocessor
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Packet
Accelerator
Security
Accelerator
PLL
EDMA
x3
C66x™
CorePac
L1
P-Cache
L1
D-Cache
L2 Cache
HyperLink
TeraNet
Notes: 13
NEW

## Slide 14: Device-Specific: Wireless Applications
Miscellaneous
HyperLink Bus
Diagnostic Enhancements
TeraNet Switch Fabric
Memory Expansion
Multicore Navigator
CorePac & Memory Subsystem
External Interfaces
Network Coprocessor
Device-Specific (Wireless Apps)
Application-Specific Coprocessors
Wireless-specific Coprocessors
  FFTC
  TCP3 Decoder/Encoder
  VCP2
  BCP
Wireless-specific Interfaces: AIF2 x6
Characteristics
  Package Size: 24x24
  Process Node: 40nm
  Pin Count: 841
  Core Voltage: 0.9-1.1 V
2x Rake Search Accelerator (RSA)
4 Cores @ 1.0 GHz / 1.2 GHz
C66x™
CorePac
FFTC
TCP3d
KeyStone Device Architecture
for Wireless Applications
MSMC
2MB
MSM
SRAM
64-Bit
DDR3 EMIF
TCP3e
x2
x2
Coprocessors
VCP2
x4
Power
Management
Debug & Trace
Boot ROM
Semaphore
Memory Subsystem
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
A
I
F
2
x6
S
P
I
I
C
2
Packet
DMA
Multicore Navigator
Queue
Manager
O
t
h
e
r
s
x3
32KB L1
P-Cache
32KB L1
D-Cache
1024KB L2 Cache
RSA
RSA
x2
PLL
EDMA
x3
HyperLink
TeraNet
Network Coprocessor
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
2
´
Packet
Accelerator
Security
Accelerator
BCP
Notes: 14
NEW

## Slide 15: Device-Specific: Media Applications
Miscellaneous
HyperLink Bus
Diagnostic Enhancements
TeraNet Switch Fabric
Memory Expansion
Multicore Navigator
CorePac & Memory Subsystem
External Interfaces
Network Coprocessor
Device-Specific (Media Apps)
Media-specific Interfaces
  TSIP x2
  EMIF 16 (EMIF-A)
Characteristics
  Package Size: 24x24
  Process Node: 40nm
  Pin Count: 841
  Core Voltage: 0.9-1.1 V
Application-Specific Coprocessors
1 to 8 Cores @ up to 1.25 GHz
Power
Management
Debug & Trace
Boot ROM
Semaphore
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
T
S
I
P
x2
S
P
I
I
C
2
Packet
DMA
Multicore Navigator
Queue
Manager
G
P
I
O
x3
PLL
EDMA
x3
E
M
I
F
1
6
KeyStone Device
Architecture for
Media Applications
4MB
MSM
SRAM
64-Bit
DDR3 EMIF
Memory Subsystem
MSMC
C66x™
CorePac
32KB L1
P-Cache
32KB L1
D-Cache
512KB L2 Cache
TeraNet
HyperLink
TeraNet
Network Coprocessor
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Packet
Accelerator
Security
Accelerator
Notes: 15
NEW

## Slide 16: KeyStone Overview
KeyStone Architecture
CorePac & Memory Subsystem
Interfaces and Peripherals
Coprocessors and Accelerators
Debug
Notes: NEW

## Slide 17: KeyStone Memory Topology
L1D – 32KB Cache/SRAM
L1P – 32KB Cache/SRAM
L2 - Cache/SRAM – 0.5MB
MSM – Shared SRAM 4MB
DDR3 – Up to 8GB
L1D & L1P Cache Options – 0KB, 4KB, 8KB, 16K or 32KB
L2 Cache Options – 0KB, 32KB, 64KB, 128KB, 256KB, 512KB
DDR3 (1x64b)
MSMC
IP1
IP2
IPn
L1D
L1D
L1P
L1P
L2
L2
TeraNet
New C66x CorePac
256
256
256
256
256
MSMC SRAM
New C66x CorePac
L1D
L1P
L2
New C66x CorePac
256
L1D
L1P
L2
New C66x CorePac
256
256
256

## Slide 18: MSMC Block Diagram
CorePac
2
Shared RAM
,
2048
KB
CorePac
Slave Port
CorePac
Slave Port
System
Slave Port
for shared
SRAM
(
SMS
)
System Slave Port for external memory
(
SES
)
MSMC System
Master Port
MSMC EMIF
Master Port
MSMC Datapath
Arbitration
256
256
256
Memory
Protection
and
Extension
Unit
(
MPAX
)
256
256
events
Memory
Protection
and
Extension
Unit
(
MPAX
)
MSMC Core
EMIF
–
64
bit
DDR
3
Teranet
TeraNet
256
EDC
256
256
256
CorePac
Slave Port
CorePac
Slave Port
256
256
XMC
MPAX
CorePac
3
XMC
MPAX
CorePac
0
XMC
MPAX
CorePac
1
XMC
MPAX

## Slide 19: C66 TeraNet Data Connections
QMSS
MSMC
DDR3
Shared L2
S
S
Core
S
PCIe
S
TAC_BE
S
SRIO
PCIe
QM_SS
M
M
M
TPCC
16ch QDMA
M
TC0
M
TC1
M
M
DDR3
XMC
M
DebugSS
M
TPCC
64ch
QDMA
M
TC2
M
TC3
M
TC4
M
TC5
TPCC
64ch
QDMA
M
TC6
M
TC7
M
TC8
M
TC9
Network
Coprocessor
M
HyperLink
M
HyperLink
S
AIF / PktDMA
M
FFTC / PktDMA
M
RAC_BE0,1
M
TAC_FE
M
SRIO
S
S
RAC_FE
S
TCP3d
S
TCP3e_W/R
S
VCP2 (x4)
S
…
M
EDMA_0
EDMA_1,2
Core
S
M
Core
S
M
L2 0-3
S
M
C6616 TeraNet facilitates high Bandwidth communication links between DSP cores, subsystems, peripherals, and memories.
TeraNet supports parallel orthogonal communication links
In order to evaluate the potential communication link throughput, consider the peripheral bit-width and the speed of TeraNet
Please note that while most of the communication links are possible, some of them are not, or are supported by particular Transfer Controllers. Details are provided in the C6616 Data Manual
CPUCLK/2
256bit TeraNet
FFTC / PktDMA
M
TCP3d
S
RAC_FE
S
VCP2 (x4)
S
VCP2 (x4)
S
VCP2 (x4)
S
RAC_BE0,1
M
CPUCLK/3
128bit TeraNet
S
S
S
S
Notes: CPT see physical addresses. In MSMC, one CPT per bank.

## Slide 20: TeraNet Switch Fabric
Preliminary Information under NDA - subject to change
Legend
x2
x4
x4
QM_SS
MSMC Subsystem
CPU/2
256b
TeraNet
SCR
M3_DDR
M3_SL2
CPU/3
128b
TeraNet
SCR
S
S
CorePac
S
1x to 8x
PCIe
S
SRIO
PCIe
QM_SS
M
M
M
TPCC
16ch QDMA
M
TC0
M
TC1
M
M
DDR3
S
XMC
x1 to x8
M
CPU / 6
32b
TeraNet
SCR
EMIF16
Boot ROM
SPI
S
S
S
DAP (DebugSS)
M
TPCC
64ch
QDMA
M
TC2
M
TC3
M
TC4
M
TC5
TPCC
64ch
QDMA
M
TC6
M
TC7
M
TC8
M
TC9
CPU/3
32b
TeraNet
SCR
CPU/6
32b
TeraNet
SCR
PA/SA
M
x2
TSIP0,1
M
FFTC
SRIO
S
PA/SA
S
TSIP
S
AIF2
S
VCP2
S
TCP3D
S
TCP3E
S
S
x4
x2
CP Tracer (x8)
S
x8
HyperLink
M
S
S
TPCC
TPTC
S
S
TPCC
TPTC
S
S
TPCC
TPTC
SCR
CPU /2
SCR
CPU / 3
SCR
CPU / 3
Timer
S
GPIO
S
I2C
S
INTC
S
UART
S
x8 / x16
SEC_CTL
S
PLL_CTL
S
Global
Timestamp
Bootcfg
S
HyperLink
S
Media Apps Only
Wireless Apps Only
AIF / DMA
M
FFTC / DMA
M
SRIO
S
S
CPU / 3
32b
TeraNet
SCR
MPU
TCP3E
S
TCP3e_W/R
S
CPU / 3
128b SCR
VCP2 (x4)
S
MPU
Semaphore
S
MPU
QMSS
S
MPU
TETB
S
STM
TETB
S
DebugSS
S
…
CONFIG
CPU/3
32b
Write-only
TeraNet
SCR
CP Tracer (x5)
M
CP Tracer (x8)
M
CP Tracer (x7)
M
DebugSS
STM
TETB
S
S
Bridge
CP Tracer (x7)
S
CP Tracer (x5)
S
x5
CPU/3
32b
TeraNet
SCR
x7
M
Bridge 12
Bridge 13
Bridge 14
EDMA_0
EDMA_1,2
Notes: 20
NEW

## Slide 21: Multicore Navigator Overview
Multicore Navigator
  Purpose - seamless inter-core communications between cores, IP and peripherals. “Fire and forget”
  Supports synchronization between cores, move data between cores, move data to and from peripherals
  Consists of a Queue Manager and multiple, dedicated Packet DMA engines
  Data transfer architecture designed to minimize host interaction while maximizing memory and bus efficiency
  Move Descriptors and buffers (or pointers to) between different parts of the Chip
Navigator hardware:
  Queue Manager Subsystem (QMSS)
  Multiple Packet DMA (PKTDMA)
Notes: NEW

## Slide 22: Navigator Architecture

## Slide 23: Queue Manager Subsystem (QMSS)
Features:
  8192 total hardware queues
  Up to 20 Memory regions for descriptor storage (LL2, MSMC, DDR)
  Up to 2 Linking RAMs for queue linking/management
    Up to 16K descriptors can be handled by internal Link RAM.
    Second Link RAM can be placed in L2 or DDR.
  Up to 512K descriptors supported in total.
  Can copy descriptor pointers of transferred data to destination core’s local memory to reduce access latency
Major hardware components:
  Queue Manager
  PKTDMA (Infrastructure DMA)
  2 PDSPs (Packed Data Structure Processors) for:
    Descriptor Accumulation / Queue Monitoring
    Load Balancing and Traffic Shaping
  Interrupt Distributor (INTD) module

## Slide 24: Packet DMA Topology
PKTDMA
PKTDMA
PKTDMA
PKTDMA
PKTDMA
PKTDMA
Queue Manager
SRIO
Network
Coprocessor
FFTC (A)
AIF
8192
5
4
3
2
1
0
.
.
.
Queue Manager Subsystem
Multiple Packet DMA instances in KeyStone devices:
  QMSS, PA and SRIO instances for all KeyStone devices.
  AIF2 and FFTC (A and B) instances are only in KeyStone devices for wireless applications.
Transfer engine interface between peripherals/accelerators and QMSS
Autonomously determines memory buffers to fill and queues to post based on initial setup and buffer descriptor
FFTC (B)
Notes: NEW

## Slide 25: Queues/Descriptors/Packets
PTR
PTR
PTR
PTR
.
.
.
Host Packet
Descriptor
PTR
Length
...
Host Buffer
Descriptor
PTR
Length
...
Data
Data
Monolithic
Descriptor
Length
...
Data
Queue
Notes: REUSABLE – nothing here needs to be rerecorded

## Slide 26: XMC – External Memory Controller
The XMC is responsible for:
Address extension/translation
Memory protection for addresses outside C66x
Shared memory access path
Cache and Pre-fetch support
User Control of XMC:
MPAX registers – Memory Protection and Extension Registers
MAR registers – Memory attributes registers
Each core has its own set of MPAX and MAR registers !

## Slide 27: The MPAX Registers
Translate between physical and logical address
16 registers (64 bits each) control (up to) 16 memory segments.
Each register translates logical memory into physical memory for the segment.
Segment definition in the MPAX registers:
  Segment size – 5 bits – power of 2, smallest segment size 4K, up to 4GB
  Logical base address –
  Physical (replacement address) base
  Permission – access type allowed in this address range

## Slide 28: The MAR Registers
MAR = Memory Attributes Registers
256 registers (32 bits each) control 256 memory segments.
  Each segment size is 4M Bytes, from logical address 0x00000000 to address 0xffffffff
  The first 16 registers are read-only. They control the internal memory of the core.
Each register controls the cache-ability of the segment (bit 0) and the pre-fetch-ability (bit 3). All other bits are reserved and set to 0.
All MAR bits are set to zero after reset.

## Slide 29: KeyStone Overview
KeyStone Architecture
CorePac & Memory Subsystem
Interfaces and Peripherals
Coprocessors and Accelerators
Debug
Notes: NEW

## Slide 30: EDMA
3 EDMA Channel Controllers
1 controller in CPU/2 domain
  2 transfer controllers/queues with 1KB channel buffer
  8 QDMA channels
  16 interrupt channels
  128 PaRAM entries
2 controllers in CPU/3 domain each with
  4 transfer controllers/queues with 1KB or 512B channel buffer
  8 QDMA channels
  64 interrupt channels
  512 PaRAM entries
Flexible transfer definition
  Linking mechanism allows automatic PaRAM set update
  Chaining allows multiple transfers to execute with one event
Interrupt generation
  Transfer completion
  Error conditions
510
511

## Slide 31: Interfaces Overview
Two SGMII ports with embedded switch
  Supports IEEE1588 timing over Ethernet
  Supports 1G/100 Mbps full duplex
  Supports 10/100 Mbps half duplex
  Inter-working with RapidIO message
  Integrated with packet accelerator for efficient IPv6 support
  Supports jumbo packets (9 Kb)
  Three-port embedded Ethernet switch with packet forwarding
  Reset isolation with SGMII ports and embedded ETH switch
HyperLink bus
  Hardware hooks for analog device or customer ASIC
Application-Specific Interfaces
For Wireless Applications
Antenna Interface 2 (AIF2)
  Multiple-standard support (WCDMA, LTE, WiMAX, GSM/Edge)
  Generic packet interface (~12Gbits/sec ingress & egress)
  Frame Sync module (adapted for WiMAX, LTE & GSM slots/frames/symbols boundaries)
  Reset Isolation
For Media Gateway Applications
Telecommunications Serial Port (TSIP)
  Two TSIP ports for interfacing TDM applications
  Supports 2/4/8 lanes at 32.768/16.384/8.192 Mbps per lane & up to 1024 DS0s
Common Interfaces
One PCI Express (PCIe) Gen II port
  Two lanes running at 5G Baud
  Support for root complex (host) mode and end point mode
  Single Virtual Channel (VC) and up to eight Traffic Classes (TC)
  Hot plug
Universal Asynchronous Receiver/Transmitter (UART)
  2.4, 4.8, 9.6, 19.2, 38.4, 56, and 128 K baud rate
Serial Port Interface (SPI)
  Operate at up to 66 MHz
  Two-chip select
  Master mode
Inter IC Control Module (I2C)
  One for connecting EPROM (up to 4Mbit)
  400 Kbps throughput
  Full 7-bit address field
General Purpose IO (GPIO) module
  16-bit operation
  Can be configured as interrupt pin
  Interrupt can select either rising edge or falling edge
Serial RapidIO (SRIO)
  RapidIO 2.1 compliant
  Four lanes @ 5 Gbps
    1.25/2.5/3.125/5 Gbps operation per lane
    Configurable as four 1x, two 2x, or one 4x
  Direct I/O and message passing (VBUSM slave)
  Packet forwarding
  Improved support for dual-ring daisy-chain
  Reset isolation
  Upgrades for inter-operation with packet accelerator
Notes: 31
MOSTLY REUSABLE (PCIe, UART, SPI, I2C, GPIO, SRIO, SGMII) – Need new audio for HyperLink and Application-specific I/O >> AIF2 and TSIP

## Slide 32: Ethernet Switch: Overview
3 Port Ethernet Switch
  Port 0: CPPI port
  Port 1: SGMII 0 Port
  Port 2: SGMII 1 Port
Ethernet Switch Modules
  2 EMAC modules
  Address Lookup Engine (ALE) module
  2 Statistics modules
  CPTS (connect Port TS) module
The PA will be discussed later

## Slide 33: RapidIO
SRIO or RapidIO provides a 3-Layered Architecture
  Physical defines electrical characteristics, link flow control (CRC)
  Transport defines addressing scheme (8b/16b device IDs)
  Logical defines packet format and operational protocol
2 Basic Modes of Logical Layer Operation
  DirectIO
    Transmit Device needs knowledge of memory map of Receiving Device
    Includes NREAD, NWRITE_R, NWRITE, SWRITE
    Functional units: LSU, MAU, AMU
  Message Passing
    Transmit Device does not need knowledge of memory map of Receiving Device
    Includes Type 11 Messages and Type 9 Packets
    Functional units: TXU, RXU
Gen 2 Implementation – Supporting up to 5 Gbps

## Slide 34: PCIe Interface
KeyStone incorporates a single PCIe interface with the following characteristics:
  Two SERDES lanes running at 5 GBaud/2.5GBaud
  Gen2 compliant
  Three different operational modes (default defined by pin inputs at power up; can be overwritten by software):
    Root Complex (RC)
    End Point (EP)
    Legacy End Point
  Single Virtual Channel (VC)
  Single Traffic Class (TC)
  Maximum Payloads
    Egress – 128 bytes
    Ingress – 256 bytes
  Configurable BAR filtering, IO filtering, and configuration filtering

## Slide 35: HyperLink Bus
Provides a high-speed interface between device interfaces through the TeraNet switch fabric.
A single 4x bus operating at up to 12.5 Gbps per lane
Connections are point-to-point.
Device #1
TeraNet Switch Fabric
Device #2
TeraNet Switch Fabric
HyperLink
Notes: 35
NEW

## Slide 36: AIF 2.0
AIF2 is a peripheral module that supports data transfers between uplink and downlink baseband processors through a high-speed serial interface. AIF2 directly supports the following:
  WCDMA/FDD
  LTE FDD
  LTE TDD
  WiMax
  TD-SCDMA
  GSM/Edge (OBSAI only)Autonomous DMA
PKTDMA or AIF VBUS Master
More efficient data transfer for OFDM standards
FIFO-based buffer provides flexible support for various sampling frequencies.
Notes: 36
NEW

## Slide 37: AIF2 Module Architecture
PHY layer {SD, RM, CI, RT, CO, TM, AT}
Protocol layer {PD, PE, DB}
DMA layer {AD, CDMA}

## Slide 38: Other Peripherals & System Elements (1/3)
TSIP
  Supports 1024 DS0s per TSIP
  Supports 2/4/8 lanes at 32.768/16.384/8.192 Mbps per lane
UART Interface – Operates at up to 128,000 baud
I2C Interface
  Supports 400Kbps throughput
  Supports full 7-bit address field
  Supports EEPROM size of 4 Mbit
SPI Interface
  Operates at up to 66 MHz
  Supports two chip selects
  Support master mode
GPIO Interface
  16 GPIO pins
  Can be configured as interrupt pins
  Interrupt can select either rising edge or falling edge

## Slide 39: Other Peripherals & System Elements (2/3)
EMIF16
  Used for booting, logging, announcement, etc.
  Supports NAND flash memory, up to 256MB
  Supports NOR flash up to 16MB
  Supports asynchronous SRAM mode, up to 1MB
64-Bit Timers
  Total of 16 64-bit timers
    One 64-bit timer per core is dedicated to serve as a watchdog (or may be used as a general purpose timer)
    Eight 64-bit timers are shared for general purpose timers
  Each 64-bit timer can be configured as two individual 32-bit timers
  Timer Input/Output pins
    Two timer Input pins
    Two timer Output pins
    Timer input pins can be used as GPI
    Timer output pins can be used as GPO
On-Chip PLLs
  Core
  Packet & Security CoProcessors
  DDR

## Slide 40: Other Peripherals & System Elements (3/3)
Hardware Semaphores: 8 master and 32 shared resources
Power Management
Support to assert NMI input for each core – separate hardware pins for NMI and core selector
Support for local reset for each core – separate hardware pins for local reset and core selector

## Slide 41: KeyStone Overview
KeyStone Architecture
CorePac & Memory Subsystem
Interfaces and Peripherals
Coprocessors and Accelerators
Debug
Notes: NEW

## Slide 42: Network and Security Coprocessor Overview
Packet Accelerator (PA)
  Deciphers and adds protocol headers to (and from) packets.
  Standard protocols and limited user’s defined protocol routing
Security Accelerator (SA)
  Encrypts and decrypts packages
Notes: NEW

## Slide 43: Network Coprocessor (Logical)
Classify
Pass 1
Lookup Engine
(IPSEC16 entries, 32 IP, 16 Ethernet)
DSP 0
Ethernet TX MAC
Ethernet
RX MAC
PKTDMA Queue
QMSS FIFO Queue
Security Accelerator
(cp_ace)
TX PKTDMA
Modify
Classify
Pass 2
RX PKTDMA
Modify
Egress Path
Ingress Path
DSP 0
DSP 0
CorePac 0
Ethernet TX MAC
SRIO message TX
SRIO message RX
Packet Accelerator
Notes: REUSABLE – nothing here needs to be rerecorded

## Slide 44: Session Identification
Hardware lookup identifies the session.
First-pass lookup:
  IPv4, IPv6, or Ethernet only
  64 entries (16 Ethernet, 32 up to IPv6, 16 up to IPSec)
  IP with ESP or AH as next protocol and SPI
Second-pass lookup:
  8192 entries
  UDP, SCTP, etc. or proprietary up to 32-bit identifier within the first 128 bytes of the packet
Notes: REUSABLE – nothing here needs to be rerecorded

## Slide 45: IP/UDP or Raw Ethernet/Flow ID
Classify
Pass 1
Lookup Engine
(IPSEC16 entries, 32 IP, 16 Ethernet)
DSP 0
Ethernet TX MAC
Ethernet
RX MAC
PKTDMA Queue
QMSS FIFO Queue
Security Accelerator
(cp_ace)
TX PKTDMA
Modify
Classify
Pass 2
RX PKTDMA
Modify
Egress Path
Ingress Path
DSP 0
DSP 0
CorePac 0
Ethernet TX MAC
SRIO message TX
Packet Accelerator
3. UDP checksum verified and result set in descriptor.
SRIO message RX
2. UDP port or proprietary session ID number matched.
1. No IP Sec detected, IPv6 address matched.
Notes: REUSABLE – nothing here needs to be rerecorded

## Slide 46: IPSec Flow (IP/UDP in IP/ESP)
Classify
Pass 1
Lookup Engine
(IPSEC16 entries, 32 IP, 16 Ethernet)
DSP 0
Ethernet TX MAC
Ethernet
RX MAC
PKTDMA Queue
QMSS FIFO Queue
Security Accelerator
(cp_ace)
TX PKTDMA
Modify
Classify
Pass 2
RX PKTDMA
Modify
Egress Path
DSP 0
DSP 0
CorePac 0
Ethernet TX MAC
SRIO message TX
SRIO message RX
Packet Accelerator
2. Authenticate, decrypt, and replay protection.
3. IPv6 address and UDP port or proprietary session ID number matched.
4. UDP checksum verified and result set in descriptor.
1. IP Sec detected and SPI matched against configured security contexts.
Ingress Path
Notes: REUSABLE – nothing here needs to be rerecorded

## Slide 47: IPSec Transmit Flow
Classify
Pass 1
Lookup Engine
(IPSEC16 entries, 32 IP, 16 Ethernet)
DSP 0
Ethernet TX MAC
Ethernet
RX MAC
PKTDMA Queue
QMSS FIFO Queue
Security Accelerator
(cp_ace)
TX PKTDMA
Modify
Classify
Pass 2
RX PKTDMA
Modify
Ingress Path
DSP 0
DSP 0
CorePac 0
Ethernet TX MAC
SRIO message TX
SRIO message RX
Packet Accelerator
1. Host SW builds payload and IP/ESP header.
3. Payload is encrypted and authentication tag is computed and stored in trailer.
2. UDP checksum calculated and result stored in IP header.
Egress Path
Notes: REUSABLE – nothing here needs to be rerecorded

## Slide 48: What is FFTC?
The FFTC is an accelerator that can be used to perform FFT and Inverse FFT (IFFT) on data.
The FFTC has been designed to be compatible with various OFDM-based wireless standards like WiMax and LTE.
The Packet DMA (PKTDMA) is used to move data in and out of the FFTC module.
The FFTC supports four input (Tx) queues that are serviced in a round-robin fashion.
Using the FFTC to perform computations that otherwise would have been done in software frees up CPU cycles for other tasks.

## Slide 49: FFTC Features
Provides algorithms for both FFT and IFFT
Multiple block sizes:
  Maximum 8192
  All LTE DFT (Long Term Evolution Discrete Fourier Transform) sizes
LTE 7.5 kHz frequency shift
16 bits I/ 16 bits Q input and output – block floating point output
Dynamic and programmable scaling modes
  Dynamic scaling mode returns block exponent
Support for left-right FFT shift (switch the left/right halves)
Support for variable FFT shift
  For OFDM (Orthogonal Frequency Division Multiplexing) downlink, supports data format with DC subcarrier in the middle of the subcarriers
Support for cyclic prefix
  Addition and removal
  Any length supported
Three-buffer design allows for back-to-back computations
128-bit, CPU/3, full-duplex VBUS connection
Input data scaling with shift eliminates the need for front-end digital AGC (Automatic Gain Control)
Output data scaling
Notes: 450-550 Msubcarriers/sec throughput
  222,000, 2048-FFTs per second or one, 2048-FFT every 4.5μs
80dB SNR

## Slide 50: FFTC Functional Block Diagram
B2 Configuration Register Set
FFT
Engine
Streaming Interface
Packet DMA
(PKTDMA)
B0
B1
B2
Ch3 Configuration Register Set
Ch2 Configuration Register Set
Ch1 Configuration Register Set
Ch0 Configuration Register Set
4 Sets
FREE_BUFFER
DATA
Handshaking
Signals
Peripheral Bus
D A T A
Channel-3
Interrupt
Channel-0
Interrupt
Channel-1
Interrupt
Channel-2
Interrupt
3 Sets
4 Sets
3 Sets
R
RW
RW
3 Sets
B1 Configuration Register Set
Scheduler
B0 Configuration Register Set

## Slide 51: Turbo CoProcessor 3 Decoder (TCP3D)
TCP3D is a programmable peripheral for decoding of 3GPP (WCDMA, HSUPA, HSUPA+, TD_SCDMA), LTE, and WiMax turbo codes.
Turbo decoding is a part of bit processing.
Decoded bits
De-Rate
Matching
LLR
combining
Channel
De-interleaver
TCP3D
De-Scrambling
LLR Data
Systematic
Parity 0
Parity 1
Hard decision
Per Transport Block
Per Code Block
LTE Bit Processing
TB CRC
Soft Bits
Notes: TCP turbo coprocessor
TCP3D is a programmable peripheral for decoding of 3GPP (WCDMA, HSUPA, HSUPA+, TD_SCDMA), LTE and WiMax turbo codes.
Turbo decoding is a part of bit processing which are very similar in CDMA and OFMD systems. TCP3D is used in LTE system, the inputs into the TCP3D are LLR data for systematic and parity bits coming form rate de-matching, the outputs of TCP are hard decision, also called decoded bits.
TCP3 calculate decoded code block’s CRC, in case of TB with one CB, CRC result generated by TCP3 is TB CRC, so in this case TB CRC do not need to perfermed by CPU anymore.
Only in TB with multiple CBs case, the TB CRC need to calculate by CPU when all CBs are avalible.

## Slide 52: TCP3D Key Features (1/2)
Supports 3GPP Rel-7 and older (WCDMA), LTE, and WiMAX turbo decoding
Native Code Rate: 1/3
Radix 4 Binary and Duo-Binary MAP Decoders
Dual MAP decoders for non-contentious interleavers
Split decoder mode: TCP3D works as two independent, single MAP decoders
Max Star and Max log-map algorithms
Double Buffer input memory for lower latency transfers (except in split mode)
128-bit data bus for reduced latency transfers
Input data bit width: 6 bits
Programmable hard decision bit ordering within a 128-bit word: 0-127 or 127-0
Soft output information for systematic and parity bits: 8 bits
Extrinsic scaling per MAP for up to eight iterations (Both Max and Max Star)

## Slide 53: TCP3D Key Features (2/2)
Block sizes supported: 40 to 8192
Programmable sliding window sizes {16, 32, 48, 64, 96, 128}
Max number of iterations: 1 to 15
Min number of iterations: 1 to 15
SNR stopping criterion: 0 to 20 dB threshold
LTE CRC stopping criterion
LTE, WCDMA and WiMAX Hardware Interleaver Generators
Channel Quality Indication
Emulation support
Low DSP pre-processing load
Runs in parallel with CorePac
Targets base station environment
Notes: No data prepare needed
No interleaver table needed
In LTE, TCP3D ouput CB CRC, so in case of TB with one CB, TB CRC is not needed

## Slide 54: Turbo CoProcessor 3 Encoder (TCP3E)
TCP3E = Turbo CoProcessor 3 Encoder
  No previous versions, but came out at same time as third version of decoder co-processor (TCP3D)
  Runs in parallel with DSP
Performs Turbo Encoding for forward error correction of transmitted information (downlink for basestation)
  Adds redundant data to transmitted message
  Turbo Decoder in handset uses the redundant data to correct errors
  Often avoids retransmission due to a noisy channel
Turbo Encoder
(TCP3E)
Downlink
Turbo Decoder
in Handset

## Slide 55: TCP3E Features Supported
3GPP, WiMAX and LTE encoding
  3GPP includes: WCDMA, HSDPA, and TD-SCDMA
Code rate: 1/3
Can achieve throughput of 250 Mbps in all three modes
On-the-fly interleaver table generation
Dual-encode engines with input and output memories for increased throughput
Programmable input and output format within a 32-bit word
Block sizes supported: 40 to 8192
Tail biting for WiMAX
CRC encoding for LTE

## Slide 56: TCP3E Block Diagram
Internally, TCP3E has dual (ping/pong) encode engines, config registers, input and output memories
Externally, TCP3E looks like a single set of config regs and input / output buffers
Routing to ping/pong is handled internally
Alternates between ping and pong from one code block to the next

## Slide 57: Bit Rate Coprocessor (BCP)
The Bit Rate Coprocessor (BCP) is a programmable peripheral for baseband bit
processing. Integrated into the Texas Instruments DSP, it supports FDD LTE, TDD LTE, WCDMA, TD-SCDMA, HSPA, HSPA+, WiMAX 802.16-2009 (802.16e), and monitoring/planning for LTE-A.
Primary functionalities of the BCP peripheral include the following:
  CRC
  Turbo / convolutional encoding
  Rate Matching (hard and soft) / rate de-matching
  LLR combining
  Modulation (hard and soft)
  Interleaving / de-interleaving
  Scrambling / de-scrambling
  Correlation (final de-spreading for WCDMA RX and PUCCH correlation)
  Soft slicing (soft demodulation)
  128-bit Navigator interface
  Two 128-bit direct I/O interfaces
  Runs in parallel with DSP
  Internal debug logging
Notes: 57
NEW

## Slide 58: Viterbi Decoder Coprocessor (VCP2)

## Slide 59: VCP2 Functional Block Diagram

## Slide 60: KeyStone Overview
KeyStone Architecture
CorePac & Memory Subsystem
Interfaces and Peripherals
Coprocessors and Accelerators
Debug
Notes: NEW

## Slide 61: Emulation Features (1/2)
Host tooling can halt any or all of the cores on the device.
  Each core supports a direct connection to the JTAG interface.
  Emulation has full visibility of the CorePac memory map.
Real-Time Emulation allows the user to debug application code while interrupts designated as real-time continue to be serviced.
  Normal code execution runs code in the absence of a debug event halting execution with the peripheral operating in a continuous fashion.
  Secondary code execution runs code related to the service of a real-time interrupt after a debug event has halted code execution.
  No code execution does not run code because a debug event halts code execution, and no real-time interrupt is serviced after code execution is halted.
Notes: 61
NEW -- Not much at all was said about emulation features in the original presentation. I’ve broken it into two slides to make it more readable. Can you record new audio here and briefly touch on what is on each slide?

## Slide 62: Emulation Features (2/2)
Advanced Event Triggering (AET) allows the user to identify events of interest:
  Utilize instruction and data bus comparators, auxiliary event detection, sequencers/state machines, and event counters
  Manage breakpoints, trace acquisition, data collection via an interrupt, timing measurement, and generate external triggers
  Control a state machine and the counters used to create the intermediate events (loop counts and state machines)
  Allow event combining to create simple or complex triggers using modules call trigger builders
AET logic is provided for monitoring program, memory bus, system event activity, remembering event sequences, counting event occurrences, or measuring the interval between events.
  Perform range and identity comparisons
  Detect exact transactions
  Detect touching of a byte or range of bytes by memory references
External event detectors allow monitoring of external triggers or internal states of interest (i.e., cache miss).
  Enables four states for the identification of a sequence of triggers
  Allow specific system activity to generate breakpoints, an interrupt used for the collection of system data, or the identification of program activity that is observed through trace
Any system event routed to a C66x core can be routed (through software selection) to the AET.
Notes: 62
NEW

## Slide 63: Trace Subsystem (Simplified)
DMA
Switch Fabric
CorePac
0
S
0
Sm
Other
Masters
ETB
0
ETBn-1
CP_MONITOR 0
ETBn
DRM
STM
CP_MONITOR_M
TeraNet
Other
Slaves
VBUS command signals
exported to CP
_
MONITORs
Trace Logs generated
through dedicated SCR
One CP
_
MONITOR per
monitored slave endpoint
One Embedded Trace Buffer
per CorePac
One Embedded Trace for
System Trace
Trace
Stream
(
s
)
Optionally
Exported
CorePac
n
Notes: 63
REUSABLE – nothing here needs to be rerecorded

## Slide 64: Trace Features
Trace Pin Support for XDS560T Trace
On-Chip Embedded Trace Buffers
  4 KB (Core) /32 KB (STM) on-chip receiver
  One ETB per core for Trace and one for STM
  Snapshot and circular buffer mode
  Simultaneous write (sink) and read (drain) capability
  Can be used in CoreSight ETB mode
C66x CPU Trace:
  Trace targets the debug of unstable code:
    Provides for the recording of program flow, memory references, cache statistics, and application specific data with a time stamp, performance analysis, and quality assurance.
    Bus snoopers to collect and export trace data using hardware dedicated to the trace function.
    All or a percentage of the debug port pins can be allocated to trace for any of the cores (or a mix).
  Program flow and timing can be traced at the same rate generated by the CPU.
  Event trace provides a log of user-selectable system events. Event trace can also be used in conjunction with profiling tools.
  Data references must be restricted however as the export mechanism is limited to a number of pins, which is insufficient to sustain tracing of all memory references.
    The Advanced Event Triggering facilities provide a means to restrict the trace data exported to data of interest to maintain the non-intrusive aspect of trace.
    Error indications are embedded in the debug stream in the event the export logic is unable to keep up with the data rate generated by the collection logic.
    The user can optionally select the export of all specified trace data.
      In this case, the CPU is stalled to avoid the loss of trace data
      The user is notified that trace stalls have occurred although the number of stalls and their location is not recorded.
For more information on these features, please refer to Debug/Trace User Guide for your selected KeyStone device.
Notes: 64
MOSTLY REUSABLE – Record new audio as follows “Basically, all of the trace features listed here as the same implementation on previous devices. For more information, please refer to the CP Tracer User Guide.”

## Slide 65: KeyStone CP Tracer Modules
Preliminary Information under NDA - subject to change
Legend
x2
x4
x4
QMSS
MSMC_SS
CPU/2
256b
TeraNet
SCR
M3_DDR
M3_SL2
CPU/3
128b
TeraNet
SCR
S
S
CorePac
S
x4 for Wireless
x8 for Media
PCIe
S
SRIO
PCIe
QMSS
M
M
M
TPCC
16ch QDMA
M
TC0
M
TC1
M
M
DDR3
S
XMC
X 4/ x 8
M
CPU / 6
32b
TeraNet
SCR
EMIF16
Boot ROM
SPI
S
S
S
DAP (DebugSS)
M
TPCC
64ch
QDMA
M
TC2
M
TC3
M
TC4
M
TC5
TPCC
64ch
QDMA
M
TC6
M
TC7
M
TC8
M
TC9
CPU/3
32b
TeraNet
SCR
CPU/6
32b
TeraNet
SCR
CPT
PA/SA
M
x2
TSIP0,1
M
FFTC
SRIO
S
PA/SA
S
TSIP
S
AIF2
S
VCP2
S
TCP3D
S
TCP3E
S
S
x4
x2
CP Tracer (x8)
S
x8
CPT
VUSR
M
S
S
TPCC
TPTC
S
S
TPCC
TPTC
S
S
TPCC
TPTC
SCR
CPU /2
SCR
CPU / 3
SCR
CPU / 3
Timer
S
GPIO
S
I2C
S
INTC
S
UART
S
X8 / x16
SEC_CTL
S
PLL_CTL
S
Global
Timestamp
Bootcfg
S
VUSR
S
CPT
for EMIF_DDR3
(36b)
CPT
CPT
4 CPTs for SRAM
(36b)
Media Apps Only
Wireless Apps Only
AIF / DMA
M
FFTC / DMA
M
RAC_BE0,1
M
TAC_FE
M
SRIO
S
S
CPU / 3
32b
TeraNet
SCR
MPU
TCP3d
S
TCP3e_W/R
S
CPU / 3
128b SCR
VCP2 (x4)
S
x2
Monitors transactions
from AIF, TCs
Monitors transactions
from AIF,SRIO, Core, TCs
MPU
Semaphore
S
CPT
MPU
QMSS
S
CPT
MPU
TETB
S
STM
TETB
S
DebugSS
S
…
CONFIG
CPU/3
32b
TeraNet
Write-only
SCR
CP Tracer (x5)
M
CP Tracer (x8)
M
CP Tracer (x7)
M
DebugSS
STM
TETB
S
S
Bridge
CP Tracer (x7)
S
CP Tracer (x5)
S
x5
CPU/3
32b
TeraNet
SCR
x7
M
Bridge 12
Bridge 13
Bridge 14
EDMA_0
EDMA_1,2
CP Tracer
CPT
CPT
CPT
CPT
Notes: 65
REUSABLE – nothing here needs to be rerecorded

## Slide 66: CP Tracer Module Features (1/2)
Transaction trace (output to STM)
Ability to 'see' the transactions for each master to selected slave interfaces through tracing of key transaction points:
  Arbitration Won (Event B)
  Transaction Complete (Event C, E)
Two filtering functions for transaction traces to bring out the specific transactions:
  Transaction-qualifier-filtering: read/write
  Address-range-based filtering
Statistics counters:
  Throughput counts represent the total number of bytes forwarded to the target slave during a specified time duration.
    Counter accumulates the byte-count presented at the initiation of a new transfer.
    Can be used to calculate the effective throughput in terms of bytes-per-second at a given memory slave interface.
    Can be used to track the bandwidth consumed by the system masters. (#bytes/time)
  Each CP Tracer provides two independent throughput counters.
    Each can be used to track the total number of bytes forwarded from a group of masters.
    Each system master can be assigned to either / both /none of the two masters groups for throughput collection.
    CP Tracer also provides address range based filtering and transaction qualifier based filtering functions to further narrow the interested transactions.
  Accumulated Wait time counter
    Provides an indication of how busy the bus is and how many cycles elapsed with at least one bus master waiting for access to the bus
  Num Grant counter
    Provides an indication of the number of bus grants. The average transaction size can be determined by looking at throughput / num Grant
Notes: 66
REUSABLE – nothing here needs to be rerecorded

## Slide 67: CP Tracer Module Features (2/2)
Sliding Time Window:
  Specifies the measurement interval for all the CBA statistic counters implemented in the CP Tracer module.
  When the sliding window timer expires, the counter values are loaded into the respective registers and the count starts again.
  If enabled, an interrupt is also generated when the sliding time window expires.
  The host CPU and/or EDMA can read the statistics counters upon assertion of the interrupt.
  If enabled, the counter values can also be exported to STM automatically after the sliding time window is expired.
Cross-trigger generation: can assert EMU0/1 when a qualified event occurs
  External trigger to start/stop monitoring.
  The EMU0 trigger line is coupled to trace start. The EMU1 trigger line is coupled to trace stop.
  Both EMU0 and EMU1 are sourced from any of the CorePac cores.
  It can also be controlled from an external source via the EMU0 and EMU1 pins on the device.
  The EMU0 trigger enables the EMU01_TraceEnableStatus bit of the Transaction Qualifier register, the EMU1 trigger disables this bit.
STM Trace Export Enables
  Status message
  Event message
  Statistics message
Notes: 67
REUSABLE – nothing here needs to be rerecorded

## Slide 68: For More Information
For more information, refer to the C66x Getting Started page to locate the data manual for your KeyStone device.
View the complete C66x Multicore SOC Online Training for KeyStone Devices, including details on the individual modules.
For questions regarding topics covered in this training, visit the support forums at the TI E2E Community website.
Notes: NEW