## Slide 1: Inter-Processor Communication (IPC)

## Slide 2: Agenda
IPC Overview
IPC Configurations
IPC Module Details

## Slide 3: Agenda
IPC Overview
IPC Configurations
IPC Module Details

## Slide 4: What is IPC?
SYS/BIOS component that allows Communication:
  between processors in a Multiprocessor Environment
  to Peripherals
Communication Methods
  Message Passing
  Streams
  Linked Lists
Communication Mechanisms work transparently in both single and multi-processor systems
NOTES

## Slide 5: How can IPC be used?
IPC Can natively be used to communicate with:
  Other threads on the same processor
  Threads on other processors running SYS/Bios
  Threads on General Purpose processors running SYS/Link

## Slide 6: Supplied Packages
Input/Output Package
  Streams
  ti.sdo.io
Inter-Processor Communication Package
  Gates, Heaps, Linked Lists (ShMem), Variable Size Messages, Notify
  ti.sdo.ipc
Utilities Package
  List, MultiProc, NameServer
  ti.sdo.utils

## Slide 7: Agenda
IPC Overview
IPC Configurations
IPC Module Details

## Slide 8: IPC Configurations
Minimal Use
  Minimal data passing
Data Passing
  Passed linked list elements between processors
Dynamic Allocation
  Dynamically Allocate linked list elements from a heap
Powerful, Easy Messaging
  MessageQ Module

## Slide 9: Minimal Use
API Calls made to Notify Module
Callback functions can be registered to handle incoming events
Notify module
MultiProc module
Uses
/* Send an event message to the destination processor */
status = Notify_sendEvent(dstProc, INTERRUPT_LINE, EVENTID, seq, TRUE);
/*
* Register call back with Notify. It will be called when the processor with id = srcProc sends
* event number EVENTID to this processor.
*/
status = Notify_registerEvent(srcProc, INTERRUPT_LINE, EVENTID,(Notify_FnNotifyCbck)cbFxn, NULL);
/*
* ======== cbFxn ========
* This function was registered with Notify. It is called when any event is sent to this processor.
*/
Void cbFxn(UInt16 procId, UInt16 lineId, UInt32 eventId, UArg arg, UInt32 payload)
{
/* The payload is a sequence number. */
recvProcId = procId;
seq = payload;
Semaphore_post(semHandle);
}
Application Calls API
Configuration Only
No Configuration Necessary

## Slide 10: Data Passing
Notify
MultiProc
Uses
ListMP
SharedRegion
NameServer
GateMP
Uses
ListMP – doubly linked list designed to be shared by multiple processors
  Address Translation performed internally
  Cache coherency maintained when cacheable shared memory used
  GateMP used to protect read/write accesses
Application Calls API
Configuration Only
No Configuration Necessary

## Slide 11: Dynamic Allocation
Notify
MultiProc
Uses
ListMP
SharedRegion
NameServer
GateMP
Uses
HeapBufMP, HeapMultiBufMP, or HeapMemMP
Uses
API Calls made to Notify, ListMP, and a Heap*MP module
  Heap*MP modules use GateMP
Application Calls API
Configuration Only
No Configuration Necessary
/* Send the message to the remote processor */
status = MessageQ_put(remoteQueueId, msg);
/* Get a message */
status = MessageQ_get(messageQ, &msg, MessageQ_FOREVER);

## Slide 12: Messaging with MessageQ
MultiProc
Notify
ListMP
SharedRegion
GateMP
MessageQ
HeapBufMP, HeapMultiBufMP, or HeapMemMP
Transport SHM
NameServer
Application Calls API
Configuration Only
No Configuration Necessary
All API Calls to MessageQ for inter-processor communication
Configuration of MultiProc and Shared Region

## Slide 13: Agenda
IPC Overview
IPC Configurations
IPC Module Details

## Slide 14: IPC Module
Initializes subsystems of IPC
All applications that use IPC Modules must call IPC_start()
Configuration Specifics
  setupNotify specifies whether to setup and start the Notify module
  setupMessageQ specifies whether to setup the MessageQ module

## Slide 15: MessageQ Module
MessageQ_Create
MessageQ_Open
MessageQ_alloc
MessageQ_get
MessageQ_put
MessageQ_free
MessageQ_delete
MessageQ_close
Typical MessageQ Flow
Supports structured sending/receiving of variable length messages
OS independent
Works with all threading models
3 Priority Levels

## Slide 16: ListMP Module
Uses shared memory to provide a way for processors to share, pass, and store data buffers
Uses multi-processor gate to prevent multiple processors from simultaneously accessing the same linked list

## Slide 17: ListMP APIs
ListMP_empty() – test for empty ListMP
ListMP_getHead() – Get the element from the front of the ListMP
ListMP_getTail() – Get the element from the end of the ListMP
ListMP_insert() – Insert element into ListMP at current location
ListMP_next() – Return the next element in the ListMP
ListMP_prev() – Return the previous element in the ListMP
ListMP_putHead() – Put an element at the head of the ListMP
ListMP_putTail() – Put an element at the tail of the ListMP
ListMP_remove() – Remove the current element from the ListMP

## Slide 18: Heap*MP Modules
HeapBufMP – Fixed size memory manager (All allocated buffers are of the same size)
HeapMultiBufMP – Each instance supports up to 8 different fixed sizes of buffers.
HeapMemMP – Variable-size memory manager

## Slide 19: GateMP Module
Can be used to enforce both local and remote contect protection
  Can prevent preemption by another thread running on the same processor
  Can prevent a remote processor from entering the same Gate.
Typically used to protect reads/writes to a shared resource

## Slide 20: GateMP APIs
GateMP_open() – create GateMP instance
GateMP_close() – free GateMP instance
GateMP_delete() – similar to –close() with the addition of the shared memory being flagged
GateMP_enter() – gain access to the shared data protected by the gate
GateMP_leave() – Return access control to the shared data
GateMP_query() – Test a gate for Blocking and Preempting qualities

## Slide 21: Utilities Package
List Module
MultiProc Module
NameServer Module

## Slide 22: List Module (Single Core, Multi Thread)
Provides support for creating lists of objects
Implemented as a doubly-linked list
/*
* List Element Structure (First field must be List_elem
*/
typedef struct Rec {
List_Elem elem;
Int data;
} Rec;
Void main(){
…
…
List_Handle myList;
Rec r1, r2;
Rec* rp;
r1.data = 100;
r2.data = 200;
myList = List_create(NULL, NULL); /* No parameters needed for creation */
List_put(myList, &(r1.elem)); /* Put the two elements on the list */
List_put(myList, &(r2.elem));
/* Get all items off the list and print them */
while ((rp = List_get(myList != NULL){
System_Printf(“rec: %d\n”, rp->data);
}
}