## Slide 1: KeyStone IPC For Internal Audience Only
Multicore Applications
Ran Katzur
Acknowledge the help of Ramsey Harris

## Slide 2: Agenda
KeyStone Hardware Support for IPC
IPC Issues
Progress of IPC Support for KeyStone
Shared Memory IPC
Demo

## Slide 3: KeyStone Hardware Support for IPC
Memory
IPC Registers
Multicore Navigator
Semaphores

## Slide 4: Memory Resources
Shared memory
  DDR
  MSMC memory
Local “private” L1D and L2 memory both use global addresses
Semaphores
Block of 32 hardware semaphores
  Used to protect shared resources

## Slide 5: IPC Registers
Each CorePac has its own pair of IPC registers:
  IPCGRx generating interrupt
  IPCARx acknowledge interrupt (clearing)
28 bits can be used to define a protocol; 28 concurrent sources are available for interrupt definition

## Slide 6: IPC Registers

## Slide 7: Multicore Navigator
QMSS (Queue Manager Subsystem)
  Descriptors carry messages between queues
  Receive queues are associated with cores
  Enables zero copy messaging
Infrastructure PKTDMA (Packet DMA) facilitates copying of messages between sender and receiver

## Slide 8: IPC Issues
Memory
Coherency
Allocation and free
Race Condition
Linux Protection

## Slide 9: Logical and Physical Memory
MPAX registers map the same logical memory to different physical memory
Must agree on the location and translation of the shared memory
Current solution: Use the default MPAX for shared memory
Proc 0
Proc 1
Shared Memory Region (DDR3)
Proc 0 Local Memory Region
Proc 1 Local Memory Region
0x90000000
0x90000000

## Slide 10: Logical and Physical Memory: User Space ARM
MMU assigns (non-contiguous) physical locations for buffers translation lookaside buffer (TLB)
CorePac
MMU
TLB
Memory
…
Page 1
Page 2
Page 3
Page 4
Page 5
Logical
Address
Physical
Addresses

## Slide 11: Coherency
DSP L2 cache does not have coherency with the external world
What about ARM? - Depends what port interfaces with the MSMC
  Coherency from the TeraNet
  Not coherent from DSP CorePac

## Slide 12: Coherency
Can we use the MAR registers to disable cache? Yes, but
  Do we want to disable cache for a message? -
    If the data in the message needs complex processing it is better to be cached
  MSMC memory MAR register is given in the next slide

## Slide 13
MAR0 is implemented as a read-only register. The PC of the MAR0 is always read
as 1.
2. MAR1 through MAR11 correspond to internal and external configuration
address spaces. Therefore, these registers are read-only, and their PC field reads
as 0.
3. MAR12 through MAR15 correspond to MSMC memory. These are read-only
registers, the PC always read as 1. This makes the MSMC memory always
cacheable within L1D when accessed by its primary address range
*****Using MPAX may disable L1 cache for MSMC memory *****

## Slide 14: Allocation and Free
Messages are not consumed in the same order that they are generated
The core that allocates the memory is not the core that frees the memory, thus global (all cores) heap management is needed
Race Condition
If multiple cores can access the same heap, protection against race condition is needed
  Semaphores can protect resource that is shared by multiple cores

## Slide 15: Linux Protection
In user space, MMU protects one process from another process, and protects the kernel space from any user space
Using physical pointer in the user space breaks the protection

## Slide 16: Agenda
Keystone Hardware support for IPC
IPC issues
Progress of IPC support for Keystone
Shared memory IPC
Demo

## Slide 17: Keystone IPC Support
Keystone I IPC solution
Appleton IPC
Keystone II initial release
Keystone II MCSDK_3_1 release

## Slide 18: Keystone I IPC solution
Based on the standard IPC API from legacy TI products
Same API for messages inside a core, between cores or between devices
Multiple transport mechanisms, all have the same run-time API
  Shared memory
  Multicore Navigator
  SRIO
Examples: MCSDK_2_01_6\pdk_C6678_1_1_2_6\packages\ti\transport\ipc\examples

## Slide 19: Appleton IPC 6612 and 6614
Navigator-based msgCom package
  DSP to DSP
  ARM to DSP
Developed for the vertical market, not easy to adapt to the broad market

## Slide 20: IPC Technologies in KeyStone II MCSDK 3.0.3.15

## Slide 21
IPC Libraries MCSDK release 3_0_3_15

## Slide 22: Keystone II MCSDK_3_1
Dropped syslib from the release, no msgCom
IPC based on shared memory is still supported
Transport_net_lib (appeared in release 3.0.4.18 as well) is used for openCL/ openMP type of communications

## Slide 23: Common to all releases – Shared memory IPC library
IPC library based on shared memory
  DSP: Must build with BIOS
  Designed for moving messages and “short” data
  Compatible with legacy devices (same API)
  Supported by all Keystone generation (2014)

## Slide 24: Agenda
Keystone Hardware support for IPC
IPC issues
Progress of IPC support for Keystone
Shared memory IPC
Demo

## Slide 25: IPC Library
KeyStone IPC

## Slide 26: IPC Library: Transports
Current IPC implementation uses several transports:
Device 1
SRIO
CorePac 1
Thread 1
IPC
Thread 2
MEM
CorePac 2
Thread 1
IPC
Thread 2
Device 2
SRIO
CorePac 1
Thread 1
IPC
Thread 2
CorePac  CorePac (Shared Memory Model)
Device  Device (Serial Rapid I/O) – KeyStone I
Chosen at configuration; Same code regardless of thread location.

## Slide 27: IPC Services
The IPC package is a set of APIs.
MessageQ uses the modules below.
But each module can also be used independently.
Application

## Slide 28: IPC Services In the release
Top-level modules, used by application
Ipc
MessageQ
Notify
MultiProc
SharedRegion
GateMP
NameServer
HeapMemMP
HeapBufMP
MCSDK_3_0_4_18\ipc_3_00_04_29\packages\ti.sdo.ipc
MCSDK_3_0_4_18\ipc_3_00_04_29\packages\ti\sdo\util

## Slide 29: Ipc Module
Ipc – IPC Manager
  Used to initialize IPC and synchronize with other processors.
  Ipc_start – reserve memory, create default gate and heap
  Ipc_stop – release all resources
  Ipc_attach – setup transport between two processors
  Ipc_detach – finalize transport

## Slide 30: NameServer Module
NameServer – distributed name/value database
  Manages name/value pairs
  Used for registering data which can be looked up by other processors
API Summary
  NameServer_create – create a new database instance
  NameServer_add – add a name/value entry into database
  NameServer_get – retrieve value for given name

## Slide 31: MultiProc Module
MultiProc – processor identification
  Stores processor ID of all processors in the multi-core application.
  Stores processor name
Processor ID is a number from 0 – (n-1)
Processor name is defined by IPC
  See ti.sdo.utils.MultiProc > Configuration Settings, MultiProc.setConfig Click on Table of Valid Names for Each Device
API Summary
  MultiProc_getSelf – return your own processor ID
  MultiProc_getId – return processor ID for given name
  MultiProc_getName – return processor name

## Slide 32: SharedRegion Module
SharedRegion – shared memory address translation
  Manages shared memory and its cache configuration
  Manages shared memory using a memory allocator
Multiple shared regions are supported
Each shared region has optional HeapMemMP instance
  Memory is allocated and freed using this HeapMemMP instance
  HeapMemMP_create/open and managed internally at IPC initialization
  SharedRegion_getHeap API to get this heap handle

## Slide 33: HeapMemMP HeapBufMP Modules
HeapMemMP, HeapBufMP – multi-processor memory allocator
  Shared memory allocators that can be used by multiple processors
  HeapMemMP – variable size allocations
  HeapBufMP – fixed size allocations, deterministic, ideal for MessageQ
All allocations are aligned on cache line size.
  Warning: Small allocations will occupy full cache line.
Uses GateMP to protect shared state across cores.
Every SharedRegion uses a HeapMemMP instance to manage the shared memory

## Slide 34: GateMP Module
GateMP – protect a critical section
  Multiple processor gate that provides context protection against threads on both local and remote processors
Device-specific gate delegates offer hardware locking to GateMP
  GateHWSem for C6474, C66x
API Summary
  GateMP_create – create a new instance
  GateMP_open – open an existing instance
  GateMP_enter – acquire the gate
  GateMP_leave – release the gate

## Slide 35: Notify – Basic Communication
Simpler form of IPC communication
Send and receive event notifications
Device 1
CorePac 1
Thread 1
IPC
Thread 2
MEM
CorePac 2
Thread 1
IPC
Thread 2

## Slide 36: Notify Model
Comprised of SENDER and RECEIVER.
The SENDER API requires the following information:
  Destination (SENDER ID is implicit)
  16-bit Line ID
  32-bit Event ID
  32-bit payload (For example, a pointer to message handle)
The SENDER API generates an interrupt (an event) in the destination.
Based on Line ID and Event ID, the RECEIVER schedules a pre-defined call-back function.

## Slide 37: Notify Model

## Slide 38: Notify Implementation
How are interrupts generated for shared memory transport?
  The IPC hardware registers are a set of 32-bit registers that generate interrupts. There is one register for each core.
How are the notify parameters stored?
  The allocation of the memory is done by HeapMP and SharedRegion
How does the notify know to send the message to the correct destination?
  MultiProc and name server keep track of the core ID.
Does the application need to configure all these modules?
  No. Most of the configuration is done by the system. They are all “under the hood”

## Slide 39: Example Callback Function
/*
* ======== cbFxn ========
* This fxn was registered with Notify. It is called when any event is sent to this CPU.
*/
Uint32 recvProcId ;
Uint32 seq ;
void cbFxn(UInt16 procId, UInt16 lineId, UInt32 eventId, UArg arg, UInt32 payload)
{
/* The payload is a sequence number. */
recvProcId = procId;
seq = payload;
Semaphore_post(semHandle);
}

## Slide 40: Data Passing Using Shared Memory (1/2)
When there is a need to allocate memory that is accessible by multiple cores, shared memory is used.
However, the MPAX register for each DSP core might assign a different logical address to the same physical shared memory address.
Solution: Maintain a shared memory area in the default mapping (Until future release, when the shared memory module will do the translation automatically)
Proc 0
Proc 1
Shared Memory Region (DDR2)
Proc 0 Local Memory Region
Proc 1 Local Memory Region
0x90000000
0x90000000

## Slide 41: Data Passing Using Shared Memory (2/2)
Communication between DSP core and ARM core requires knowledge of the DSP memory map by the MMU. To provide this knowledge, the MPM (Multiprocessor management unit on the ARM) must load the DSP code. Other DSP code load method will not support IPC between ARM and DSP

## Slide 42: MessageQ – Highest Layer API
SINGLE reader, multiple WRITERS model (READER owns queue/mailbox)
Supports structured sending/receiving of variable-length messages, which can include (pointers to) data
Uses all of the IPC services layers along with IPC Configuration & Initialization
APIs do not change if the message is between two threads:
  On the same core
  On two different cores
  On two different devices
APIs do NOT change based on transport; only the CFG (init) code
  Shared memory
  SRIO

## Slide 43: MessageQ and Messages
How does the writer connect with the reader queue?
  MultiProc and name server keep track of queue names and core IDs. Each MessageQ has a unique name known to all elements of the system
What do we mean when we refer to structured messages with variable size?
  Each message has a standard header and data. The header specifies the size of payload.
If there are multiple writers, how does the system prevent race conditions (e.g., two writers attempting to allocate the same memory)?
  GateMP provides hardware semaphore API to prevent race conditions.
What facilitates the moving of a message to the receiver queue?
  This is done by Notify API using the transport layer.
Does the application need to configure all these modules?
  No. Most of the configuration is done by the system. More details later.

## Slide 44: Using MessageQ (1/3)
MessageQ_create(“myQ”, *synchronizer);
MessageQ_get(“myQ”, &msg, timeout);
CorePac 2 - READER
Step I - MessageQ creation during initialization:
  MessageQ transactions begin with READER creating a MessageQ.
Step 2 – During run-time
  READER’s attempt to get a message results in a block (unless timeout was specified), since no messages are in the queue yet.
“myQ”

## Slide 45: Using MessageQ (2/3)
“myQ”
MessageQ_create(“myQ”, …);
MessageQ_get(“myQ”, &msg…);
MessageQ_open (“myQ”, …);
msg = MessageQ_alloc (heap, size,…);
MessageQ_put(“myQ”, msg, …);
CorePac 1 - WRITER
WRITER begins by opening MessageQ created by READER.
WRITER gets a message block from a heap and fills it, as desired.
WRITER puts the message into the MessageQ.
Heap
CorePac 2 - READER

## Slide 46: Using MessageQ (3/3)
“myQ”
MessageQ_create(“myQ”, …);
MessageQ_get(“myQ”, &msg…);
*** PROCESS MSG ***
MessageQ_free(“myQ”, …);
MessageQ_delete(“myQ”, …);
MessageQ_open (“myQ”, …);
msg = MessageQ_alloc (heap, size,…);
MessageQ_put(“myQ”, msg, …);
MessageQ_close(“myQ”, …);
Heap
Once WRITER puts msg in MessageQ, READER is unblocked.
READER can now read/process the received message.
READER frees message back to Heap.
READER can optionally delete the created MessageQ, if desired.
CorePac 1 - WRITER
CorePac 2 - READER

## Slide 47: MessageQ – Configuration
All API calls use the MessageQ module in IPC.
User must also configure MultiProc and SharedRegion modules.
All other configuration/setup is performed automatically by MessageQ.
Notify
MultiProc
User APIs
Uses
Shared Region
Uses
GateMP
NameServer
HeapMemMP +
Uses
Cfg
MessageQ

## Slide 48: More Information About MessageQ
For the DSP, all structures and function descriptions are exposed to the user and can be found within the release:
  \ipc_U_ZZ_YY_XX\docs\doxygen\html\_message_q_8h.html
IPC User Guide \MCSDK_3_00_XX\ipc_3_XX_XX_XX\docs\IPC_Users_Guide.pdf
Notes: NEW

## Slide 49: IPC Device-to-Device Using SRIO
Currently available only on KeyStone I devices

## Slide 50: IPC Transports: SRIO (1/3) KeyStone I Only
The SRIO (Type 11) transport enables MessageQ to send data between tasks, cores and devices via the SRIO IP block.
Refer to the MCSDK examples for setup code required to use MessageQ over this transport.
Writer CorePac W
msg = MessageQ_alloc
MessageQ_put(queueId, msg)
TransportSrio_put
Srio_sockSend(pkt, dstAddr)
Reader CorePac Y
MessageQ_get(queueHndl,rxMsg)
MessageQ_put(queueId, rxMsg)
TransportSrio_isr
“get Msg from queue”
SRIO x4
SRIO x4

## Slide 51: IPC Transports: SRIO (2/3) KeyStone I Only
From a messageQ standpoint, the SRIO transport works the same as the QMSS transport. At the transport level, it is also somewhat the same.
The SRIO transport copies the messageQ message into the SRIO data buffer.
It will then pop a SRIO descriptor and put a pointer to the SRIO data buffer into the descriptor.
Writer CorePac W
msg = MessageQ_alloc
MessageQ_put(queueId, msg)
TransportSrio_put
Srio_sockSend(pkt, dstAddr)
Reader CorePac Y
MessageQ_get(queueHndl,rxMsg)
MessageQ_put(queueId, rxMsg)
TransportSrio_isr
“get Msg from queue”
SRIO x4
SRIO x4

## Slide 52: IPC Transports: SRIO (3/3) KeyStone I Only
The transport then passes the descriptor to the SRIO LLD via the Srio_sockSend API.
SRIO then sends and receives the buffer via the SRIO PKTDMA.
The message is then queued on the Receiver side.
Writer CorePac W
msg = MessageQ_alloc
MessageQ_put(queueId, msg)
TransportSrio_put
Srio_sockSend(pkt, dstAddr)
Reader CorePac Y
MessageQ_get(queueHndl,rxMsg)
MessageQ_put(queueId, rxMsg)
TransportSrio_isr
“get Msg from queue”
SRIO x4
SRIO x4
Notes: Dotted line to show what the application is doing and what is done automatically

## Slide 53: IPC Transport Details
Benchmark Details
IPC benchmark examples from MCSDK
CPU Clock = 1 GHz
Header Size = 32 bytes
SRIO in loopback Mode
Messages allocated up front
Message Size | Shared Memory | SRIO
 | Throughput (Mb/second) | 
48 | 23.8 | 4.1
256 | 125.8 | 21.2
1024 | 503.2 | -

## Slide 54: Demonstrations & Examples
KeyStone IPC

## Slide 55: Examples and Demos
There are multiple IPC library example projects for KeyStone I in the MCSDK 2.x release at mcsdk_2_X_X_X\pdk_C6678_1_1_2_5\packages\ti\transport\ipc\examples
IPC example for communication part of the Lab. Instructions how to build, run and modify this example is part of KeyStone II Lab book

## Slide 56: For More Information
Device-specific Data Manuals for the KeyStone SoCs can be found at TI.com/multicore.
For articles related to IPC, refer to the Embedded Processors Wiki for the KeyStone Device Architecture.
For questions regarding topics covered in this training, visit the support forums at the TI E2E Community website.

## Slide 57
ti

## Slide 58
Backup - configuration

## Slide 59: Configuration

## Slide 60: Static Configuration
Open cfg file in CCS with XDCScript Editor
var Settings = xdc.module('ti.sdo.ipc.family.Settings');
var Cache = xdc.useModule('ti.sysbios.family.c66.Cache');
var MessageQ = xdc.useModule('ti.sdo.ipc.MessageQ');
var Notify = xdc.module('ti.sdo.ipc.Notify');
var Ipc = xdc.useModule('ti.sdo.ipc.Ipc');
Notify.SetupProxy = xdc.module(Settings.getNotifySetupDelegate());
MessageQ.SetupTransportProxy= xdc.module(Settings.getMessageQSetupDelegate());
Notes: NEW

## Slide 61: Static Configuration
Open cfg file in CCS with XDCScript Editor
switch (Program.platformName) {
case "ti.sdo.ipc.examples.platforms.evm6678.core0":
case "ti.platforms.evm6678":
Program.global.USING_C6678 = 1;
Program.global.maxNumCores = 8;
procNameList = ["CORE0", "CORE1", "CORE2", "CORE3", "CORE4", "CORE5", "CORE6", "CORE7"];
Program.global.shmBase = 0x0C000000;
Program.global.shmSize = 0x00200000;
break;
Notes: NEW

## Slide 62: Static Configuration
Open cfg file in CCS with XDCScript Editor
var MultiProc = xdc.useModule('ti.sdo.utils.MultiProc');
MultiProc.setConfig(procName, procNameList);
var SharedRegion = xdc.useModule('ti.sdo.ipc.SharedRegion');
SharedRegion.translate = false;
SharedRegion.setEntryMeta(0,
{ base: Program.global.shmBase,
len: Program.global.shmSize,
ownerProcId: 0,
isValid: true,
cacheEnable: cacheEnabled,
cacheLineSize: cacheLineSize, /* Aligns allocated messages to a cache line */
name: "internal_shared_mem",
});
Notes: NEW

## Slide 63: Static Configuration
Open cfg file in CCS with XGCONF
Notes: NEW

## Slide 64: Static Configuration
Open cfg file in CCS with XGCONF
Notes: NEW