## Slide 1: KeyStone II Interrupts

## Slide 2: IPC registers

## Slide 3: C66 CorePac Primary Interrupts
124 events + 4 combined events
Event number 20 – SRIO, event 17 – PCIe, IPC event
42 events from the device interrupt controllers

## Slide 4: ARM CorePac Primary Interrupts
4 IPC events
4 PCIe legacy interrupts
8 PCIe MSI interrupts
24 SRIO interrupts
8 interrupts from each EDMA controller (5)
32 interrupts from the device interrupt controllers

## Slide 5: C66 CorePac Secondary Interrupts
474 secondary events
  8 from each EDMA controller (5)
  4 PCIe legacy interrupts
  4 PCIe MSI interrupts
  20 SRIO interrupts
  2 Hyperlink interrupts (0 and 1)

## Slide 6: EDMA and Hyperlink Interrupts
479 secondary events
  24 SRIO interrupts
  2 Hyperlink interrupts
  8 IPC interrupt generations