## Slide 1: Introduction to K2E Devices
KeyStone Training
Multicore Applications
Ran Katzur

## Slide 2: Agenda
KeyStone Device Overview
Introducing K2E (Edison)
K2E Device Summary
For More Information

## Slide 3: KeyStone Device Overview

## Slide 4: Keystone II: K2H/K2K Devices
High performance ARM + DSP
Memory Subsystem
  Multi-bank shared memory
  32- to 36- (40) bit translation
  Smart access arbitration
  Error detect/protect/correct
Multicore Navigator: HW routing
NETCP: HW acceleration
High bit-rate peripherals: SRIO, PCIe, Ethernet, TSIP
TeraNet:
  Non-blocking
  Smart arbitration
  Fast and wide
HyperLink: Seamless interface
Lots of connectivity

## Slide 5
S
R
I
O
x4
P
C
I
e
x2
U
A
R
T
S
P
I
I
C
2
GPIO
S
w
i
t
c
h
E
t
h
e
r
n
e
t
S
w
i
t
c
h
S
G
M
I
I
x2
Packet
DMA
Multicore Navigator
Queue
Manager
MSMC
MSM
SRAM
Memory Subsystem
1 to 8 Cores @ up to 1.25 GHz
C66x™
CorePac
L1P
Cache/RAM
L1D
Cache/RAM
L2 Memory Cache/RAM
HyperLink
TeraNet
Network Coprocessor
Power
Boot ROM
Semaphore
x3
PLL
EDMA
x3
Management
DDR3 EMIF
Debug/Trace
Packet
Accelerator
Security
Accelerator
Device Specific I/O
Device Specific I/O
Keystone I: C667x Devices
High end of the market for signal processing:
  Amazing performance
  Great SOC features
Challenges for broad market:
  Power consumption 10-15W
  Prices reflect performance
Notes: 5
NEW

## Slide 6
Keystone I: C665x Devices (Gauss)
1 Cores @ 850 MHz
C66x™
CorePac
C6654
MSMC
32-Bit
DDR3 EMIF
Memory Subsystem
Packet
DMA
Multicore Navigator
Queue
Manager
PLL
EDMA
TeraNet
Ethernet
MAC
SGMII
S
P
I
U
A
R
T
x2
P
C
I
e
x2
I2C
U
P
P
M
c
B
S
P
x2
G
P
I
O
EMIF16
Boot ROM
Debug/Trace
Power
Management
Semaphore
Security /
Key Manager
Timers
32KB L1P
Cache/RAM
32KB L1D
Cache/RAM
1024KB L2 Cache
x2
Signal Processing Engine
Few, more generic, accelerators
No NETCP
No TSIP, but McBSP
Smaller, slower DDR, less pins
Maintains most advantages of KeyStone
Typical applications:
Sealed box, power limitations
Performance requirements that can be achieved with 1-2 DSP cores
No requirement for accelerators or TSIP
Smaller DDR requirements
Notes: 6
NEW

## Slide 7
Embedded Processing Domain

## Slide 8: TI Embedded Processing Devices

## Slide 9: Introducing K2E (Edison)

## Slide 10: Comparing K2H and K2E Architecture
 | K2H | K2E
DSP CorePacs | Up to 8 | 0 or 1
DSP Maximum Clock | 1.2 GHz | 1.4 GHz
External Memory | DDRA and DDRB | DDRA only
MSMC Memory (Shared L2) | 6 MB | 2 MB
PLL | 5 | 3
SRIO | 4 lanes (20 Gbaud) | -
Multicore Navigator | 2 QMSS (16K queues) | Single QMSS (8K queues)
Hyperlink | 2 Links | 1 link
USIM (Universal Subscriber Identity Module) | NA | 1
TSIP | NA | 1
USB 3.0 | 1 | 2
Secure Mode | No | Yes
MDIO | 1 | 3

## Slide 11: K2E Features Summary
  Powerful Quad-ARM A15CorePac with DSP CorePac support, as needed
  Robust Ethernet options:
  Up to 2 ports 10G and 8 ports 1G
  Multiple MDIOs support multiple physical Ethernet interfaces
  Optimized external data movement:
  Standard high-bit rate interfaces: Ethernet and PCIe
  EDMA and Multicore Navigator
  Optimized internal traffic, priorities, arbitrations
  TeraNet bus
  MSMC
  Fast (1600 MHz), wide (72 bits), and large (8G) external memory

## Slide 12: Typical K2E Application Requirements
  Small, medium, or large I/O bandwidth
  Efficient signal processing calculations, fixed point or floating point or both
  Efficient micro-controller applications
  Within the processor(s) (A15)
  Within the device (NetCP)
  External to the device (10G)
  Power to performance ratio is important

## Slide 13: 66AK2E05 Key Features
Powerful microcomputer with DSP coprocessor
  Quad-ARM A15 CorePac
  1x Queue Manager supports up to 8K queues
  1x Network Coprocessor (NETCP)
  1x 3-port 10GBE Switch Subsystem
10 Ethernet ports:
  2x 10G
  8x 1G
  Telecommunications Serial Port (TSIP)
  2x PCIe and 2x USB 3.0 to support solid-state drive
Notes: 13
NEW

## Slide 14: 66AK2E05 Applications
Communication and networking
Fast hard-disk storage (PCIe, USB)
Imaging, including analytics
Example: Defense communication systems
Advantages
Integrated SOC solution
High-speed communication and disk bandwidth for data storage
DSP enables on-the-fly data processing
Ability to scale up using HyperLink, or scale down using 66AK2E02
Low power (compared to other solutions)
Notes: 14
NEW

## Slide 15: TI Embedded Processing Devices

## Slide 16: 66AK2E02 Key Features
Scaled-down version of 66AK2E05
High connectivity, but does not have 10GBE
2x PCIe and 2x USB 3.0 enables fast disk storage
Communication, storage with some analytics
Notes: 16
NEW

## Slide 17: 66AK2E02 Applications
Smart Grid and Smart Metering
Factory automation
Building control
Aerospace and defense
Industrial networking and Fieldbus protocols (IEC 61158)
Medical imaging
Notes: 17
NEW

## Slide 18: TI Embedded Processing Devices

## Slide 19: AM5K2E04 Key Features
  ARM-only TI multicore device
  Quad-ARM A15 CorePac
  1x Queue Manager supports up to 8K queues
  1x Network Coprocessor (NETCP)
  1x 3-port 10GBE Switch Subsystem
  Telecommunications Serial Port (TSIP)
  2x PCIe and 2x USB 3.0 to support solid-state drive
Notes: 19
NEW

## Slide 20: AM5K2E04 Applications
Networking:
  Enterprise
  Service Provider
  Data Center/Cloud
  Industrial network and Fieldbus protocols (IEC 61158)
Other industrial applications that do not require DSP
Notes: 20
NEW

## Slide 21: AM5K2E04 Wins
Defense Munitions
  Power efficiency
  High performance processing
  Large amount of internal memory
  Efficient ARM instructions
Flight Control Panel
  High-performance, Linux-based processor
  Efficient memory and internal bus utilization (MSMC, TeraNet)
  Open-source applications available
  Support for big Endian
Notes: 21
NEW

## Slide 22: TI Embedded Processing Devices

## Slide 23: AM5K2E02 Key Features/Applications
  Scaled-down version of AM5K2E04
  Dual-ARM A15 CorePac
  1x NETCP
  10GBE not included
  Supports low-end applications of AM5K2E04
Notes: 23
NEW

## Slide 24: TI Embedded Processing Devices

## Slide 25: K2E Device Summary

## Slide 26: K2E Software Support
MCSDK _03_01_XX supports K2E and K2L (also, K2K and K2H):
  Contiguous memory (cmem) allocation for ARM User Space enables internal and external DMA-based communication.
  User Space IO (UIO) driver support for mmap interface, interrupt handling, and chip power control
  TSIP LLD: MCSDK_3_1_0_2\pdk_keystone2_3_01_00_02\packages\ti\drv\tsip
  mmap LLD: MCSDK_3_1_0_2\pdk_keystone2_3_01_00_02\packages\ti\runtime\mmap
  Automatic setting of DEVM frequency based on the chip EFUSE value instead of environment variable in Uboot

## Slide 27: For More Information
  Datasheets:
  66AK2E05/02: http://www.ti.com/lit/SPRS865
  AM5K2E04/02: http://www.ti.com/lit/SPRS864
  Product Folders:
  66AK2E05: http://www.ti.com/product/66ak2e05
  66AK2E02: http://www.ti.com/product/66ak2e02
  AM5K2E04: http://www.ti.com/product/am5k2e04
  AM5K2E02: http://www.ti.com/product/am5k2e02
  For questions regarding topics covered in this training, visit the support forums at the TI E2E Community website.