## Slide 1: Cache Overview

## Slide 2: C66x Cache Details
 | L1P | L1D | L2
Organization | Direct | 2-Way SA | 4-Way SA
Allocate | Read Alloc | Read Alloc,Write Back | Read+Write Alloc, Write Back
Access Time | 1 Cycle | 1 Cycle | 
Capacity | 4, 8, 16, 32 Kb | 4, 8, 16, 32 Kb | 32, 64, 128, 256 Kb
Line Size | 32 bytes | 64 bytes | 128 bytes
Ext. Mem. Cacheability | Always Cached | Configurable | Configurable

## Slide 3: L1P Line Size Example
L1P - 4 KB Direct Mapped
32-Byte Line Size
32 Byte Memory “lines” 4 KB apart will share the same cache line
0x80000000
0x80000020
0x80000040
0x80000060
0x80000080
0x800000A0
0x800000C0
0x800000E0
0x80001000
0x80001020
0x80001040
0x80001060
0x80001080
0x800010A0
0x800010C0
0x800010E0

## Slide 4: L1P Thrashing Example
Example
  Two small functions stored in DDR3
    func1()
    func2()
  func 1 is called within a loop context
    Linked at address 0x800000A0
    Length 128 Bytes
  func 2() is a child of func1() (always called by func 1)
    Linked at address 0x80001060
    Length 160 Bytes

## Slide 5: DDR3 Layout
func2()
func1()
0x80000000
0x80000020
0x80000040
0x80000060
0x80000080
0x800000A0
0x800000C0
0x800000E0
0x80000100
0x80001000
0x80001020
0x80001040
0x80001060
0x80001080
0x800010A0
0x800010C0
0x800010E0
0x80001100
Function | Start Address | Size
func1 | 0x800000A0 | 0x80
func2 | 0x80001060 | 0xA0

## Slide 6: Cache View/Allocation
func1()
func2()
func1()
0x80000000
0x80000020
0x80000040
0x80000060
0x80000080
0x800000A0
0x800000C0
0x800000E0
0x80000100
0x000
0x020
0x040
0x060
0x080
0x0A0
0x0C0
0x0E0
0x100
0x120
0x140
0x160
0x180
0x1A0
1. Cache is Initially Empty
2. Func1 is called. Since it is not in Cache, it is loaded into cache (Compulsory Miss)
3. Func2 is called. Since it is not in Cache, it is loaded into cache
(Compulsory Miss)
func2()
0x80001000
0x80001020
0x80001040
0x80001060
0x80001080
0x800010A0
0x800010C0
0x800010E0
0x80001100
Q: What are the consequences?
A: Conflict misses
Depending on where func2 is returning to, there will be an L1P miss either upon the return to func2, or on the subsequent loop iteration call to func 1.
Solution:
Ensure that functions that are dependent on each other don’t share the same cache lines. (group them in the linker command file)
Increase the size of the cache of the cache (if possible)