## Slide 1: QMSS: Components Overview
Major HW components of the QMSS:
Queue Manager
Two PDSPs (Packed Data Structure Processors):
  Descriptor Accumulation / Queue Monitoring
  Load Balancing and Traffic Shaping
Interrupt Distributor (INTD) module
Two timers
Internal RAM for descriptor memory
PKTDMA that supports all cores
TeraNet

## Slide 2: Infrastructure Packet DMA
The Rx and Tx Streaming I/F of the QMSS PKTDMA are wired together to enable loopback.
Data packets sent out the Tx side are immediately received by the Rx side.
This PKTDMA is used for core-to-core transfers and peripheral-to-DSP transfers.
Because the DSP is often the recipient, a descriptor accumulator can be used to gather (pop) descriptors and interrupt the host with a list of descriptor addresses. The host must recycle them.

## Slide 3: QMSS: Queue Mapping
Queue Range | Count | Hardware Type | Purpose
0 to 511 | 512 | pdsp/firmware | Low Priority Accumulation queues
512 to 639 | 128 | queue pend | AIF2 Tx queues
640 to 651 | 12 | queue pend | PA Tx queues (PA PKTDMA uses the first 9 only)
652 to 671 | 20 | queue pend | CPintC0/intC1 auto-notification queues
672 to 687 | 16 | queue pend | SRIO Tx queues
688 to 695 | 8 | queue pend | FFTC_A and FFTC_B Tx queues (688..691 for FFTC_A)
696 to 703 | 8 |  | General purpose
704 to 735 | 32 | pdsp/firmware | High Priority Accumulation queues
736 to 799 | 64 |  | Starvation counter queues
800 to 831 | 32 | queue pend | QMSS Tx queues
832 to 863 | 32 |  | Queues for traffic shaping (supported by specific firmware)
864 to 895 | 32 | queue pend | vUSR queues for external chip connections
896 to 8191 | 7296 |  | General Purpose

## Slide 4: Tx Example
Understanding how the PKTDMAs are triggered and controlled is critical.
TeraNet

## Slide 5: Receive Example
Rx PKTDMA receives packet data from Rx Streaming I/F.
Using an Rx Flow, the Rx PKTDMA pops an Rx FDQ.
Data packets are written out to the descriptor buffer.
When complete, Rx PKTDMA pushes the finished descriptor to the indicated Rx queue.
The core that receives the descriptor must recycle the descriptor back to an Rx FDQ.
Queue Manager (QMSS)
buffer
buffer
buffer
buffer
Rx Free Desc Queue
Rx queue
Rx PKTDMA
pop
push
w
r
i
t
e
Memory
Peripheral
TeraNet SCR
push
pop

## Slide 6: How Does it Work During Run Time?
For example, Core A wants to send a message to Core B.
Core A picks available descriptor (e.g., message structure) that is either partially or completely pre-built.
  As needed, Core A adds missing information.
Core A pushes the descriptor into a queue.
  At this point, Core A is done.
The Navigator processes the message and sends it to a queue in the receive side of Core B where it follows a set of pre-defined instructions (Rx flow), such as:
  Interrupt Core B and tell it to process the message.
  Set a flag so Core B can pull and change a flag value on which Core B synchronizes.
  Move buffer into Core B memory space and interrupt the core.
After usage, the receive core recycles the descriptors (and any buffer associated with) to prevent memory leaks.

## Slide 7: What Needs to Be Configured?
Link Ram - Up to two LINK-RAM
  One internal, Region 0, address 0x0008 0000, size up to 16K
  One External, global memory, size up to 512K
Memory Regions - Where descriptors actually reside
  Up to 20 regions, 16 byte alignment
  Descriptor size is multiple of 16 bytes, minimum 32
  Descriptor count (per region) is power of 2, minimum 32
  Configuration – base address, start index in the LINK RAM, size and number of descriptors
  The way the region is managed
Loading PDSP firmware

## Slide 8: What Needs to Be Configured?
Descriptors
  Create and initialize.
  Allocate data buffers and associate them with descriptors.
Queues
  Open transmit, receive, free, and error queues.
  Define receive flows.
  Configure transmit and receive queues.
PKTDMA
  Configure all PKTDMA in the system.
  Special configuration information used for PKTDMA.