## Slide 1: Very Large Fast DFT (VL FFT) Implementation on KeyStone
Multicore Applications

## Slide 2: Outlines
Basic Algorithm for Parallelizing DFT
Multi-core Implementation of DFT
Review Benchmark Performance

## Slide 3: Goals and Requirements
Goal:
  To implement very large floating point fast DFT on TI C66x multicore devices
Requirements:
  FFT sizes: 4K – 1M samples
  Configurable to run on different number of cores: 1, 2, 4, 8
  High performance

## Slide 4: Algorithm for Very Large DFT
A generic discrete Fourier transform (DFT) is shown below,
Here N is the total size of DFT ,

## Slide 5: Algorithm for Very Large DFT
For very large N, it can be factored into N = N1*N2 and with decimation-in-time, the DFT can be formulated as,

## Slide 6: Algorithm for Very Large DFT
The above DFT formula can be :

## Slide 7: Algorithm for Very Large DFT
A very large DFT of size N=N1*N2 can be computed in the following steps:
  Formulate input into N1xN2 matrix
  Matrix transpose: N1xN2 -> N2xN1
  Compute N2 FFTs and multiply twiddle factors. Each FFT is N1 size.
  Matrix transpose: N2xN1 -> N1xN2
  Compute N1 FFTs. Each is N2 size.
  Matrix transpose: N1xN2 -> N2xN1

## Slide 8: Implementing VLFFT on Multiple Cores
Two iterations of computations
1st iteration
  N2 FFTs are distributed across all the cores.
  Each core implements matrix transpose and computes N2/numCores FFTs and multiplying twiddle factor.
2nd iteration
  N1 FFTs of N2 size are distributed across all the cores
  Each core computes N1/numCores FFTs and implements matrix transpose before and after FFT computation.

## Slide 9: Data Buffers
DDR3: Three float complex arrays of size N
  Input buffer, output buffer, working buffer
L2 SRAM:
  Two ping-pong buffers, each buffer is the size of 16 FFT input/output
  Some working buffer
  Buffers for twiddle factors
    Twiddle factors for N1 and N2 FFT
    N2 global twiddle factors

## Slide 10: Global Twiddle Factors
Global Twiddle Factors:
Total of N1*N2 global twiddle factors are required.
N1 are actually pre-computed and saved.
The rest are computed during run time.

## Slide 11: DMA Scheme
Each core has dedicated in/out DMA channels
Each core configures and triggers its own DMA channels for input/output
On each core, the processing is divided into blocks of 8 FFT each.
For each block on every core
  DMA transfer 8 lines of FFT input
  DSP computes FFT/transpose
  DMA transfers 8 lines of FFT output

## Slide 12: VLFFT Pseudo Code
VLFFT_start:
1) Core0 sends message to each core to start 1st iteration processing.
2) Each core does the following,
Wait message from core 0 to start,
numBlk = 0;
While( numBlk < totalBlk )
{
1) Trigger DMA to transfer (n+1)th blk from Input Buffer to L2 and to transfer (n-1)th blk output from
L2 to Temp Buffer
2) Implement transpose, compute FFT, and multiply twiddle factors for nth blk
3) wait for DMA completion
4) numBlk++
}
Send a message to core 0
3) Core0 waits for message from each core for completion of its own processing
4) After receiving all the messages from all the other cores, core0 sends message to each core to start 2nd
iteration processing
5) Each core does the following,
Wait message from core 0 to start,
numBlk = 0;
While( numBlk < totalBlk )
{
1) Trigger DMA to transfer (n+1)th blk from Temp Buffer to L2 and to transfer (n-1)th blk output from
L2 to Output Buffer
2) Compute FFT and transpose for nth blk
3) wait for DMA completion
4) numBlk++
}
Send a message to core 0
6) Core0 waits for message back from each core for completion its own processing
VLFFT_end:

## Slide 13: Matrix Transpose
The transpose is required for the following matrixes from each core:
  N1x8 -> 8xN1
  N2x8 -> 8xN2
  8xN2 -> N2x8
DSP computes matrix transpose from L2 SRAM
  DMA bring samples from DDR to L2 SRAM
  DSP implements transpose for matrixes in L2 SRAM
  32K L1 Cache

## Slide 14: Major Kernels
FFT: single precision floating point FFT from c66x DSPLIB
Global twiddle factor compute and multiplication: 1 cycle per complex sample
Transpose: 1 cycle per complex sample

## Slide 15: Major Software Tools
SYS BIOS 6
CSL for EDMA configuration
IPC for inter-processor communication

## Slide 16: Conclusion
After the demo …