## Slide 1: KeyStone Interrupts
KeyStone Training
Multicore Applications
Literature Number: SPRPXXX

## Slide 2: Agenda
Interrupt Scheme (SPI 0 Example)
Configuring Interrupts (Hyperlink Example)

## Slide 3: Interrupt Scheme
KeyStone Interrupts

## Slide 4: Link Events to ISR

## Slide 5: C66 core input events

## Slide 6: C66 core Primary events
To connect event to ISR:
Connect Primary event to one of the 12 maskable interrupt lines
Connect interrupt line to ISR
CSL OR BIOS API are used to connect event to interrupt line and interrupt to ISR
List of Primary event – table 6-22 in 66AK2H14/12/06 Data Sheet

## Slide 7: Configuring an Hwi Using BIOS Statically via GUI
Use Hwi module (Available Products), insert new Hwi (Outline View)
Example:
event 94 to the CPU HWI5
NOTE: BIOS objects can be created via the GUI, script code, or C code (dynamic).
By the way, event 94 is not connected to anything – it is reserved

## Slide 8: Configuring an Hwi Using BIOS Statically via GUI

## Slide 9: Configuring an Hwi Using BIOS using run-time functions
The include file Hwi.h in the release MCSDK_3_0_4_18\bios_6_37_00_20\packages\ti\sysbios\family\c64p\Hwi.h
Has the definition of the Hwi class
Where do you find the Event Id #?

## Slide 10: C66 Core Prime Event IDs (Core Events Only)
From the C66x User’s Guide:
22 assigned events
  5 reserve primary events
  17 secondary events
7 reserved events
99 Available events
The available events are connected to the device.

## Slide 11: C66 Core Prime Event IDs When it is part of KeyStone 2 Device

## Slide 12: Configure HWI using csl
CSL interrupt files are in the release
  MCSDK_3_0_4_18\pdk_keystone2_3_00_04_18\packages\ti\csl\src\intc
Include files – csl_intc.h csl_intcAux.h
Source files in src/intc directory
  CSL_intcPlugEventHandler()
  CSL_intcInit()
  CSL_intcGlobalNmiEnable
  CSL_intcGlobalEnable()
  CSL_intcHwControl()
  CSL_intcOpen
  And more
Note – In addition to the mapping, the interrupt must be enabled
  Global enable – enable the global interrupt register
  Enable the particular interrupt

## Slide 13: KeyStone II Interrupt Topology
All events from all IP come to the interrupt controllers.
Some are connected directly to C66x or other masters (EDMA, ARM, Hyperlink)
Some are mapped by the interrupt controllers
CIC0
CIC1
CIC2
Events
C66x CorePac0
C66x CorePac1
C66x CorePac2
C66x CorePac3
C66x CorePac4
C66x CorePac5
C66x CorePac6
C66x CorePac7
HyperLink
EDMA CC0
EDMA CC1
EDMA CC2
EDMA CC3
EDMA CC4
ARM A15
CorePac
Peripherals

## Slide 14: C66 core Secondary events

## Slide 15: CIC to C66 core connections Event No – the core input event Event name – the CIC output line

## Slide 16: Connecting System Event
Mapping (Connecting) system events (input to CIC)
to channels (output of CIC)

## Slide 17: KeyStone II CIC input system events

## Slide 18: Mapping CIC - API
Read the following Wiki: http://processors.wiki.ti.com/index.php/Configuring_Interrupts_on_Keystone_Devices
csl APIs- For KeyStone II (MCSDK 3.x), look at the two include files to see all the API that are needed:
  csl_cpIntc.h
  csl_cpIntCAux.h
SysBios APIs – look at cpInitc.h and cpInitc.c in directory MCSDK_Y_XX\bios_6_BB_AA_ZZ\packages\ti\sysbios\family\c66\tci66xx

## Slide 19: Example 1
SPIXEVT - Get an interrup

## Slide 20: Example 1 – ISR connected to SPIXEVT
66AK2H12 has multiple instances of SPI; We will look at SPI 0
SPIXEVT is NOT a primary event so it should be mapped via CIC
The next slide shows the system events that are associated with SPIXEVT

## Slide 21: KeyStone II CIC input events

## Slide 22: ISR connected to SPIXEVT
SPI_0_XEVT is input event number 56 to CIC
What channel should be used?
Table 5-22 shows the C66 core input event. There are multiple CIC output events that are connected to C66 core
Some of these events are broadcast event (meaning – they are connected to all 4 cores that CIC supports) and some are individual core events.

## Slide 23: ISR connected to SPIXEVT
Eight events (56 to 63) come out of the interrupt controller are broadcast events, they are connected to CIC output channel 0 to 7 respectively. This example uses C66 input event 63 that is connected to CIC_OUT7

## Slide 24: ISR connected to SPIXEVT
They are other events from the interrupt controller that could be considered (Both, broadcast and single core)
The ARM GIC has 480 input events and 12 of them are connected to SPI

## Slide 25: Connecting SPI 0 Transmit event to core 3 ISR

## Slide 26: csl map system event (input) to output
  csl_cpIntCAux.h shows the APIs that connect system events to channels (e.g., the output of the CIC).
Connecting channel events to interrupt queues is done using CSL or SYSBIOS, as described previously.
Error = CSL_CPINTC_mapSystemToChannel(hnd, 56,7) ;//CSL
Error = CpIntc_mapSysIntToHostInt(0, UInt 56, 7); // BIOS

## Slide 27: Examples 2 Hyperlink
MCSDK includes examples of interrupts originating from peripherals: MCSDK_3_01_12\pdk_keystone2_3_00_01_12\packages\ti\drv
Consider an example using HyperLink, where an interrupt is sent from Hyperlink 0 to a DSP core.

## Slide 28: Following Hyperlink Interrupt 0 From Table 5-24 of 66AK2H12- CIC0 input events
Event number 111 (ox6F) is HyperLink 0 interrupt.
Next, this interrupt is connected to a core …

## Slide 29
static int hyplnkExampleInitChipIntc (void)
{
CSL_CPINTC_Handle hnd;
// I drop some of the functions here (enable/disable interrupts etc.
CSL_CPINTC_mapSystemIntrToChannel (hnd, CSL_CIC0_HYPERLINK_0_INT, hyplnk_EXAMPLE_INTC_OUTPUT);
// I drop some of the functions here (enable/disable interrupts etc.
return 0;
}
CSL_CIC0_HYPERLINK_0_INT = 111
What about hyplnk_EXAMPLE_INTC_OUTPUT?

## Slide 30
Choose to use event 45 of the core
It could be any one of other CIC_OUT lines (look at the complete table for even more)

## Slide 31: Following Hyperlink Interrupt 0 - Continue
Event 45 on the C66 core is connected to CIC out 64 + 10 x N, that is
  Core 0 event 45 is connected to CIC output event 64
  Core 1 event 45 is connected to CIC output event 74
  Core 2 event 45 is connected to CIC output event 84
  You got the point
CIC0 should map input event 111 to output event 64 (or 74, or 84 or … depends on what core is used)

## Slide 32
ARM A15 Interrupt Scheme

## Slide 33
System Events Mapping to GIC

## Slide 34: Following GPIO 0 From Table 5-23 of 66AK2H12- ARM CorePac Interrupts

## Slide 35: From the file gpio-keystone.c

## Slide 36: From the file gpio-keystone.c

## Slide 37: Questions?