## Slide 1: KeyStone II Interrupts

## Slide 2: Agenda
Motivation for this presentation
The interrupt Scheme
Configure interrupt

## Slide 3: Configuring an Hwi: Statically via GUI
1
Use Hwi module (Available Products), insert new Hwi (Outline View)
Example:
Tie SPI_INT to the CPU HWI5
2
Configure Hwi: Event ID, CPU Int #, ISR vector:
To enable INT at startup, check the box
Where do you find the Event Id #?
NOTE: BIOS objects can be created via the GUI, script code, or C code (dynamic).

## Slide 4: Hardware Event IDs
How do you know the names of the interrupt events and their corresponding event numbers?
Look it up in the datasheet.
Source: TMS320C6678 datasheet
As appropriate, refer to the datasheet for your target platform.
What happens in the ISR ?

## Slide 5: Agenda
Motivation for this presentation
The interrupt Scheme
Configure interrupt

## Slide 6: System Events

## Slide 7: System Events Some events are connected directly to Cores But not event 56

## Slide 8: C66 Event Mapping
Table 9-2 in the C66 UG
22 assigned events (5 reserve primary events, 17 secondary events)
7 reserved events
99 Available events
The available events are connected to the Device. The next slides will show how and what is connected to the available events in the 6638 device.

## Slide 9: C6638 Interrupt Topology
Table 5-4 in the 66AK2H12
All events from all IP come to the interrupt controllers
Some are connected directly to C66 or other masters (EDMA, ARM, Hyperlink) and some are mapped by the interrupt controllers

## Slide 11: Where is SPIXEVT?
Not on the above page
Not on any of the other two pages in the table
But we see that there are eight events (56 to 63) that come out of the interrupt controller. We can connect SPIXEVT through the interrupt controller to one of these events (broadcast events)
They are other events from the interrupt controller that could be considered (Both, broadcast and single core)
The ARM GIC has 480 input events and 12 of them are connected to SPI

## Slide 12: Connecting SPIXEVT to Core 3
66AK2H12 has multiple instances of SPI, we will look at SPI 0
The next slide will show one page from the input table for CIC0. Same events are connected to CIC1 as well

## Slide 14: Connecting SPI 0 Transmit event to core 3 ISR

## Slide 15: Agenda
Motivation for this presentation
The interrupt Scheme
Configure interrupt

## Slide 16: Configuration API
Read the following Wiki: http://processors.wiki.ti.com/index.php/Configuring_Interrupts_on_Keystone_Devices
For KeyStone II (MCSDK 3), look at the two include files csl_cpIntc.h and csl_cpIntCAux.h to see all the API that are needed
The next slide with show APIs to connect system events to channels (output of the CIC) and the channel events to interrupt line