## Slide 1: Introduction to K2E Devices New members of the keystone II family

## Slide 2: Keystone II Architecture
Strong Core Performances
Memory Sub-system –
  Multi-banks shared memory
  32 to 36 (40) bit translation
  Smart access arbitration
  Memory protection EDC
Multicore Navigator
  Hardware routing
NetCP
  Hardware Accelerators
High bit rate peripherals
  SRIO, PCIe, Ethernet, TSIP
Teranet –
  Non blocking
  Smart arbitration
  Fast and wide
Hyperlink
  Seamless interface
Lot’s of connectivity

## Slide 3: Keystone I Architecture
High end of the market for signal
processing
  Amazing performances
  Great SOC features
But
  Power consumption 10-15W
  Prices reflect the performances
Low-end devices –
The Gauss family
Application-Specific
Coprocessors
Memory Subsystem
Multicore Navigator
Network Coprocessor
C66x™
CorePac
HyperLink
TeraNet
External Interfaces
Miscellaneous

## Slide 4: Keystone I Gauss Family
1 or 2 Cores @ up to 1.25 GHz
C66x™
CorePac
C6655/57
MSMC
1MB
MSM
SRAM
32-Bit
DDR3 EMIF
Memory Subsystem
Packet
DMA
Multicore Navigator
Queue
Manager
x2
PLL
EDMA
VCP2
TCP3d
x2
Coprocessors
HyperLink
TeraNet
Ethernet
MAC
SGMII
S
R
I
O
x4
S
P
I
U
A
R
T
x2
P
C
I
e
x2
I2C
U
P
P
McBSP
x2
G
P
I
O
Boot ROM
Debug/Trace
Power
Management
Semaphore
Security /
Key Manager
Timers
2nd core, C6657 only
32KB L1P
Cache/RAM
32KB L1D
Cache/RAM
1024KB L2 Cache
EMIF16
Signal Processing Engine
Few, more generic, accelerators
No NetCP
No TSIP but McBSP
Smaller, slower DDR, less pins
Maintain most of Keystone
Family advantages
Typical Usage
Low power project –
  Sealed box, power limitations
Projects that need performances
But 2 cores is enough
Projects that do not need the
Accelerators or TSIP
Projects that need smaller DDR

## Slide 6: Embedded Processing offering

## Slide 7: K2E Arrives

## Slide 8: 66AK2E05
Powerful micro-computer with DSP co-processor
10 Ethernet ports, 2x10G, 8x1G
2x PCIe
2x USB
Notes: 8
NEW

## Slide 9: 66AK2E05 Applications
Communication and network
Storage – fast hard disk (PCIe, USB)
Imaging – including analytic
Example - Defense communication system
Advantages
Integrate solution – SOC
High communication Speed and disk bandwidth to store data
DSP enables data processing on the fly
Ability to scale up using hyperlink, scale down using 66AK2E02
Low power (compare to other solutions)
Notes: 9
NEW

## Slide 10: Embedded Processing offering

## Slide 11: 66AK2E02
Scaled-down version of 66AK2E05
High connectivity but does not have 10G
2xPCIe and 2x USB enables fast disk storage
Communication, storage with some analytics
Notes: 11
NEW

## Slide 12: 66AK2E02 Applications
Smart Grid and Smart Metering
Factory Automation
Building Control
Aerospace and Defense
Industrial Network and Field Bus Protocols
Medical Imaging
Notes: 12
NEW

## Slide 13: Embedded Processing offering

## Slide 14: AM5K2E04
  ARM-only TI multicore device
  Quad-ARM A15 CorePac
  1x Queue Manager supports up to 8K queues
  1x Network Coprocessors (NETCP)
  1x 3 port 10GBE Switch Subsystem
  Telecommunications Serial Port (TSIP)
  PCIe and 2x USB 3.0 to support solid state drive
Notes: 14
NEW

## Slide 15: AM5K2E04 Applications
Networking
  Enterprise
  Service Provider
  Data Center/Cloud
  Industrial Network and Field Bus Protocols
Other industrial applications that do not require DSP
Notes: 15
NEW

## Slide 16: AM5K2E04 Win
Defense Munition project
AM5K2E04 provides:
power efficient
high performance processor.
large amount of internal memory
Efficient ARM instructions
Notes: 16
NEW

## Slide 17: AM5K2E04 Win
Flight Control Panel
AM5K2E04 provides:
high performance Linux based processor
Efficient memory and internal bus utilization (MSMC, Teranet)
Open source applications available
Support for Big endian
Notes: 17
NEW

## Slide 18: Embedded Processing offering

## Slide 19: AM5K2E02
  Scaled-down version of AM5K2E04
  Dual-ARM A15 CorePac
  1x Network Coprocessor
  10GBE not included
  Applications
  Low-end applications of AM5K2E04
Notes: 19
NEW

## Slide 20: Embedded Processing offering

## Slide 21: K2E Devices Summary

## Slide 22: K2h and K2E Architecture compare
 | K2H | K2E
DSP Cores | Up to 8 | 1 or 0
DSP maximum clock | 1.2G | 1.4G
External Memory | DDRA and DDRB | DDRA only
MSMC memory (shared L2) | 6 MB | 2 MB
PLL | 5 | 3
SRIO | 4 lanes (20Gbaud) | -
Multicore Navigator | 2 QMSS (16k queues) | Single QMSS (8k queues)
Hyperlink | 2 Links | 1 link
USIM (Universal Subscriber Identity Module) | - | 1
TSIP | - | 1
USB 3.0 | 1 | 2
Secure Mode | No | Yes
MDIO | 1 | 3

## Slide 23: K2E Features
Powerful ARM core, multiple A15 with help from DSP core, if needed
High Ethernet interface, 2 ports 10G and 8 ports 1G
  Multiple MDIO supports multiple physical Ethernet interface
Optimized external data movement –
  Standard high bit rate interfaces – Ethernet and PCIe
  EDMA and multicore navigator
Optimized internal traffic, priorities, arbitrations
  Teranet bus
  MSMC
Fast (1600MHZ) wide (72 bits) and large (8G) external memory

## Slide 24: K2E Typical Applications
Applications that need small, medium or large I/O bandwidth
Applications that need some efficient signal processing calculations, fixed point or floating point or both, and
Applications that need efficient micro-controller type of application, in the processor(s) and moving data within the device and external to the device
Applications where power per performances is important (and where it is not?)

## Slide 25: K2E Software support
MCSDK _03_01_XX supports K2E and K2L (In addition to K2K and K2H)
  Contiguous memory allocation for ARM User Space – cmem
    Enable internal and external DMA based communication
  User space IO driver UIO
    Support for mmap interface, interrupt handling and chip power control
  TSIP LLD- MCSDK_3_1_0_2\pdk_keystone2_3_01_00_02\packages\ti\drv\tsip
  mmap LLD - MCSDK_3_1_0_2\pdk_keystone2_3_01_00_02\packages\ti\runtime\mmap

## Slide 26: K2E EVM Software support
Automatic setting of DEVM frequency based on the chip EFUSE value instead of environment variable in Uboot