## Slide 1: KeyStone MPM Basics
KeyStone Training
Multicore Applications
Literature Number: SPRPxxx

## Slide 2: Questions
How does LINUX MMU know where is the DSP code?
What needs to be done so DSP and ARM can work concurrently and together?

## Slide 3: MPM Architecture

## Slide 4: MPM Functionality
MPM Basics

## Slide 5: Disclaimer
The Following presentation shows how TI implementation that runs on TCIEVM6638K2K words
  Other implementations may be different

## Slide 6: 6638 Memory Architecture (8G DDRA)

## Slide 7: 6638 Memory Architecture (2G DDRA)

## Slide 8: 6638 Memory Architecture (1G DDRA) (32bit DDR)

## Slide 9: DDR and MSM Memories
DSP and other masters translate the 32 bit logical address into 36 (40) bits physical address using MPAX registers
ARM MMU translates 32 bit logical memory into 40 bits physical memory
In TI implementation, U-BOOT defines the memory that is available to the MMU
Starting from device tree and modifies it
Arm A15 in KeyStone uses large Physical Address Extension mode
The file board.c defines the physical memories for the MMU

## Slide 10: The Device Tree
In the device tree we define what memories will be used by the Linux and what by the DSP
The device tree is defined in an ASCII file with extension dts. A compiler converts it to binary
During boot time (U-BOOT) builds a device tree table and updates it based on U-BOOT environment
Device Tree for the EVM is tci6638-evm.dts. It defines several memories. It defines the total logical memory and what part of it will be used by the kernel, and it defines what memories will be available for the DSP

## Slide 11: DSP definition in Device Tree
For each C66 CorePac, 7 memory allocations:
  Address of Core control registers (boot address, power)
  L1 P global memory address
  L1 D global memory address
  L2 global memory address
In addition, the MSM memory address and DDR addresses that are dedicated to DSP usage are defined.
DSP code that uses DDR must use ONLY the DDR addresses that are assigned to it

## Slide 12: Memory definitions from TCI6638-evm Device tree
dspmem: dspmem
{
compatible = "linux,rproc-user";
mem = <0x0c000000 0x000600000 0xa0000000 0x20000000>;
label = "dspmem";
};
memory
{
reg = <0x00000000 0x80000000 0x00000000 0x20000000>;
};
Note – We will see later how the start address of the DSP DDR is determined by the U-BOOT parameters.
When build DSP code, one must be aware what is the start DDR address for DSP

## Slide 13: Memory definitions from TCI6638-evm Device tree
dsp7: dsp7
{
compatible = "linux,rproc-user";
reg = <0x0262005C 4
0x02350858 4
0x02350a58 4
0x0262025C 4
0x17e00000 0x00008000
0x17f00000 0x00008000
0x17800000 0x00100000>;
reg-names = "boot-address", "psc-mdstat", "psc-mdctl", "ipcgr", "l1pram", "l1dram", "l2ram";

## Slide 14: U-BOOT and mem_reserve
Two segment of memory are defined for the MMU to use.
The first starts at physical address 0x08 0000 0000 and size of 2G
The second segment starts at 0x08 8000 0000 and size 6G
Part of the first segment of memory is reserved for the DSP memory. This is used to load programs and data from the ARM user’s domain to the DSP memory
The size of the DSP reserve memory is defined in U-BOOT. It is called mem_resereve. A default size is 512M – 0x2000 0000

## Slide 15: U-BOOT and mem_reserve
To change the size of the reserve memory, the value mem_reserve should be changed in the U-BOOT using setenv mem_reserve Value
Note that the U-BOOT code uses the function ustrtoul to convert the ASCII value into a numeric value. It understands notations such as 512M
Is changing the mem_reserve value in U-BOOT enough to change the memory segment that is dedicated to the DSPs for MPM?
  The file mpm_config.json tells mpm what memories are available. It must agree with the device tree and the U-BOOT

## Slide 16: Example code from board.c

## Slide 17: MPM Configuration
The file mpm_config.json is a Java Script Object Notation file that describes the DSP access memory segments to the ARM
10 memory segments are defined, 8 segments are for each DSP core l2 local memory, one for MSM memory, and one for part of DDR that is used by the MPM as shared memory
mpm_config.json definition of core 0 L2 memory:
{
"name": "local-core0-l2",
"localaddr": "0x00800000",
"globaladdr": "0x10800000",
"length": "0x100000",
"devicename": "/dev/dsp0"
},

## Slide 18: MPM Configuration (2)
The two shared memory definitions show that the DSP dedicated memory in DDR starts at 0xa0000000 and has a size of 512M (-1K) bytes.
{
"name": "local-msmc",
"globaladdr": "0x0c000000",
"length": "0x600000",
"devicename": "/dev/dspmem"
},
{
"name": "local-ddr",
"globaladdr": "0xa0000000",
"length": "0x1FFFFC00",
"devicename": "/dev/dspmem"
}

## Slide 19: Modify 6638 Memory (1G DDRA)

## Slide 20: Standard K2H platform definition For DSP RTSC build

## Slide 21: Demo
I started with the FIR filter program that is part of the DSP optimization Lab.
  Runs on one core, two cores, four cores and 8 cores
  Has various steps of optimization
Modify for MPM - Change printf to system_printf and so on
Modified the target definition – partition the DDR into two memories
Rebuild the code without any changes to the linker command
Can not run the code from MPM
Change the linker to use the memory area that is dedicated to DSP
The code runs from mpm perfectly

## Slide 22: Define New DSP platform 2G DDR, 512M dedicated ARM memory

## Slide 23: Demo steps
Demo steps:
  Try to load the original code into DSP0
  Show the map file of the original code
  Try to load the new code into 8 cores
  Show the new map file
  Reset, load and run the 8 cores
  Look at the results cat /debug/remoteproc/remoteprocN/trace0